## Slide 1: Generic Management Actions A mechanism for all MAC enhancement groups
Michael Fischer
CHOICE-Intersil
4242-3 Medical Drive
San Antonio, TX 78229
+1-210-614-4096 x107
mfischer@choicemicro.com

## Slide 2: The Problem
Each set of functional enhancements to the 802.11 MAC requires new management frame functions
  There are only 5 reserved management subtypes
  Adding elements to existing subtypes is only a partial solution, and may reduce efficiency and reliability as the management frame bodies get longer and longer
There are some functions that need unique subtypes
  Mostly frames that use special rules, like Beacon, Probe & ATIM
  The "Container" for MPDU aggregation is a new special case
  We need to save a few management subtypes for future special cases, because backward compatibility constraints make it messy to add MMPDUs as control subtypes

## Slide 3: The Proposed Solution
Define a mechanism to add all new generic management frames using 1 subtype, and leave the last 3 management subtypes for future special cases
The "generic Management Action" subtype in the QoS baseline proposal achieves this
  Supports both request/response and notification models
  Allows for uniform status reporting (where beneficial)
  Places no format or content restrictions on frame body contents
    However, unless there is clear justification for a different approach, generic action frames will use fixed fields and elements
  Facilitates non-conflicting, parallel work by different task groups

## Slide 4: Generic Action Request Frame
Management subtype 14, with (at least) 1, 4-octet fixed field
  Category code, assigned per task group or sub-group
      Identifies general subject, such as QoS Actions, Security Actions, etc.
      Allows non-conflicting assignment of Action codes by each group
  Action code (even), for a specific function within the category
      Request and notification actions use even action code values
  Activation Delay, allows occurrence of action to be delayed
      Delay=0 for immediate actions, >0 is count of TBTTs prior to action
      Delay>0 only for Category,Action specified to allow or require delay
  Dialog Token (octet needed for alignment…)
      Value ignored, but returned in corresponding octet of Action Response
  The rest of the frame body is specific to the Category,Action
FCS
MAC Header
(subtype 14)
Action (even)
Category
Activation Delay
Dialog Token
(24)
(1)
(1)
(1)
(1)
(0-2300)
Action-specific fixed fields & elements
(4)

## Slide 5: Generic Action Response Frame
  Response frames only used to return results and report errors
      Notification-style actions do not require responses
  Category code: same as in request frame
      If category is not recognized, frame is ignored without error response
  Action code (odd): ResponseCode:= RequestCode + 1
      An unrecognized action in a recognized category causes an error response
  Status code: indicates success or failure of action
      Status=0 for success; Status=1 for unrecognized action
      Status>1 is failure code specific to Category,Action
  Dialog Token: value copied from Dialog Token of request
      May be useful in matching responses at stations that may have more than one request outstanding concurrently
  The rest of the frame body is specific to the Category,Action
FCS
MAC Header
(subtype 14)
Action (odd)
Category
Status
Dialog Token
(24)
(1)
(1)
(1)
(1)
(0-2300)
Action-specific fixed fields & elements
(4)