## Slide 1: Enhance D-QoS through Virtual DCF
Maarten Hoeben, Menzo Wentink
Intersil

## Slide 2: D-QoS Objectives
Provide service differentiation
  Without losing fairness (delay and throughput)
    Both between classes of same priority as well as cross priority, both local and remote
  Without increasing complexity too much
Limit the delay for higher priority classes
  Limit medium load
  Avoid starvation of lower priority classes

## Slide 3: DCF Properties
DCF is a reasonable fair access mechanism, given that:
  All frames are equal in size (throughput fairness)
  Fairness is monitored over a longer period
  All STAs use the same Contention Window (CW) settings
  Near-far problem is not considered an issue
Delay properties are reasonable if medium load is kept low
Manipulation of CW allows for differentiation

## Slide 4: D-QoS Concept
Separate queues for each priority class
Differentiate through per class CW settings and/or Submission Rate (SR)
CW and SR are dynamically adapted to current medium load
See presentation by Wim Diepstraten, Lucent for more details

## Slide 5: D-QoS Access Mechanism Problems
Fairness issues:
  Throughput unfairness
    Proposal does not solve intrinsic DCF problem
  Possible unfairness between same priority classes of local and remote STAs
    For example: if the local STA has frames in both high priority as well as low priority classes while the remote STA has frames in only low priority classes, the access distribution for the low priority classes is not the same

## Slide 6: D-QoS Access Mechanism Problems (cont’d)
Distribution not consequent within same local class
  If a high priority queue empties, the new tx-opportunity rate distribution for a lower priority queue changes in an unpredictable way
Difficult to predict behavior or analyze theoretically
Granularity of service rate control is low
Many tuning-parameters (backoff and service rate)

## Slide 7: Virtual DCF
Enhance D-QoS through “Virtual DCFs”
  Model the queues of the priority classes in an STA as independent (virtual) DCFs
    Each V-DCF contends for the medium independently of the other local V-DCFs
    Solving a local collision between V-DCFs is a policy decision
    Incase of a collision with a remote V-DCF, the CW for a retry is doubled for the colliding V-DCF only
  Differentiate solely through CW differentiation (service rate not required)
  Making CW also dependent of the total duration of the frame exchange for which the V-DCF contends will increase fairness

## Slide 8: V-DCF Advantages
Predictable and fair service differentiation
  Decoupling of the entire fairness matrix (local-remote, high-low priority)
  Decoupling of access mechanism from drop rate control because queue backlog does not influence distribution of access per class
    Drop rate control does not have to be standardized because it is not coupled
Allows for a simple solution of inherent DCF throughput fairness issue

## Slide 9: V-DCF Advantages (cont’d)
Low implementation complexity
Easier to analyze than current D-QoS access mechanism
Enhances D-QoS with a better differentiation method
  All ideas of Lucent’s proposal (Load monitoring and controlling, AP priority, drop rate control etc) are still applicable
Fairer integration of legacy stations

## Slide 10: V-DCF Issues
V-DCFs increase the number of entities contending (up to 2007*8!). Is this a problem?
  No, the intent of D-QoS is to keep the medium load reasonably low through rate control and increased CWs, so contention is less of an issue
  Not all V-DCFs contend with the same (low) CW
  The local V-DCFs avoid collisions
Does the local (station internal) interaction of V-DCFs introduce unwanted side effects, such as fairness issues?
  As analyzed so far, these side effects are minimal and do not impact the fairness noticeably