## Slide 1: Scheduled DCF vs. Virtual DCF
Maarten Hoeben, Menzo Wentink
Intersil

## Slide 2: Goal
To compare the two proposed D-QoS solutions:
  V-DCF (Virtual DCF)
    Each class has an independent Virtual DCF
  S-DCF (Scheduled DCF)
    Each station has one DCF which uses the CW for the highest backlogged class. An internal scheduler provides for rate adaptation in the case that more than one local class has backlogged traffic

## Slide 3: Scheduled DCF
S-DCF stations merge traffic from different classes in the scheduler, prior to sending the muxed stream into the DCF
The DCF uses the CW value corresponding to the highest backlogged queue i (CWi). The CW values are controlled by the AP
The scheduler can be vendor specific but the ratios are probably controlled by the AP
Scheduler
Class 3
Class 2
Station
DCF - CWi
Class 1
Class 0

## Slide 4: Scheduled DCF
PROS
  The number of contenders is the same as the number of stations
CONS
  Stations must implement a scheduler  more complexity
  Many variables must be controlled: CW and scheduler ratios.
  Traffic from different classes is multiplexed in two different ways, which do not result in similar behavior:
    Locally: in the Scheduler
    Remotely: through the DCF
  This will result in an intrinsically unfair system! – see example

## Slide 5: Virtual DCF
Stations maintain a separate (virtual) DCF for each class.
  CW values are controlled by the AP
The V-DCFs (implicitly) merge the traffic
Station
V-DCF CW2
Class 3
Class 2
Class 1
Class 0
V-DCF CW3
V-DCF CW1
V-DCF CW0

## Slide 6: Virtual DCF
PROS
  No scheduler required in stations, which reduces complexity
  Predictable and fair inter-station behavior
  Easy to understand conceptually
  Smallest possible number of variables to be managed
  Under the assumption that most stations will use only one class at a time, V-DCF is the simplest solution
  The AP (which will usually have traffic in all of it’s queues) becomes more aggressive
CONS
  Increased number of medium contenders, especially when classes are frequently used in parallel
    But this is an advantage for the Access Point

## Slide 7: S-DCF Fairness Issue
Example:
  Several stations are transmitting Class 2 traffic only. All S-DCFs use the same CW (CW2), so on average the individual streams will be equal in size.
  One station starts transmitting Class 3 traffic also, while it keeps on sending the Class 2 traffic.
  The S-DCF in that station will switch to a new CW (CW3) and start transmitting the Class 3 traffic, while it interleaves the Class 2 frames.
  The Class 2 rates from other stations will automatically adapt to the presence of the additional Class 3 traffic, and the DCF again ensures that on average each Class 2 stream will be equal in size.
  However, the Class 2 stream that comes from the station with Class 3 traffic will be determined by the internal scheduler. So while all Class 2 rates are (indirectly) determined by the ensemble of DCFs, there is one Class 2 rate which is determined by the scheduler. Theoretically that rate could be the same, but it is very likely that it is not.
  This a a fundamental fairness issue with S-DCF.

## Slide 8: S-DCF Fairness Issue (cnt’d)
Fairness demands that the Class 2 traffic streams from station A and B are the same (statistically)
The intrinsic problem with S-DCF is that traffic is multiplexed in two different ways: locally in the scheduler AND remotely by the DCF’s.
Scheduler
Class 3 Traffic
Class 2 Traffic
DCF(CW2)
Scheduler
Class 2 Traffic
Class 3 traffic +
Class 2 traffic
Class 2 traffic
Station A
Station B
DCF(CW3)

## Slide 9: Fairness in V-DCF
  DCF is a fair mechanism, so V-DCF is also
DCF(CW3)
Class 3 Traffic
Class 2 Traffic
DCF(CW2)
Class 2 Traffic
Class 3 traffic
Class 2 traffic
Class 2 traffic
Station A (V-DCF)
Station B (V-DCF)
DCF(CW2)