## Slide 1: Summary of the QoS Baseline Proposal Developed by the QoS Baseline Ad-hoc Group September-November, 2000
Michael Fischer
CHOICE-Intersil
4242-3 Medical Drive
San Antonio, TX 78229
+1-210-614-4096 x107
mfischer@choicemicro.com
Document Editor:

## Slide 2: Results of Baseline Ad-hoc Group
Explored areas of consensus and disagreement
  Sets of functions that had to be present to achieve >75% support
  Sets of functions that had to be absent to achieve >75% support
  Fortunately, there was sufficient willingness to compromise that the intersection of these sets is not null!
Defined nested conformance model, no disjoint option sets
Defined a uniform higher-layer interface within the confines of the 802 MAC SAP and MLME SAP
  A consistent set of frame formats based on 8 traffic categories
  Made substantial progress on defining the enhanced DCF, enhanced PCF, and traffic category support mechanisms
Can have initial draft within weeks if this baseline is adopted

## Slide 3: Why Adopt a Baseline
To have a framework within which to evaluate proposals for specific mechanisms
  The original 802.11 MAC group spent >2 years trying to build a MAC function-by-function, and got nowhere
  To focus effort on areas which are incomplete or undefined
    But this does not preclude improvements to areas already defined
To move quickly to a draft for initial letter ballot
  The rate of progress improves greatly during the balloting process
My personal views:
  This baseline is "good enough" (actually, better than that) and standards are, by definition neither perfect nor state-of-the-art
  If the apparent consensus in and since Scottsdale is not sufficient to adopt this baseline, we might as well let the PAR expire

## Slide 4: Key Features of Proposed Baseline
Upward compatible from and coexistent with 802.11-1999
Supports both prioritized and parameterized QoS
  Prioritized QoS provides relative differentiation between priorities
  Parameterized QoS provides managed delivery using traffic specs
  But as viewed from above the MAC SAP there is only one service!
Provides QoS delivery under both (E)DCF and (E)PCF
  Parameterized QoS only available under EPCF
  Improved efficiency through new and streamlined mechanisms
BSS Overlap Mitigation
Structural elements to extend BSS coverage & connectivity
  Bridge Portal (BP): infrastructure access at non-AP location
  Alternate AP/PC: to preserve BSS (& QoS) in event of failure
  Remote AP/PC: to extend spatial coverage via WDS link

## Slide 5: Conformance Levels
There are 4 conformance levels, designated 0 to 3
Each higher level is a proper superset of the level beneath
Conformance levels are attributes of the Association
Level 0
Level 1
Level 2
Level 3
Prioritized QoS (EDCF)
Prioritized QoS (EDCF)
No QoS (DCF)
Contention Period
Parameterized QoS (EPCF)
No QoS (PCF) ?
No QoS (PCF)
Contention-Free Period
Prioritized QoS (EDCF)
Prioritized QoS (EPCF)
Level 0
Level 1
Level 2
Level 3
No QoS (DCF)
Parameterized QoS (EPCF)
Prioritized QoS (EDCF)
Style of QoS
Level 0
Level 1
Level 2
Level 3
No QoS (DCF)
Enhanced DCF only
Enhanced DCF and PCF
Coordination Functions

## Slide 6: New Terminology
BP: Bridge Portal
EAP: Enhanced AP
EPC: Enhanced point coordinator
ESTA: Enhanced station
QBSS: BSS that provides associations at QoS Levels >0
TCA: {Traffic Category, AID}
TCID: Traffic category identifier (0-7)
TXOP: Transmission opportunity
WSTA: Wireless station (an ESTA other than EAP or BP)

## Slide 7: MAC SAP
No changes to service primitives
Priority parameter of MA-UNITDATA.request/indication is used to identify traffic category
  When association supports prioritized QoS, traffic category is mapped to delivery priority.
  When association supports parameterized QoS, traffic category identifies the traffic specification (supplied via MLME SAP)
This interface is uniform across all conformance levels
  So higher layer software can work (to some quality level, not necessarily the desired quality) at any QoS level (perhaps even 0)

## Slide 8: Enhanced Station Model
Below the MAC SAP are a plurality of (logical) traffic queues
  4 is suggested as the minimum
  If there are <8 queues, the mapping of traffic category to queue follows guidelines in 802.1D-1998, Annex H.2.
A scheduler function selects a frame for transmission at the next TXOP
  A common scheduler is suitable for QoS levels 1 & 2
The channel access function (EDCF, EPCF-Station) is independent of the scheduler
MAC SAP
MLME SAP
Scheduler
Channel Access
Queues

## Slide 9: Traffic Categories
For prioritized QoS, TC is (QBSS-global) delivery priority
  Defaults as in 802.1D-1998, Annex H.2, can be remapped via MIB (lowest) 1, 2, 0, 3, 4, 5, 6, 7 (highest) -- 0 is best effort
For parameterized QoS, TC selects the traffic specification
    Traffic specs are interpreted in the context of the source station's MAC address/AID, unless the source is not in the QBSS, in which case the destination station's MAC address/AID is used
    Parameters in traffic specification:
      TS Info (periodic/aperiodic, Ack policy, delivery priority)
      Retry Interval (for delayed Acks) & Polling Interval (for periodic polling)
      Transmit Interval (Committed Time for aperiodic)
      Nominal MSDU Size
      Minimum Data Rate & Mean Data Rate
      Maximum Burst Size
      Delay Bound & Jitter Bound

## Slide 10: MAC Functional Improvements
Direct ESTA-ESTA transfers
Directed Probe Request to find peers and learn capabilities
Improved Beacon reliability
  Rigid limit at TBTT (similar to CFPMaxDuration)
  Medium sensing to detect beacon collision
  BSS overlap information added to Beacons
  "Proxy Beacon" may be sent by ESTAs to inform adjacent APs
Allow RTS/CTS (with actual duration) during CFP
CF-Polls convey TXOPs with specified duration
...
& Clarify many ambiguous provisions in 802.11-1999

## Slide 11: New MAC Mechanisms (general)
Transmission Opportunities (TXOPs)
  The right to transmit defined by starting time & duration limit
    Applies to EDCF contention winner as well as CF-poll recipients
    Limit is global during CP, piggybacked with poll during CFP
  Can be allocated in advance during CFP
Traffic Category Identifiers (TCIDs)
  A 2-octet field at end of MAC header in QoS data subtypes
    High-order 3 bits are priority parameter for MSDU
    Same layout as TCI field of 802.1Q VLAN tag, VID field is reserved
    Amount of traffic queued for TC piggybacked during CFP
  Some control frames and elements use TCA field with {TC,AID}

## Slide 12: New MAC Mechanisms
  Aggregation of multiple MPDUs into a single PSDU
  Burst transfers (EDCF) of SIFS-separated frames that fit in TXOP
  Delayed Acknowledgment (level 3 only)
    Basic format allows up to n*16 unacknowledged frames per TC
    A "retry delay" parameters allows fallback to ARQ
  Centralized Contention & Reservation Request (EPCF only)
  Alternate EAP/EPC
  BSS Overlap Mitigation
  Bridge Portals

## Slide 13: Enhanced DCF
Priority-based Distributed Coordination
  To achieve fairness access among traffic of the same priority at different stations
  And relative to best effort traffic from legacy stations
  Without a penalty for non-used traffic classes
Details in separate presentations

## Slide 14: Enhanced PCF
Largely based on the detailed effort from the Joint Proposal (00/071, 00/120) by AT&T, Lucent, Sharewave, and others (00/120r1)
Uses mechanism enhancements from Joint Proposal
    Centralized Contention (CC)
    Reservation Request (RR)
    Ack Policy (normal, delayed, none)
    TXOP limit and TC size piggybacked on QoS data frames
    CF-Multipoll for multiple TXOP assignment
    CF-Schedule for periodic (CBR-type) traffic
foo
But does not require BSS-unique VSIDs nor external classifier entities

## Slide 15: MLME SAP
Minor additions to Scan, Start, Join, etc. to add QoS levels as association attributes
MLME-TSUPDATE.request/confirmation used to define and modify traffic specifications
MLME-WMSTATUS.request/confirmation for WLAN-aware higher-layer bandwidth reservation and QoS management entities to obtain information on the state of the wireless medium

## Slide 17: Power Save
Listen Epoch
  Portions of beacon interval when power save ESTA is awake
  ESTA requests amount of awake time, EAP assigns epoch(s)
Level 1
  Uses existing power save with PS-Poll
Level 2
  EAP can use "PS-non-poll" during WSTA's listen epoch
Level 3
  TXOPs can be allocated during listen epoch to allow direct ESTA-ESTA under power save

## Slide 18: Incomplete Items & Placeholders
FEC (at MAC layer)
EDCF channel access
BSS Overlap Mitigation (partial)
Bridge Portals
Interaction with HL end-to-end QoS management entities