## Slide 1: Summary of the QoS Baseline Proposal Developed by the QoS Baseline Ad-hoc Group September-November, 2000 Revision 1, incorporating changes made during the November meeting
Michael Fischer
CHOICE-Intersil
4242-3 Medical Drive
San Antonio, TX 78229
+1-210-614-4096 x107
mfischer@choicemicro.com
Document Editor:

## Slide 2: Results of Baseline Ad-hoc Group
Explored areas of consensus and disagreement
  Sets of functions that had to be present to achieve >75% support
  Sets of functions that had to be absent to achieve >75% support
  Fortunately, there was sufficient willingness to compromise that the intersection of these sets is not null!
Defined nested conformance model, no disjoint option sets
Defined a uniform higher-layer interface within the confines of the 802 MAC SAP and MLME SAP
  A consistent set of frame formats based on 8 traffic categories
  Made substantial progress on defining the enhanced DCF, enhanced PCF, and traffic category support mechanisms
Can have initial draft within weeks if this baseline is adopted

## Slide 3: Key Features of Proposed Baseline
Upward compatible from and coexistent with 802.11-1999
Supports both prioritized and parameterized QoS
  Prioritized QoS provides relative differentiation between priorities
  Parameterized QoS provides managed delivery using traffic specs
  But as viewed from above the MAC SAP there is only one service!
Provides QoS delivery under both (E)DCF and (E)PCF
  Parameterized QoS only available under EPCF
  Improved efficiency through new and streamlined mechanisms
BSS Overlap Mitigation
Structural elements to extend BSS coverage & connectivity
  Bridge Portal (BP): infrastructure access at non-AP location
  Alternate AP/PC: to preserve BSS (& QoS) in event of failure
  Remote AP/PC: to extend spatial coverage via WDS link

## Slide 4: Conformance Levels
There are 4 conformance levels, designated 0 to 3
Each higher level is a proper superset of the level beneath
Conformance levels are attributes of the Association
Level 0
Level 1
Level 2
Level 3
Prioritized QoS (EDCF)
Prioritized QoS (EDCF)
No QoS (DCF)
Contention Period
Parameterized QoS (EPCF)
Stations are CF-Pollable
No QoS (PCF)
Contention-Free Period
Prioritized QoS (EDCF)
Prioritized QoS (EPCF)
Level 0
Level 1
Level 2
Level 3
No QoS (DCF)
Parameterized QoS
Prioritized QoS
Style of QoS
Level 0
Level 1
Level 2
Level 3
No QoS (DCF)
Enhanced DCF only (CF-Pollable)
Enhanced DCF and PCF
Coordination Functions

## Slide 5: New Terminology
BP: Bridge Portal
EAP: Enhanced AP
EPC: Enhanced point coordinator
ESTA: Enhanced station
QBSS: BSS that provides associations at QoS Levels >0
TCA: {Traffic Category, AID}
TCID: Traffic category identifier (0-7)
TXOP: Transmission opportunity
WSTA: Wireless station (an ESTA other than EAP or BP)

## Slide 6: MAC SAP
No changes to service primitives
Priority parameter of MA-UNITDATA.request/indication is used to identify traffic category
  When association supports prioritized QoS, traffic category is mapped to delivery priority.
  When association supports parameterized QoS, traffic category identifies the traffic specification (supplied via MLME SAP)
This interface is uniform across all conformance levels
  So higher layer software can work (to some quality level, not necessarily the desired quality) at any QoS level (perhaps even 0)

## Slide 7: Enhanced Station Model
Below the MAC SAP are a plurality of (logical) traffic queues
  4 is suggested as the minimum
  If there are <8 queues, the mapping of traffic category to queue follows guidelines in 802.1D-1998, Annex H.2.
A scheduler function selects a frame for transmission at the next TXOP
  A common scheduler is suitable for QoS levels 1 & 2
The channel access function (EDCF, EPCF-Station) is independent of the scheduler
MAC SAP
MLME SAP
Scheduler
Channel Access
Queues

## Slide 8: Traffic Categories
For prioritized QoS, TC is (QBSS-global) delivery priority
  Defaults as in 802.1D-1998, Annex H.2, can be remapped via MIB (lowest) 1, 2, 0, 3, 4, 5, 6, 7 (highest) -- 0 is best effort
For parameterized QoS, TC selects the traffic specification
    Traffic specs are interpreted in the context of the source station's MAC address/AID, unless the source is not in the QBSS, in which case the destination station's MAC address/AID is used
    Parameters in traffic specification:
      TS Info (periodic/aperiodic, Ack policy, delivery priority)
      Retry Interval (for delayed Acks) & Polling Interval (for periodic polling)
      Transmit Interval (Committed Time for aperiodic)
      Nominal MSDU Size
      Minimum Data Rate & Mean Data Rate
      Maximum Burst Size
      Delay Bound & Jitter Bound

## Slide 9: MAC Functional Improvements
Direct ESTA-ESTA transfers
Directed Probe Request to find peers and learn capabilities
Improved Beacon reliability
  Rigid limit at TBTT (similar to CFPMaxDuration)
  Medium sensing to detect beacon collision
  BSS overlap information added to Beacons
  "Proxy Beacon" may be sent by ESTAs to inform adjacent APs
Allow RTS/CTS (with actual duration) during CFP
CF-Polls convey TXOPs with specified duration
Clarify many ambiguous provisions in 802.11-1999

## Slide 10: New MAC Mechanisms (general)
Transmission Opportunities (TXOPs)
  The right to transmit defined by starting time & duration limit
    Applies to EDCF contention winner as well as CF-poll recipients
    Limit is global during CP, piggybacked with poll during CFP
  Can be allocated in advance during CFP
Traffic Category Identifiers (TCIDs)
  A 2-octet field at end of MAC header in QoS data subtypes
    High-order 3 bits are priority parameter for MSDU
    Same layout as TCI field of 802.1Q VLAN tag, VID field is reserved
    Amount of traffic queued for TC piggybacked during CFP
  Some control frames and elements use TCA field with {TC,AID}

## Slide 11: New MAC Mechanisms
  Aggregation of multiple MPDUs into a single PSDU
  Burst transfers (EDCF) of SIFS-separated frames that fit in TXOP
  Delayed Acknowledgment (level 3 only)
    Basic format allows up to n*16 unacknowledged frames per TC
    A "retry delay" parameters allows fallback to ARQ
  Centralized Contention & Reservation Request (EPCF only)
  Alternate EAP/EPC
  BSS Overlap Mitigation
  Bridge Portals

## Slide 12: Enhanced DCF
Priority-based Distributed Coordination
  To achieve fairness access among traffic of the same priority at different stations
  And relative to best effort traffic from legacy stations
  Without a penalty for non-used traffic classes
Details will be “Black Box” in Baseline draft text and resolved based on proposals made through November 2000.
Details in separate presentations

## Slide 13: Enhanced PCF
Largely based on the detailed effort from the Joint Proposal (00/071, 00/120) by AT&T, Lucent, Sharewave, and others (00/120r1)
Uses mechanism enhancements from Joint Proposal
    Centralized Contention (CC)
    Reservation Request (RR)
    Ack Policy (normal, delayed, none)
    TXOP limit and TC size piggybacked on QoS data frames
    CF-Multipoll for multiple TXOP assignment
    CF-Schedule for periodic (CBR-type) traffic
But does not require BSS-unique VSIDs nor external classifier entities

## Slide 14: MLME SAP
Minor additions to Scan, Start, Join, etc. to add QoS levels as association attributes
MLME-TSUPDATE.request/confirmation used to define and modify traffic specifications
MLME-WMSTATUS.request/confirmation for WLAN-aware higher-layer bandwidth reservation and QoS management entities to obtain information on the state of the wireless medium

## Slide 15: Aggregation
To send multiple MPDUs in a single PSDU
Uses special management frame known as "Container"
  Directed MPDUs to single address (unicast container)
  Multicast MPDUs to a single group address (multicast container)
  Broadcast and/or multicast MPDUs to any group address (broadcast container)
Either immediate acknowledgement or delayed acknowledgement (if level 3 QoS)
Size nominally limited to 2302 octets

## Slide 16: Power Save
Listen Epoch
  Portions of beacon interval when power save ESTA is awake
  ESTA requests amount of awake time, EAP assigns epoch(s)
Level 1
  Uses existing power save with PS-Poll
Level 2
  EAP can use "PS-non-poll" during WSTA's listen epoch
Level 3
  TXOPs can be allocated during listen epoch to allow direct ESTA-ESTA under power save

## Slide 17: Incomplete Items & Placeholders
FEC (at MAC layer)
EDCF channel access
BSS Overlap Mitigation (partial)
Bridge Portals
Interaction with HL end-to-end QoS management entities

## Slide 18: Open Issues (from November Meeting)
TomT
  want all pieces mandatory if implementing the QoS option
  does not want options inside of options
Anil
  level 3 is too complex, in the absence of justification should be dropped
  scheduled TXOPs, very hard to implement, cost/benefit concerns
  aggregation, too limited to be worth the effort
  delayed acknowledgement is unjustifiable in a MAC protocol
Bob Miller
  there should be no options, or collapse levels (presumably 1 & 2 to 1.5)
Matthew Sherman, Harry Worstell
  wants to merge levels 1 and 2 into a level 1.5

## Slide 19: Open Issues (from November Meeting)
Sungyhun
  need bss overlap mitigation, but wants more details are needed
Wen-Ping
  wants to use same level 0 frames for level 2 PCF
  primarily wants to remove RR/CC in level 2
John K.
  concern over whether QoS under DCF is useful, wants mainly level 3
Raju & Matthew Fischer (changed from no to abstain based on responses)
  wants fec frame format from joint proposal included for use with 802.11b
  wants to reserve the 4 NoData qos data subtypes, the reason the 2 +CF-Ack
  polling interval and transmission interval redundant in traffic specification
    marked as open issue in 360r2
  retry interval in TU
    this was discussed in NJ, is not always a benefit, and appears to hurt jitter because ESTA's TXOP may fall too early in subsequent superframe to be usable for retries, probably still open
    (marked as an open issue in 360r2)

## Slide 20: Open Issues (from November Meeting)
Raju & Matthew Fischer (changed from no to abstain based on responses)
  qbss activtity change not present the QoS action code is assigned and placeholders are included in 360r1 (7.4.4 & 7.4.5), don't know if issue is still open
Kahlid
  Wants one simulation framework
Adrian
  concerned about real-time response (implied that 2us responses must be hardwired??)
Bob Meier
  Concern about the overlapping BSS mitigation mechanism, would be happy with black box for now.
  made remark about PCF "not obvious that it is really contention free ...“ <<not said at meeting: we had a semantic problem with this once or twice before -- the name is not ideal but is in the published standard, so we may need again to clarify that "contention" in this context means "CSMA channel access contention" which is indeed absent during the CFP ("CSMA-free period" ??). What may occur during the CFP is co-channel interference from a hidden station or nearby BSS.