## Slide 1: Distributed QoS resolution Greg Chesson- Altheros Wim Diepstraten- Lucent Technologies WCND Duncan Kitchin- Intel Harold Teunissen- Lucent Technologies Menzo Wentink- Intersil/NWN Prepared by: Wim Diepstraten

## Slide 2: Proposal Agreement
We did come to an agreement.
  Resolved all misunderstandings between the proposals.
  Agreed on vDCF as the basic mechanism (as in Oct 18 proposal).
    Use vDCF as a Scheduler for both level 1 and 2 (Stations)
  We converged on the “Fairness” definition.
    Statistical equal Tx-Op probability across the whole BSS within a traffic category as in standard DCF.
  Agreed on additional mechanism questions
    vDCF Retry mechanism
    IBSS mechanism
    AP preferential access methodology
Extremely simple to implement.
  Will publish pseudo code
D-QoS simulations
  Encouraging first results, will publish.

## Slide 3: General Framework
802 D-SAP,
3-bit traffic class
MPDU Scheduler
Number of Q’s depends on QoS level
Channel access function independent of scheduler
D-SAP
M-SAP
Scheduler
Access

## Slide 4: Basic Concepts
Basic framework should conceptual work for both level 1 and level 2 station mechanism.
  During CFP the random number generation aspect of vDCF can be the schedule mechanism.
    While the PCF determines the Tx-Op
  During the CP the vDCF scheduling and access mechanism is active.
    Where the parallel DCF backoff mechanism is generating the Tx-Ops.
In an ESS a “Load monitor” function in the AP will determine the CW per priority class, which is to be adopted by every station.
  The translation from “Load to CWx vectors” is NOT standardized.
In an IBSS a default CWx map is assumed, but a CWx distribution by a “Load Monitor” function will override the default.
  In IBSS a ‘Load Monitor” function is not mandatory.
  The default assumes CW=31 as the “Best Effort” reference.

## Slide 5: V-DCF mechanism
Access differentiation controlled by a CWx parameter per priority category.
  Multiple DCF’s running in parallel, with conceptually an individual Backoff counter for Backoff and Post-Backoff.
    Implementations based on a single Delta-Backoff counter are possible.
  The scheduling function is based on random number generated per access priority level, using individual CWx parameters causing differentiation in access ratio according to: 1/CW3 : 1/CW2 : 1/CW1 : 1/CW0
At a local collision the highest priority frame is being transmitted, while the other DCF is deferring and generate a new Backoff.

## Slide 6: V-DCF retry mechanism
Functional Goal:
  Exhaustive Retry is to be prevented, when there is higher priority traffic Q’d up.
  Objective of the retry mechanism is to temporarily reduce the load of the station on the medium for stability reasons.
    To improve the probability of contention resolution success under high load conditions.
    And to circumvent possible hidden interferers causing the failure.
vDCF mechanism:
  Therefore the whole station (all vDCF’s) need to back off, and not only the vDCF that experience a failure.
    So all DCF’s need to double their CW’s and generate a new backoff

## Slide 7: Mechanisms needed
Priority in frame header
  a new field compatible with also the PCF approach needs to be defined.
D-QoS Element in the Beacon
  Containing the CWx list per access priority level.
  Which can also provide the “Total Load” info, which can be used for “Load Balancing” purposes.
Rules to use CW and retry change
  See elsewhere in this document.
Sequence# generation and Duplicate detection rule changes.
  To support the non-exhaustive retry approach in a station, it is needed to maintain a sequence# per SA.Class combination.
    So the sequencing rules need to change, such that individual S# is maintained per Class, and will increment.
    And AP’s and Station receivers need to maintain duplicate detection mechanism on a SA.Class basis, and expand its resources for that.
Capability exchange mechanisms to determine service levels.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 8: Mechanisms cont’d
In order to improve the efficiency of the AP, the AP should be allowed to concatenate multiple frames in one Tx-Access Opportunity.
  A (MIB?) limited burst of frames are allowed per access opportunity with SIFS in between.
  This can be done in a similar way as specified for fragmentation.
    With the “Duration” field containing the proper values for the next exchange.
    So Ack contains the duration of the next data frame, and its associated Ack.
Also a station can be allowed to send a burst, but limited to a max size (2304 Byte) duration equivalent size.
  We probably need to limit this functionality only to a 2304 Byte duration equivalent for the highest Basic rate only.
    To prevent excessive jitter.
    A Tx-Opp limit mechanism to reduce excessive medium occupancy situations, while allowing rate fallback.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 9: Conclusion
A D-QoS mechanism has been proposed that can be used in both ESS and IBSS environments.

## Slide 10: Next Steps
Prepare simulation results
  define simulation scenario’s (starting point simulation group)
Generate Clause 9.2 text for inclusion in the Baseline proposal.
Present D-QoS based on vDCF approach.