## Slide 1: A Framework for Evaluating 5GHz PARs

## Slide 2: Hard Lessons from 2.4GHz
The wireless channel is inherently shared with all devices in a physical location -- i.e. there is only one “wire” that must be shared by all communications in a given house.
Competing protocols in the same band, with similar capabilities (e.g. .11, Bluetooth, HomeRF) create many problems:
  Interference, and the perception/fear of interference
  Decreased volumes and increased costs due to fragmentation
  Lack of inter-operability, reducing the utility of devices
  Market confusion that delays adoption of new technology
  Increased cost for multi-mode devices and supporting legacy systems
Avoiding the above problems is the point of standards activities
Can we do better at 5GHz?

## Slide 3: 5 GHz Opportunity and Peril
Currently two primary types of WLAN standard compete in the 5.15-5.35 GHz band: 802.11a and Hiperlan2 (MMAC is similar to these)
802.11a, Hiperlan2, MMAC, and 5GWLIAG are all working at creating a single worldwide standard by merging these standards
For international regulatory recognition of 5GHz wireless networking, the industry must speak with one voice
However, there are discussions of standardizing new types of systems with similar performance and capabilities in this band:
  802.16 Fixed Wireless Access
  802.15 Personal Area Network (High Rate and Low Rate)
  HomeRF MM? (most likely to operate at 2.4GHz)

## Slide 4: 802’s Role
Protect the valuable resource of radio spectrum. We can’t afford the luxury of competing standards -- Token ring and Ethernet PARs would never have been approved if they were intending to use the same wire at the same time!
Avoid proposals that do not have distinct identity and are not compatible with existing standards in this band. Currently, 802 standard proposals pose a great threat to themselves.
Act proactively. Efforts to recover co-existence for competing, dissimilar MACs are costly, are unlikely to alleviate interference problems, and cannot achieve the other standardization benefits
802 is not serving the industry or consumer well when it creates interfering standards in the same spectrum that would be used in the same physical space.

## Slide 5: Building International Consensus
Over 60 corporations (5GWLIAG) documented concern that they cannot develop a WLAN market that is not international and is characterized by conflicting systems and protocols
The industry and 802 are already struggling for coexistence among defined WLAN systems with differing MACs
ETSI and ERC already allocated 5.15-5.35 GHz for indoor-only WLAN and BRAN opposes the use of 5.15-5.35 GHz for FWA
Overlaying new applications and protocols into designated 5GHz bands jeopardizes international allocations for WLANs
  Frequency spreading to accommodate WLAN users requires an adequate number of channels for spreading energy
  5.15-5.35 GHz must be shared with primary satellite services. Sharing studies assume indoor WLAN usage.

## Slide 6: Methods to Reduce Interference
Encourage greater use and incremental extension of already defined standards
  There is relatively little difference between the capabilities of 802.15.3 proposals and 802.11e/g
  Similarly, the 802.11e/a enhancements to 802.11 can most likely serve many of the 802.16 applications quite well
Encourage a partitioning of the spectrum. Examples:
  Request that new protocols for 802.16 use only licensed bands and the 5.725-5.825 GHz unlicensed band
  Encourage 802.15 to stay in the 2.4 GHz band
  Preserve the 5.15-5.35 GHz band for 802.11 WLAN

## Slide 7: Spectrum Partitioning Proposals
5 GHz spectrum partitioning proposals similar to that shown below are gaining consensus in international regulatory bodies and industry organizations.
Frequency (MHz) Use
5150-5350 WLAN
Indoor systems
200 mW EIRP maximum
5470-5725 WLAN
(where allocated) Indoor and outdoor nomadic access systems
5725-5825 Outdoor, Fixed Wireless Access systems
Up to 4W EIRP, depending on region

## Slide 8: A Unique Opportunity
It is not too late to save the 5GHz band from chaos
While some other organizations may create interfering standards in this band, 802 can take a leadership role in preserving its utility
There is an opportunity to create an international standard by being consistent with allocations set out by ETSI/CEPT, and possibly ITU and other international bodies
At the very least, 802 should not create interference problems with its own standards!