## Slide 1
‘Tiered Contention’, A QoS-Based Distributed Medium Access Control Protocol
Mathilde Benveniste
AT&T Labs, Research

## Slide 2: Scheduling by ‘urgency class’
A scheduling algorithm assigns the pending packet (in the access buffer) an ‘urgency class’ at each node.
Nodes access the channel in the order of decreasing urgency class of their access-buffer packet
To meet delay requirements, packet fragmentation is assumed because of non-preemptive transmission
Priority of packet in access buffer C > B > A
Packet Stream to Node A
Packet Stream to Node B
Access Buffer
Packet Stream to Node C
Contention
for access
CHANNEL
TRANSMISSIONS

## Slide 3
transmission
transmission
transmission
Time
Node C
Node B
Node A
UAT 2
UAT 3
UAT 1
Urgency Arbitration Times
Partitioning of contention by urgency class
Each urgency class is assigned a different arbitration time -- UAT
Arbitration Time = interval that the channel must be sensed idle by a node before decreasing its backoff counter.
Length of UAT decreases with increasing urgency.
Lower urgency packets will not cause collisions to higher urgency packets.
Higher urgency packets will dominate the channel in congestion as lower urgency packets would get less of a chance to decrease their backoff counters.

## Slide 4
Backoff window adjustment
Instead of increasing backoff ranges, start with a backoff counter appropriate for the traffic intensity at hand.
Retry upon failure with successively smaller backoff counters.
Discipline increases the persistence of aging packets and decreases contention.
The overall delay jitter is reduced.
Discipline is good for isochronous traffic.
In congestion, this discipline would be preferable for real-time traffic because of tendency to reduce long delays.
In light traffic, there is the risk that high starting backoff counters may postpone the transmission of the packet needlessly.
Better estimates of current traffic intensity would lessen problem.

## Slide 5
Congestion-adaptive, traffic-specific backoff
To select initial backoff, the nodes estimate traffic intensity from the number of failed transmission attempts, both their own and those of neighboring nodes.
  Each node remembers its own number of retrial attempts
  and broadcasts [i.e., includes in the messages exchanged during reservation and/or in the packet headers] its number of retrial attempts.
Alternatively, initial backoff is based on traffic intensity estimated by urgency class
  Each node remembers its own retrial attempts by urgency class,
  and broadcasts its number of retrial attempts by urgency class.

## Slide 6
Collision resolution combined with collision avoidance
Backoff before a transmission attempt; backoff is used for collision avoidance.
Given a good estimate of traffic intensity, the backoff counter can be set to disperse traffic bursts properly, thus reducing contention.
By postponing transmission of newly arrived packets at the outset, aged packets face less competition for the channel, with a reduction in resulting delay jitter.

## Slide 7
Exhausting retrial limit
A maximum retrial number or delay is permitted, after which transmission is cancelled.
A better discipline for packet transmission cancellation would rely directly on the delay experienced by the packet where the limit would vary by traffic type as
  delayed packets have little value and limited packet loss is acceptable for real-time traffic.
  data applications are tolerant of longer delays but intolerant of missing packets.

## Slide 8
Summary and conclusions
‘Tiered contention’ enables random multiple access control while supporting QoS management as follows:
Assigns urgency class to access buffer packet by various QoS-driven scheduling algorithms
Uses different ‘arbitration times’ for different packet ‘urgency classes’.
Broadcasts the number of (class-specific) transmission attempts
Estimates (class-specific) current congestion levels
Adjusts starting backoff counter to provide proper dispersion of traffic bursts and reduce contention.
Starts with traffic-adjusted backoff counters and decreases them upon transmission failure to reduce contention and increase persistence for aging packets.
Use collision avoidance through backoff with similar benefits.
Cancels transmission retrials based on delay-related criteria that discriminate between traffic types.