## Slide 1: Proposal to use KPS to Enhance Security of MAC Layer
Shinichiro Watanabe, Kazuaki Naito, Masayuki Ikeda
Seiko Epson Corporation
November 2000
Notes: This is a proposal for enhancing WLAN security by employing KPS in the MAC layer. The proposal discusses the suitability for small systems, such as peer to peer communications, and reinforced user authentication performed in the upper layer.
In March, we proposed KPS, or Key Predistribution System, to enhance MAC. This revised proposal is designed to fit the requirements issued after March.

## Slide 2: Reinforcing Security in the MAC Layer, and Problems with the Present IEEE802.11 WEP
The Need to Reinforce Security in the MAC Layer
- Dumb terminals; printers, BCRs, mobile terminals with low capacity, etc.
- Unmanned systems;
- Point to point systems.
Problems with the Present IEEE802.11 WEP
    Default-Key
      The following problems exist because the key is shared by a number of people.
        Authentication
        Allows unauthorized access to the network.
        Key establishment algorithm
        All the members of the group are exposed to risks including eavesdropping.
        Key expiration
        The key needs frequent changes, or it is easily broken.
    Privacy algorithm
      The privacy algorithm of the 40-bit RC4 is not very robust.
Notes: According to the Security Baseline Agreement, document number 321r1, MAC level negotiation uses the present IEEE802.11 or the upper layer algorithms.
But, there are some systems such as dumb terminals or unmanned systems in which there are no human operations, and user authentication is difficult.
Reinforcing security in the MAC layer of the wireless LAN is necessary for these systems.
The present IEEE802.11 WEP uses a default key set by the user. It is shared by group members. Therefore, this algorithm has the following problems.
If the key is somehow stolen, even once, all encrypted communications can be broken into and decoded immediately.
The person who stole the key can break the MAC authentication barrier and hack into the network.
If the key is stolen, all of the members of the group are exposed to risks including eavesdropping.
The key needs to be changed frequently, or it can be easily broken.
The 40-bit RC4 has a short key length. Therefore, as discussed, it cannot withstand violent attacks, thus allows communications to be easily decoded.
Other problems derived from relatively small initial vectors in the current 802.11MAC protocols are pointed out by Mr. Jesse Walker yesterday.
The following measures are necessary to solve these problems.

## Slide 3: Solution
Default-Key0
Default-Key1
Default-Key2
Default-Key3
Data
ICV
Data(plain)
Encryption
Solution
Current Algorithm
Default-Key0
Default-Key1
Default-Key2
Default-Key3
xor
Session key
Nonce
Encryption
Session key
(Encrypted)
Data
ICV
Data(plain)
Encryption
KPS
Shared key
Fig.1
Fig.2
Notes: In this slide, Figure 1 shows a block diagram of current 802.11 security protocols and Figure 2 shows a block diagram of my proposal.
For an authentication, the authentication data is encrypted using a session key generated in the MAC layer instead of the default key of the current 802.11 MAC, and the user authentication algorithm in the upper layer is used in parallel.
For the key establishment, the session key is encrypted by per-user keys generated by KPS in MAC layer. A shared key is generated in the MAC layer with the KPS. Then the shared key is exclusive-ORed with the default key to generate per-user keys.
For the data encryption, use a nonce generated in the MAC layer as a session key instead of a default key.
As described in Security Baseline Agreement r1, it is desirable to use an encryption algorithm, such as the 104-bit RC4 for the privacy algorithm.

## Slide 4: Effects of the Solution
Increases a security level of the communications between two STAs and between a STA and an AP.
  Unable to analyze the session keys
  Unable to decode the encrypted session keys
Suitable for systems with dumb terminals or unmanned systems
The security level of user authentication is increased.
  Usable with other authentication protocols in parallel.
  The authentication message is also encrypted.
User authentication
PC
PC
STA
Generation of per-user keys with KPS
STA
Encryption with session key
Notes: My proposal for encryption in the MAC layer would have the following effects.
It would increase the security level of communications between two stations, or between a station and the access point, that is the basis of communications.
  Analyzing the session key is disabled because the nonce generated within the MAC layer is used as the session key.
  The decoding of the session key or encrypted message is also prevented because the session key is encrypted with per-user keys.
Our proposal is suitable for such systems including dumb terminals or unmanned systems where there is no human operations.
By combining user authentication in the upper layer with the proposed MAC enhancements, the security level of the upper layer packets increases, and we can build more robust systems.
Now I would like to explain about the user authentication.

## Slide 5: User Authentications
Current user authentication
PC
PC
STA
KPS
STA
Default key
PC
PC
STA
KPS
STA
802.1X, GSS-API
PC
PC
STA
KPS
STA
Current user authentication + KPS
Default key + KPS
802.1X, GSS-API + KPS
Fig.1
Fig.2
Fig.3
Notes: The enhanced MAC with KPS can be used in combinations with various protocols in the upper layer.
In these figures, the boxes denoted PC indicate the upper layer algorithms, and STA boxes indicate MAC layer algorithms.
Figure 1 shows the combination with a legacy protocol of a current network. Even then, eavesdropping from the wireless media will be disabled and unauthorized access to the network will be prevented.
In the case of the IEEE802.1X WEP or GSS-API shown as in Figure 2, even the first packet of the communications from the upper layer can be protected by encryption with a per user key generated by KPS. Therefore, no data including authentication message can be stolen by outsiders.
Figure 3 shows an ad-hoc mode combined with KPS. Even if no ad-hoc user authentication is implemented, closed encrypted communications by KPS between two parties will still be enabled with the default key shared. The effect of which is virtually the same as mutual user authentication.
In this way, by enhancing the security within the wireless portion of communications by encryption in the MAC layer, and combining it with user authentication performed in the upper layer, we can reinforce security in large-scale wireless LANs as well as small-scale ad-hoc networks.

## Slide 6: Basic Flow of the KPS Communications
Setting a Private-ID
KPS Center
PA = G × (f1(A))T
(Procedure necessary only once)
MAC A
MAC B
NOTE：
PA or PB = Private-ID:1024bit×40bit
(Secret data / user)
A or B = Public-ID:48bit
(MAC Address)
f1 = One-way Scheme 1
G = Sytem-ID: 1024bit×1024bit×40bit
(symmetrical matrix )
PB = G × (f1(B))T
Notes: Here, I will briefly describe the use of KPS.
During production of the wireless devices that houses the MAC, the KPS center calculates confidential data (called a private ID; Pa, Pb...) derived from the MAC address, called a public ID; A, B,..., and a huge random-number matrix G, and writes it to the each MAC devices.
This operation is implemented only once during MAC production.
Confidential information is thus embedded into the device, but a proper hardware design can prevent external access. Even if someone succeeded in accessing this information, it would be impossible to learn the confidential information of the other terminals. This is because the matrix G used to calculate the private ID consists of 40 megabits, as in the example introduced in last March. On the other hand, there are only 40 kilobits in the private ID. This means that someone would have to disassemble an extremely large number of devices in order to collect sufficient information to decipher the matrix G.

## Slide 7: Basic Flow of the KPS Communications
KPS Communications
Public-ID B
(MAC Address B)
KAB
Receiver B
(MAC Address B)
Public-ID A
(MAC Address A)
Sender A
(MAC Address A)
KPS Module
KPS Module
KBA
Default key
Per-user keys
Default key
Per-user keys
Session key
Encryption
Encrypted
Session key
Decryption
Session key
Encryption
Decryption
Encrypted DATA
DATA
DATA
KAB = f2 ((f1(B))T ×PA
KBA = f2 ((f1(A))T ×PB
KAB = KBA
NOTE:
f2 = One-way Scheme 2
Notes: Next, I’ll describe the process during communications.
The sender calculates a shared key, Kab inside the MAC from the public ID, B, of the destination and the private ID, Pa, of the source. Per-user keys are generated from the shared key, Kab, exclusive ORed with the default key.
A nonce generated within MAC is used as a session key, and the session key encrypted with the per-user key is sent to the party.
Then, the transmission data is encrypted with the session key and encrypted data are sent.
The receiver calculates the shared key, Kba, from the public ID, A, of the source received and the private ID, Pb, on the reception side. Then the shared key, Kba, is exclusive ORed with the default key to generate a per-user key.
The generated shared key, Kba, has the same value as that of the sender, Kab.
Then, the encrypted session key is decoded with the per-user keys, and the encrypted data is then decoded using the (decoded) session key.
For more details about KPS please refer to the Document numbered 031S.

## Slide 8: KPS v.s. Public key systems
KPS does not requires;
- The MAC address to be paired with a public key.
- The public key transmission frame.
Notes: Let me compare the KPS systems with the public key systems (especially D/H systems)
The MAC address is handled as public information in the KPS systems. Therefore, the MAC address need not be paired with a public key as in the Public key systems.
In the public key systems a frame to send a public key is necessary. But, no public key frame transmission is required in the KPS systems.

## Slide 9: Conclusion
Necessary to enhance the MAC security algorithm.
Combining with the upper layer security algorithm systems can be much more robust against attacks.
We proposed;
  To use session keys instead of default keys
  To use per user keys. Per user key is made by XOR-ing a default key and a shared key generated by KPS
  To encrypt the session keys with per user keys generated in the MAC layer.
Notes: I will now conclude my presentation.
1. Enhancing the MAC security algorithm is necessary for such systems including dumb terminals or unmanned systems.
2. Combining KPS with the upper layer security algorithms the system can be much more robust against attacks.
3. We proposed;
  to use session keys instead of default keys,
  to use per user keys. Per user key is made by XOR-ing a default key and a shared key generated by KPS,
  and to encrypt the session keys with per user keys generated in the MAC layer.