## Slide 1: A Joint Proposal for 802.11 Security
David Halasz, Stuart Norman, Glen Zorn
Cisco Systems, Inc.
Bernard Aboba, Tim Moore
Microsoft
Jesse Walker, Intel
Bob Beach, Symbol
Bob O’Hara
Informed Technology

## Slide 2: Outline
Introduction, Goals
Overview of 802.1X
EAP
Packet exchanges
Roaming
Sample topologies
Proposed 802.11 changes
Proposed 802.1X changes
Summary

## Slide 3: Introduction
Represents merger of proposals 275, 292 and 293
Enables use of Kerberos for authentication and fast handoff
802.1X and EAP used as the authentication transport
Works with Kerberos KDC and (optionally) RADIUS authentication server

## Slide 4: Goals
Extensible system
Modular
Authentication done at higher layer protocol
Per-session key distribution
Session encryption at IEEE 802.11 layer
Promote multi-vendor interoperability
Minimize changes to IEEE 802.11, 802.1X
Define mandatory authentication method
Fast handoff
Ability to add new authentication methods easily (without changing 802.11)

## Slide 5: Approach
Based on existing protocols
  Kerberos (RFC 1510)
  GSS-API (RFC 2743)
  IAKERB (draft-ietf-cat-iakerb-05.txt)
  EAP-GSS (draft-aboba-pppext-eapgss-02.txt)
  802.1X/EAPOL
  EAP (RFC 2284)
  802.11
Adapted for use with 802.11
  Relatively few changes required to 802.11, 802.1X

## Slide 6: 802.11 to 802.1X adaptation layer
Supplicant
Authenticator
Supplicant
1 . . . N
One IEEE 802.11 physical port becomes 1 to N virtual IEEE 802.1X ports.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: IEEE 802.1X Terminology
Controlled port
Uncontrolled port
Supplicant
Authentication Server
Authenticator
Pieces of the system.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8
Normal Data
Authentication traffic
Wireless laptop
Authentication Server
Access Point
802.1X traffic
Authentication traffic
Wireless client associaton at 802.11 layer: Data blocked by the AP
Access Point blocks everything except 802.1X to authentication traffic.
Authentication traffic is allowed to flow. Access point encapsulates 802.1X traffic into authentication server traffic and vice versa.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9
Normal Data
Authentication traffic
Wireless laptop
Authentication Server
Access Point
802.1X traffic
Authentication traffic
Wireless client mutually authenticates with Authentication Server
Access Point blocks everything except 802.1X to authentication traffic.
In the authentication process the supplicant securely obtains a WEP key.
The authentication server also sends the WEP key in the success packet to the AP. AP uses the WEP key to send the broadcast WEP key.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10
Normal Data
Authentication traffic
Wireless laptop
Authentication Server
Access Point
802.1X traffic
Authentication traffic
Wireless client and AP use WEP key, AP allows traffic to flow
After successful EAP authentication, the Access Point allows all traffic to the Wireless laptop.
The Wireless laptop sets the WEP keys through the MLME interface. (e.g. NIC driver)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: EAP Framework
EAP provides a flexible link layer security framework
  Simple encapsulation protocol
    No dependency on IP
    ACK/NAK, no windowing
    No fragmentation support
  Few link layer assumptions
    Can run over any link layer (PPP, 802, etc.)
    Does not assume physically secure link
      Methods provide security services
    Assumes no re-ordering
    Can run over lossy or lossless media
      Retransmission responsibility of authenticator (not needed for 802.1X or 802.11)
EAP methods based on IETF standards
  Transport Level Security (TLS) (supported in Windows 2000)
  GSS_API (including Kerberos)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: EAP Architecture
EAP
Layer
Method
Layer
EAP
TLS
Media
Layer
NDIS
APIs
EAP
APIs
PPP
802.3
802.5
802.11
IKE
GSS_API

## Slide 13: EAP-GSS and IAKERB
EAP-GSS (draft-aboba-pppext-eapgss-02.txt)
  Use of GSS_API authentication methods within EAP
  Typically will NOT use SPNEGO
IAKerb (draft-ietf-cat-iakberb-05.txt)
  GSS-API method enabling proxy Kerberos
  STA not able to talk to KDC directly prior to authentication
  Initial authentication
    IAKERB enables STA to obtain TGT, Ticket to AP
  Handoff
    Ticket to AP

## Slide 14: Initial Contact
Associate
EAP Identity Request
EAP Identity Response
EAP-GSS Request (Empty)
EAP-GSS Response (IAKERB: AS_REQ)
AS_REQ
EAP-GSS Request (IAKERB: AS_REP)
AS_REP
EAP-GSS Response (IAKERB: TGS_REQ)
TGS_REQ
EAP-GSS Request (IAKERB: TGS_REP)
TGS_REP
EAP IAKERB Response (Empty)
EAP-Success
EAP-Key (AP_REQ)
EAP-Key (AP_REP)
STA
AP
KDC
802.1X Unblocks
802.11 Unblocks

## Slide 15: Security Services
Authentication method defaults to IAKERB
  If STA attempts SPNEGO, AP will choose IAKERB
802.11 encryption turned on after AP_REQ/AP_REP exchange
Authentication of client to KDC (TGS_REQ)
  PADATA typically NOT used with AS_REQ!
Authentication of KDC to client (AS_REP, TGS_REP)
Session key for client-AP communication (TGS_REP, AP_REQ)
TGT, Session key for client-KDC communication (AS_REP)
Authentication of client to AP (AP_REQ)
Authentication of AP to client (AP_REP)

## Slide 16: Roaming Within Realm
Associate
EAP Identity Request?
EAP Identity Response?
EAP-Success
EAP-Key (AP_REQ)
EAP-Key (AP_REP)
STA
AP
KDC
802.1X Unblocks
802.11 Unblocks

## Slide 17: Roaming Issues
How does the STA discover the AP realm?
  Realm placed in Probe Response if asked for by the STA
  Alternative: IAKERB KRB_AP_ERR_REALM_REQUIRED error message, more packets
How does the AP obtain the authorizations for the supplicant?
  Can contact RADIUS server
    Adds an extra roundtrip
    No authorization-only message in RADIUS
  No contact with backend desirable
    RADIUS server can’t validate the ticket to the AP anyway
    Reduces latency
  Authorizations included in PADATA of AP ticket
    Authorizations obtained by KDC from RADIUS server on initial contact and plumbed by the AP on ticket/authenticator validation

## Slide 18: RADIUS Topology
Authenticator
(e.g. Access Point)
Supplicant
Enterprise Network
Semi-Public Network /
Enterprise Edge
AuthenticationServer
RADIUS
EAP Over Wireless (EAPOW)
EAP Over RADIUS
PAE
PAE

## Slide 19: Kerberos Topology
Authenticator
(e.g. Access Point)
Supplicant
Enterprise Network
Semi-Public Network /
Enterprise Edge
AuthenticationServer
KDC
EAP Over Wireless (EAPOW)
EAP-GSS with IAKERB
Kerberos
PAE
PAE

## Slide 20: RADIUS with EAP-GSS Topology
Authenticator
(e.g. Access Point)
Supplicant
Enterprise Network
Semi-Public Network /
Enterprise Edge
AuthenticationServer
RADIUS
EAP Over Wireless (EAPOW)
EAP-GSS with IAKERB
EAP-GSS Over RADIUS
PAE
PAE
KDC

## Slide 21: Broadcast Key Distribution
Broadcast key(s) gets securely delivered to the station via IEEE 802.1X EAPOL-Key.
  EAPOL-Key message encrypted using session key obtained in AP_REQ/AP_REP exchange
Authentication server timer gets configured to re-authenticate/re-key the client.

## Slide 22: Mapping to Requirements (1)
Mutual authentication (4.1.1): satisified by Kerberos
Accommodation with QoS (4.2.1): satisfied by Kerberos
Access control (4.2.2): GSS-API can be integrated into 802.11 access control model
Key derivation (4.4.1): satisfied by all GSS-API mechanisms
Security service negotiations (4.5.1): satisfied by EAP or SPNEGO pseudo-mechanism
Extensibility (4.5.2): extensibility via EAP or GSS-API

## Slide 23: Mapping to Requirements (2)
One mandatory-to-implement algorithm (4.5.3): Kerberos only mandatory-to-implement security mechanism
Scalability to all 802.11 environments (4.6)
  Mandatory to implement mechanisms support Enterprise, SoHo
  PKINIT for ad hoc support

## Slide 24: 802.11 layer
Initial client authentication
  Open authentication used, since dynamically derived WEP key not yet available
  After 802.1X authentication and setting dynamic key, run with WEP
  AP needs to be able to support a mixture of WEP/non-802.1X and non-WEP/802.1X data
  Station needs to be able to run WEP/non-802.1X and non-WEP/802.1X

## Slide 25: Proposed Change to 802.11 Authentication Exchange
Association occurs before authentication
Addition to 7.3.1.1 Authentication algorithm Number Field
  Authentication algorithm number = 2
  Authentication handled by EAP in upper layer

## Slide 26: Proposed Change: 802.11 authentication
Add bit to capabilities to mean ”upper layer authentication” so AP can advertise what it is capable of doing.
New 802.11 MAC authentication type
  Same as open handshake but with different algorithm number

## Slide 27: Current 802.11 Privacy capability
From 7.3.1.4 Capability Information
APs set the Privacy subfield to 1 within transmitted Beacon, Probe Response, Association Response and Reassociation Response Management frames if WEP encryption is required for all Data Type frames exchanged within the BSS. If WEP encryption is not required, the Privacy subfield is set to 0.
STAs within an Independent BSS set the Privacy subfield to 1 in transmitted Beacon or Probe Response Management frames if WEP encryption is required for for all Data Type frames exchanged within the IBSS. If WEP encryption is not required the Privacy subfield is set to 0.

## Slide 28: Proposed Change for Identifying 802.1X Traffic
Broadcast/Multicast data in mixed 802.1X cell run with WEP. If run broadcast without WEP, then encrypted traffic open to attack.

## Slide 29: Proposed change to 802.11 Privacy capability
Addition to 7.3.1.4 Capability Information
STAs set the Privacy subfield to 1 in transmitted Probe Request and Association Request Management frames if WEP encryption is required for all Data Type frames exchanged. If WEP encryption is optional the Privacy subfield is set to 0.

## Slide 30: Changes to 802.1X
EAPOL-Key message used to carry AP_REQ/AP_REP exchange
EAPOL-Key message needs to go from Supplicant (STA) to Authenticator (AP)
  Current 802.1X spec only supports sending EAPOL-Key from Authenticator to Supplicant

## Slide 31: For Further Investigation
Cross-realm authentication
Roaming authorizations
EAP negotiation and support for additional authentication types
Integration of 802.1X and 802.11 state machines

## Slide 32: Summary
This proposal will promote multi-vendor interoperability by making authentication an upper layer function based on 802.1X
Largely based on existing protocols with minor changes to 802.11
Changes to 802.1X specification should be made to enable transmission of keys from STA to AP
Changes to the IEEE 802.11 specification should be made to allow for mixed WEP cells and for more secure WEP data packets.

## Slide 33: For More Information
IEEE 802.1X
  http://grouper.ieee.org/groups/802/1/pages/802.1x.html
Kerberos/GSS-API
  http://www.ietf.org/rfc/rfc1510.txt (Kerberos V)
  http://www.ietf.org/rfc/rfc2743.txt (GSS-API)
  http://www.ietf.org/internet-drafts/draft-ietf-cat-iakerb-05.txt
RADIUS
  http://www.ietf.org/rfc/rfc2138.txt
  http://www.ietf.org/rfc/rfc2139.txt
  http://www.ietf.org/rfc/rfc2548.txt
  http://www.ietf.org/rfc/rfc2865.txt
  http://www.ietf.org/rfc/rfc2866.txt
  http://www.ietf.org/rfc/rfc2867.txt
  http://www.ietf.org/rfc/rfc2868.txt
  http://www.ietf.org/rfc/rfc2869.txt
EAP
  http://www.ietf.org/rfc/rfc2284.txt
  http://www.ietf.org/rfc/rfc2716.txt
  http://www.ietf.org/internet-drafts/draft-aboba-pppext-eapgss-02.txt

## Slide 34: Backup Slides

## Slide 35: Extensibility: EAP negotiation
Negotiation at EAP driven from server
  AP requests identification on initial association
  Client responses with identity
  Authentication Server responds with EAP-Type
  Client responds with credentials in that type or NAK with suggested EAP Type
  EAP negotiation not protected

## Slide 36
Wireless laptop
Radius Server
New EAP authentication types can be added in Supplicant and Authentication Server
Station and AP are aware of the authentication transport. But, they are unaware of the authentication type.
Therefore, new authentication types can be added without modifying the station or the AP.
Authentication points
Notes: <number>
<footer>
<header>
<date/time>

## Slide 37
Wireless laptop
Authentication Server
New EAP authentication type benefits everybody
Vendor A AP
Vendor B AP
Vendor C Switch
Notes: <number>
<footer>
<header>
<date/time>

## Slide 38: Extensibility: GSS-API SPNEGO
GSS-API negotiation mechanism
  SPNEGO enables selection among GSS-API mechanisms
  Negotiation protected as long as the negotiated mechanism provides authentication, integrity protection
  STA will typically use IAKERB directly, rather than SPNEGO
  AP should support SPNEGO even if only IAKERB GSS-API mechanism is available