## Slide 1: A Scheduling Scheme for Level-2 Enhanced PCF MAC Service
Wen-Ping Ying
Mike Nakahara
Sigong Ho
NextComm, Inc.
Kirkland, Washington

## Slide 2: Nature of Level-0 CF
DCF –
  Channel Access is probabilistically fair.
  Medium contention is a function of offered load from higher layer.
  Congestion control is achieved via backoff.
  In favor of more contentious applications.
PCF –
  Channel Access is deterministically fair.
  Medium contention is independent of offered load from higher layer (relatively speaking)
  No need for congestion control (except retry treatment).

## Slide 3: Base-line Model As Proposed In vDCF Scheme
802 D-SAP,
3-bit traffic class
MPDU Scheduler
Number of Q’s depends on QoS level
Level-0 Channel access function independent of scheduler
D-SAP
M-SAP
Scheduler
Access

## Slide 4: Objective of vDCF QoS
To prioritize frames based on a common scheduling algorithm observed by all STAs.
To use the Level-0 channel access mechanism (CSMA/Poll) for delivering prioritized frames.
To have the same behavior as non-QoS model when every frame has equal priority.

## Slide 5: Level-2 PCF Basic Model
Use a similar scheduler as in Level-1so that switching between CFP and CP will not result in major scheduling mechanism switches.
During CFP –
  the random number generation aspect of vDCF is used as the scheduling mechanism to rank order/prioritize the frames for transmission.
  The Level-0 PCF polling determines the channel access opportunity (Tx-Op).
During CP (vDCF) –
  the same random number used in rank ordering determines the relative backoffs and sequence for frame transmission (as specified in vDCF).
  The Level-0 DCF channel sensing determines the channel access opportunity (Tx-Op).
The “Load monitor” information (CW vector) announced by AP during CFP may be adopted by STA so that STA can adjust to the network dynamics when CP begins.

## Slide 6: Level-2 Pollable-STA in CFP
Access differentiation controlled by a CW parameter per priority category as stated in the proposed base line vDCF document.
  Only one frame from one priority queue to be retrieved by the Scheduler.
  The backoff count is used only for proper rank ordering during this period. No backoff count decrement shall be performed.
  The first frame on the Tx Q shall be transmitted upon receiving a poll independent of the backoff mechanism (backoff counter value of the frame).
  When a frame is successfully transmitted, a new frame from that priority queue is retrieved (or frames, one from each previously empty queue.) Rescheduling is performed as described in the base line document.
  Scheduler may adopt the CW vector during this period so that when transiting to CP, the backoff values are up-to-date with the dynamics of the network.
F0
F1
F2
F3
Tx
Scheduler
CW3
CW2
CW1
CW0
F0(9)
F2(7)
F3(3)
F1(3)
Poll
Tx Queue
F3(3)
F2(10)
F1(22)
F0(19)
Prioritization
Serialization

## Slide 7: Scheduling Alternative
Access differentiation controlled by a CW parameter per priority category as stated in the proposed base line vDCF document.
  Only one frame from each priority queue is used by the Scheduler for selection purpose.
  The same random number generation based on the CW is used to tag the priority of the frames. The one with the smallest number is selected to be delivered at the next TxOp.
  When a frame is successfully transmitted, all the frames at the front of each priority queue are used for the priority selection process again
  Scheduler may adopt the CW vector during this period so that when transiting to CP, the backoff values are up-to-date with the dynamics of the network. If the CW vector is not kept up-to-date, the last CW vector may be used for Level-1 scheduling processing (or learn from the next load monitoring frame.)
F0
F1
F2
F3
Tx
Scheduler
CW3
CW2
CW1
CW0
Poll
Tx Buffer
F3(3)
F2(10)
F1(22)
F0(19)
Prioritization
Serialization
F3(3)

## Slide 8: Level-2/1 STA in CP
Same access differentiation controlled by the CW mechanism outline in the previous slide.
  Only one frame from one priority queue to be retrieved by the Scheduler.
  The backoff count is used sort out a delay sequence for transmission during this period. The legacy DCF backoff procedure is used as stated in vDCF base line.
  When making transition from CFP to CP, the Scheduler reuses the backoff counters from the CFP for backoff purpose. This process remains the same for both pollable (Level-2) and non-pollable (Level-1) STA since the adoption of CW vector is required even during CFP.
  This scheme shall be the same as Level-1 proposal.
TxOP based on the DCF channel access mechanism
F0
F1
F2
F3
Scheduler
CW3
CW2
CW1
CW0
F0(9)
F2(7)
F3(3)
F1(3)
Tx Queue
F3(3)
F2(10)
F1(22)
F0(19)
Prioritization
Serialization
Backoff

## Slide 9: Level-2 AP in CFP
Accommodate priority scheduling to Level-0 CFP polling mechanism in order to maintain the same level of performance as Level-0 CFP if all the frames have the same priority.
  Level-2 AP has to operate as a Point Coordinator for delivery and polling.
  All frames are regrouped based on the destination address and the pollability of the destination.
  Within each destination group, the same prioritization and scheduling as Level-2 pollable STA is used.
Burst mode delivery
A1
A2
A3
Non-pollable STAs
A1
A2
A3
An
NP
Polling & Frame Delivery
Level-0 pollable STAs

## Slide 10: Level-2 AP in CFP – Cont.
  The delivery of frames follows the sequence of the polling list AP generated. AP retrieves one frame from the scheduler of the address group being polled and piggybacks the frame in the Poll.
  All frames destined to non-pollable STAs are put into the same group in the order of arrival and the priority classification.
  AP shall retrieve frames from the non-pollable STA group after polling all the STAs at least once. The delivery of such frames can be in burst as described in vDCF proposal.
  Polling list shall be accessed in the round-robin fashion throughout CFP periods to ensure fairness in allowing the Level-2 STA to transmit.
Burst mode delivery
A1
A2
A3
Non-pollable STAs
A1
A2
A3
An
NP
Polling & Frame Delivery
Level-0 pollable STAs

## Slide 11: Level-2 AP in CFP – Cont.
Note: 1999 standard allows the immediate delivery of polled frame to non-pollable STA but encourages the buffering of polled frames to pollable STA such that piggy-back polling & delivery can be used to reduce the overhead. In this proposal, we recommend the latter so that there is no preference to the polled frame destined to non-pollable STA over pollable STA. We further recommend to deliver buffered frames destined to non-pollable STA at the end of the polling list. This NP delivery can be in burst mode as suggested in vDCF proposal to increase the efficiency of the delivery.

## Slide 12: Level-2 AP in CP
AP behaves as a Level-1 AP during CP.
  All the destination group queues and the non-pollable queues are collapsed into one 4-priority category queue.
  AP maintains this 4-priority category CP queue with all the outbound frames sorted in the order of time of arrival and priority category independent of the frame destination.
  Upon making transition to the CP, the Scheduler regenerates the Tx queue based on the result of the last CFP delivery. One undelivered frame from each of the CP priority queue will be used to generate the Tx queue using the prevailing CW vector information.
  The mapping between the CFP queues and the CP queues is implementation dependent (apparently an efficient way to obtain the Tx Queue is required when switching between CFP and CP.)
  The AP waits for the channel access mechanism to be cleared to deliver the frames in Tx queue.

## Slide 13: Level-2 Protocol Simplified (Interoperability)
No change to the Level-0 PCF Channel Access Mechanism
  drop RR, CC, CF-Multipoll from the Level-3 protocol.
  Polling sequence is vendor specific.
  Scheduling mechanism may be simplified during CFP for prioritization efficiency.
  Support new QoS load element for CW vector update.
  Support new Mgmt Action messages as needed (channel Management.
CC
CCI
CF-multipoll
QoS Data
CF-Poll
Data
CF-Poll
Data
Data
Burst Data
CC
CF-End
Level-3
Level-2/0 PCF
Level-0 N-Poll/
Level-1 dwn-lnk
DCF

## Slide 14: Benefit of Level-2 QoS
Virtue of Level-0 PCF Polling:
  Predictable fair-share among all pollable STAs.
  Efficient data transfer.
    Less overhead.
    Reduced chance of medium contention.
Virtue of Local Prioritization:
  Prioritization process is distributed.
  For each Level-2 (pollable) STA, frames with higher priority have higher probability to be delivered and received.
  No starvation of STA with only low priority frames

## Slide 15: Conclusion
A Level-2 QoS Architecture is proposed for both STA and AP.
When operating during the CP, the QoS mechanism is the same as Level-1 QoS.
Same Scheduler may be used for both Levels to allow ease of transition between CFP and CP.
Priority Queues on AP change between CFP & CP but stay the same for STA.