## Slide 1: Overview of OFDM for a High Rate Extension
Steve Halford
Mark Webster
Intersil Corporation
Palm Bay, FL
Overview and Outline of Proposal

## Slide 2: Outline of Proposal Presentations
TGg Regulatory Approval Plan Speaker: Jim Zyren
Overview of OFDM for High Rate Speaker: Steve Halford
Reuse of 802.11b Preambles with OFDM Speaker: Mark Webster
Ultra-short Preamble with HRb OFDM Speaker: Mark Webster
OFDM System Performance Speaker: Steve Halford
Power Am Effects for HRb OFDM Speaker: Mark Webster
Channelization for HRb OFDM Speaker: Mark Webster
Phase Noise Sensitivity for HRb OFDM Speaker: Jim Zyren
Implementation and Complexity Issues for OFDM Speaker: Steve Halford
Why OFDM for the High Rate 802.11b Extension? Speaker: Jim Zyren

## Slide 3: 2.0 Why go to higher rates at 2.4GHz?
802.11b has been very successful
  Large existing Infra-structure & customer familiarity
Consumer demands for higher data rates
  Enable multi-media for home market
Superior Range and Performance is possible
  2.4 GHz will have better range than 5 GHz for same power
  Allow for antenna diversity
  5 GHz won’t be as clean as promised (802.15.3, 802.16 co-exist)
Deployment of 802.11a is slow
Opportunity exists now for 802.11b to expand market

## Slide 4: 2.0 Keys for Successful High Rate System
Performance vs. Complexity must be attractive
  AWGN performance is important to maintain range
    Implies Error correcting code for higher rate systems
  Robust to multipath
    CCK is inherently robust & need to maintain this
Time to market must be short
  Standards & FCC will drive time to market
Maintain backward compatibility
Easy to extend to higher rates
  Why stop at 22 Mbps?

## Slide 5: 2.0 Waveforms for High Rate Extensions
Codeword Modulation  CCK-like extension
  Information is transmitted by codeword selection
    Each group of n bits select one of 2n codewords
  Block coding with inherent multipath protection
Symbol Modulation  PBCC-like extension
  Coded bits used to select constellation points
  QAM or PSK with convolutional or block code
  Standard modulation for satellite communications
Multi-Code Modulation  OFDM & DS-CDMA
  Coded bits are sent in parallel using orthogonal basis functions
  Used in OFDM and in synchronous DS-CDMA (e.g, downlink of IS-95 cellular)

## Slide 6: 2.1.1 Codeword Modulation
Current CCK systems  8 chip codewords
  11 Mbps: Each codeword sends 8 bits
    6 bits used to select one of 26 = 64 codewords
    2 bits used to QPSK modulate codewords
  Receiver must correlate for 64 codewords & determine QPSK value
    Uses a fast correlator structure akin to fast Walsh and FFT
  Total codeword size  28 = 256
Extension of CCK is possible to 22 Mbps
  Each codeword sends 16 un-coded bits
  Total codeword size  216 = 65536 codewords
  Requires very large correlator -- Some simplification possible
    Example: V. S. Somayazulu, et. al. , “Proposal for extension of the IEEE 802.11b PHY to higher rates (>20Mbps)”, IEEE 802.11-00/069, May 2000.

## Slide 7: 2.1.1 Codeword Modulation: Summary
Advantages
  Backward Compatibility
  Simple Rake Receiver for multipath protection
  Re-use of some existing baseband functions
  Low Peak to Average
    PAR > 1 due to pulse shaping
Disadvantages
  Doesn’t scale easily to higher rates
  Adding FEC would only increase number of codewords
    AWGN performance & range would be limited

## Slide 8: 2.1.2 Symbol Modulation
Current PBCC systems  1 information bit per symbol @ 11 Mbps
    Rate 1/2 Convolutional Code is used for AWGN performance
Extension of PBCC is possible to higher rates
  Example: Use 8-PSK & Rate 2/3 punctured code
    8-PSK gives 33 Mbps coded
    rate 2/3 gives 22 Mbps information rate
  Could use block code instead of CC
(n,k)
Encoder
Symbol
Mapping
(bits to PSK
or QAM)
Information
Bits
(Rate = R)
Pulse Shape
filter
Carrier Modulation

## Slide 9: 2.1.2 Symbol Modulation: Example
Rate 1/2
Viterbi
Encoder
22
Mbps
44
Mbps
8-PSK
11 MHz
Chips
Puncture
4:3
33
Mbps
Transmitter
Receiver
8-PSK
Demod
11 MHz
Rx
Sig
Rate 2/3
Soft
Dec
Gen
33 MHz
DePuncture
3:4
44 MHz
Rate 1/2
Viterbi
Decoder
22
Mbps
11 MHz
Linear Equalizer
CIR Estimator

## Slide 10: 2.1.2 Symbol Modulation: Performance
AWGN Performance is very good
Equalizer complexity can be high
  Linear Equalizer requires a matrix inverse to compute
    Long equalizer required for good performance
  Adaptive equalizers may not converge quickly enough
  Non-linear Equalizers: MMSE offers optimal performance
    Channel impulse response estimate required
    Can be combined with decoder (Joint MMSE)
    Implementation will not scale easily with increasing data rate
    Complexity increases exponentially with delay spread & data rate
    Reduced state version may be necessary
      Suboptimal & sensitive to estimation errors

## Slide 11: 2.1.2 Symbol Modulation: Example
7 tap equalizer
25 tap equalizer

## Slide 12: 2.1.2 Symbol Modulation: Summary
Advantages
  Well-known waveform
  Excellent AWGN performance
  PSK Versions: Low Peak-to-average
    PAR > 1 due to pulse shaping
Disadvantages
  No inherent multipath protection
    FEC provides some help
  Equalizer complexity is high
    Linear equalizer needs to be 25 taps or more
  Not easy to extend receiver to higher rates

## Slide 13: 2.1.3 Multi-code Modulation
Information is transmitted by modulating multiple codewords
  Codewords are summed and transmitted simultaneously
  Share both time and frequency
  Codewords create independent channels
  Used in IS-95 for multiple access
Serial
to
Parallel
(M outputs)
Map N bits
to one symbol
(QAM or PSK)
Map N bits
to one symbol
(QAM or PSK)
Map N bits
to one symbol
(QAM or PSK)
Coded Bits
Rate = R
Coded Bit
Stream
Rate = R/M
Coded Bit
Stream
Rate = R/M
Coded Bit
Stream
Rate = R/M

Pulse
Shape
Carrier Modulation
Codeword
(L chips/ symbol)
Codeword
(L chips/ symbol)
Codeword
(L chips/ symbol)

## Slide 14: 2.1.3 MCM: Receiver Considerations
Receiver must separate each codeword prior to detecting
  Use a bank of correlators to separate data streams
  Detect modulation after correlator for each stream
Codewords with fast correlator structure reduce complexity
  Example: CCK, Walsh words, and complex exponentials
Codeword #1
Correlation
Codeword #2
Correlation
Codeword #3
Correlation
Correlator Bank
Received
Data
Symbol
Soft-Decision
Symbol
Soft-Decision
Symbol
Soft-Decision
Parallel
to
Serial
(M inputs)
To Decoder

## Slide 15: 2.1.3 MCM: Codeword Selection
Performance is determined by codeword set used
  Orthogonal codeword give zero cross-talk
  Non-orthogonal codewords generate “noise” due to cross-talk
    Reduces the AWGN performance significantly
Walsh Sequences
Walsh Sequences are well known
  Sequences of +/-1
  Used in IS-95
Fast Correlator exists
Orthogonal sequences
Increases peak-to-average
Orthogonality is destroyed by multipath
  Need to equalize to restore
Problems ?
Almost all sequences lose orthogonality in multipath
Why ?
These sequences are not eigenfunctions of the multipath channel!

## Slide 16: 2.1.3 MCM:Multipath & Orthogonality
When the channel is known, can design functions to retain orthogonality
  Currently a “hot topic” for researchers in CDMA & Equalization
  Impractical for wireless LANs
Solution
Complex Exponentials are eigenfunctions of linear systems
  i.e., eigenfunctions for any multipath
  Equalizers not required
  Multipath causes a change in magnitude & phase only!!
Sets of complex exponentials are orthogonal frequency is 1/(symbol length)
FFT & IFFT provide for fast correlator
OFDM uses complex exponentials as codewords

## Slide 17: 2.1.3 MCM using OFDM: Summary
Advantages
  Good AWGN performance via error correction coding
  Excellent multipath performance
  Equalizer is greatly simplified!
    Equalizer complexity is the same for all data rates
  Existing Wireless LAN standard (802.11a) provides guidance
    Reduces time to market
Disadvantages
  Peak to average ratio requires more PA back-off
  Requires block processing
    May increase gate count due to memory requirements
  Frequency roll-off not as fast as symbol modulation

## Slide 18: 2.2 OFDM for High Rate at 2.4 GHz
Use 802.11a standard as a basis
  Selected by Task Group A as best waveform for wireless LANs
  Maintain all mandatory and optional PHY’s
  Accelerates the standards process by re-using existing standard
  Dual band Access Points could provide smooth transition
Increase sample rate from 20 MHz to 22 MHz
  Common clock rate with existing 11 Mbps systems
Maintain the same channelization
  US: 25 MHz center frequency spacing, 3 channels in 90 MHz
Use existing long & short preamble for compatibility
  Ultra-short preamble is also possible
Intersil will comply with all IEEE patent policy

## Slide 19: 2.2 OFDM for High Rate: Modulation Details
Transmit information using orthogonal carriers
  Carriers/Codewords generated efficiently using 64 pt. IFFT
  Use 48 tones for data
  Use 4 tones for pilot symbols
    Provides good method for carrier, timing, & AGC tracking
  Remaining 12 orthogonal tones are null (zero)
343.75 KHz Tone Spacing
52
Subcarriers
. . .
frequency
~17.875 MHz
. . .

## Slide 20: 2.2 OFDM : Modulation Details
Each data tone is symbol modulated
  Symbol Modulation is standard BPSK, QPSK, 16-QAM, or 64-QAM
Use rate 1/2, k = 7 convolutional code for error correction
  Puncture code to rate 2/3 and 3/4
Pilot tones are modulated with a BPSK sequence
  Sequence is determined by the data scrambler

## Slide 21: 2.2 OFDM for High Rate: Modulation Details
Coded Information is interleaved over one symbol
  Interleaved after puncturing
  Places adjacent “bits” on non-adjacent subcarriers
Data is also scrambled prior to coding
Data
Scrambler
Convolutional
Encoder
(k = 7)
Puncture
Interleave
Constellation
Mapping
(bits to symbols)
64-pt
Inverse
FFT
Uncoded
Information
Bits
Depends on data rate
Cyclic
Extension
to
80 samples
To RF subsection

## Slide 22: 2.2 OFDM for High Rate: Symbol Structure
Output of the 64 pt. IFFT is cyclically extended by 16 samples
  Length of 80 samples -- Any 64 pts valid for demodulation
  First 16 are used to “absorb” multipath from preceding symbol
16
Samples
64
Samples
IFFT/FFT SPAN
Guard
Interval
time
3.63 usecs OFDM Symbol
64 + 16 = 80 samples @ 22 MHz = 3.63637 usec
Preceding Symbol
Multipath will cause preceding symbol to”bleed” into current symbol. Guard interval absorbs this interference

## Slide 23: 2.2 OFDM for High Rate: Receiver Structure
Timing
Adjust
CNCO
Frequency Correction
Carrier/Timing
Correction
Trim
Guard
Interval
FEQ
52 tones
Frequency Domain Equalizer:
Multiply each tone by inverse gain & phase of the channel
Needs to know “when” a symbol starts
Soft-Decisions
on Bits
(symbol to bits)
De-interleave
De-puncture
Extract 4 Pilot
Tones
Viterbi
Decoder
Compute
Branch
Matrix
De-Scrambler
To MAC
From A-to-D

## Slide 24: 2.3 OFDM for High Rate: Summary

## Slide 25: Compliance Matrix

## Slide 26: Compliance Matrix

## Slide 27: Compliance Matrix

## Slide 28: Compliance Matrix