## Slide 1: Reuse of 802.11b Preambles with HRb OFDM
Mark Webster and Steve Halford
Intersil Corporation

## Slide 2: 802.11b Backward Compatibility Requirement
Must maintain all 802.11b signaling timelines.
Must reuse long preamble.
Can reuse short preamble option.
Must maintain SIFS, PIFS, DIFS, EIFS
Must maintain slot times.
Must maintain CCA reaction times.
Minimal MAC impact.
INTERSIL’s HRb PHY proposal meets all these requirements.

## Slide 3: INTERSIL’s HRb OFDM Meets the 802.11b 10 usec SIFS time

## Slide 4: Compatibility with 802.11b SIFS Using Existing Short/Long Preambles
Common Problem
for HRb Proposals
802.11b SIFS Time
of 10 usecs may be
a bit too short

## Slide 5: Compatibility with 802.11b SIFS Using Existing Short/Long Preambles
10
usecs
SIFS
16
usecs
SIFS
802.11b
802.11a
OFDM
Data
Data
ACK
ACK
Extra 6 usecs required for
FFT
De-interleave
Decoder flush
EXAMPLE:
802.11b SIFS time of 10 usecs is too short for the more
sophisticated 802.11a which has a 16 usecs SIFS. Why?

## Slide 6: Compatibility with 802.11b SIFS Using Existing Short/Long Preambles
802.11 DSSS
SIFS 10 usecs
802.11b
SIFS 10 usecs
802.11 HRb
SIFS 10 usecs
Inherit
Inherit
Complexity/
Latency
Note: Can trade latency for increased design complexity and higher speed clocks.
Receiver
Sophistication

## Slide 7: Compatibility with 802.11b SIFS
Advanced
Codeword Transforms
Extended CCK
Advanced Gold codes
Equalizers
FFT/FEQ
Viterbi Equalizer
Linear equalizer
DFE
De-interleaver
Combat impulse noise
FEC
Viterbi (flush)
Reed Solomon
Matched Filters
Channel matched filter
Whitened matched filter
802.11 DSSS
SIFS 10 usecs
802.11b
SIFS 10 usecs
802.11 HRb
SIFS 10 usecs
Inherit
Inherit
HRb Proposals
Have More Advanced
Demodulators

## Slide 8: Compatibility with 802.11b SIFS
aSIFSTime = aRxRFDelay + aRxPLCPDelay + aMACPrcDelay + aRxTxTurnaroundTime
SIFS TIME BUDGET
Rx PLCP Delay Impacted by
FEC Decoder
Deinterleaver
Equalizers
Codeword transforms
Reading/Writing Data Buffers

## Slide 9: Achieving Compatibility with 802.11b SIFS with Signal Extension
802.11
HRb
Signal
HRb Data
ACK
10
usecs
SIFS
Signal
Extension
Maintain 802.11b air interface
Create flush-processing margin via packet signal extension.
Extend to integer # of usecs consistent with length field in Barker preamble header
Maintains CCA energy
Proposed
Common
Solution
Length
usecs
Read
Length
usecs
Start
Receiver
Flush
Processing
BARKER
SYNC
BARKER
HEADER

## Slide 10: Compatibility with 802.11b SIFS. Pattern HRb after 802.11a’s Behavior.
802.11a OFDM Uses Last-Symbol Data Extension.
Propose doing something similar for HRb.
Symbol
Symbol
Symbol
Symbol
Last Symbol
4 usecs
4 usecs
4 usecs
4 usecs
4 usecs
802.11a
Rate Mbps Bytes/Symbol
6 3
9 4.5
12 6
18 9
24 12
36 18
48 24
54 27
802.11a Has a Mismatch between
1. Packet length and
2. Data Rate & Number of Bytes
OFDM Symbol Contains Multiple Data Bytes
Data bytes may not fill last OFDM symbol
Last symbol extended with scrambled zeros

## Slide 11: Compatibility with 802.11b SIFS
HRb Signal
w/o Extension
HRb Data
Length
usecs
Length
usecs
HRb Signal
w/ Extension
Packet Energy Not
Integer # of usecs
BARKER
SYNC
BARKER
SYNC
BARKER
HEADER
BARKER
HEADER
HRb Data
Read
Length
usecs
With
Extension
This Signal Extension Also Provides
On-the-Air Packet-Length Consistency

## Slide 12: INTERSIL’s OFDM Proposal Achieves Compatibility with 802.11b SIFS
802.11
HRb
OFDM
OFDM Data
ACK
10
usecs
SIFS
Signal
Extend
~ 6 usecs
BARKER
HEADER
BARKER
SYNC
Length
usecs
Read
Length
usecs
Start Receiver
Flush:
FFT,
De-interleave,
FEC Decode
Maintain 802.11b air interface
Create flush-processing margin by packet signal extension.
Extend to integer # of usecs consistent with length field in Barker preamble header
Maintains CCA energy

## Slide 13: PLME-TXTIME.Confirm Primitive Calculation for Long/Short Preambles
TXTIME (usecs) =
PreambleLength +PLCPHeaderTime + Ceiling( OfdmSync +
+ OfdmSigField + 4 *(16 + 8*LENGTH + 6 )/ N DBPS )*20/22
+ SignalExtension)
Flush
Processing
Margin
Length of
PSDU in
Octets
Number of
Data Bits
Per OFDM
Symbol
Clock Rate
Conversion
802.11a: 20 MHz
HRb: 22 MHz
FEC Flush
Bits
Scrambler State
& Full-Rate
Service Field
Representative Calculation

## Slide 14
INTERSIL’s HRb OFDM Proposal Reuses 802.11b’s Long/Short Preamble/Header

## Slide 15: HRb Long/Short Preamble Definition
HEADER
48 BITS
@ 2 Mbps
PREAMBLE
72 BITS
@ 1 Mbps
PSDU
SELECTABLE
@ 2, 5.5 OR 11 Mbps
HEADER
48 BITS
@ 1 Mbps
PREAMBLE
144 BITS
@ 1 Mbps
PSDU
SELECTABLE
@ 1, 2, 5.5 OR 11 Mbps
802.11b LONG PREAMBLE
802.11b SHORT PREAMBLE
96 usecs
192 usecs
1 and 2 Mbps uses 11 chip BARKER codes.
5.5 and 11 Mbps uses 8 chip CCK codes.
Chipping is at 11 MHz.
Data Payload
CURRENT 802.11b PREAMBLES

## Slide 16
HEADER
48 BITS
@ 2 Mbps
PREAMBLE
72 BITS
@ 1 Mbps
HEADER
48 BITS
@ 1 Mbps
PREAMBLE
144 BITS
@ 1 Mbps
802.11 HRb LONG PREAMBLE
802.11 HRb SHORT PREAMBLE
96 usecs
192 usecs
Data Payload
OFDM
SYNC
OFDM
SYNC
10.9 usecs
10.9 usecs
Service Field Bit
Denotes Switch to OFDM
Service Field Bit
Denotes Switch to OFDM
PSDU SELECTABLE
OFDM Symbols
@ 6.6, 9.6, 13.2, 19.8, 26.4, 39.3, 52.8 or 59.4 Mbps
PREAMBLES for 802.11 HRb:
Reuse 802.11b preambles
PSDU SELECTABLE
OFDM Symbols
@ 6.6, 9.6, 13.2, 19.8, 26.4, 39.3, 52.8 or 59.4 Mbps
Fine-Tune
SYNC

## Slide 17
HEADER
48 BITS
4 bits to denote extended data rates
4 bits of 5 to identify # bytes in last OFDM symbol.
SIGNAL
8 BITS
SERVICE
8 BITS
LENGTH
16 BITS
CRC
16 BITS
HRb SHORT/LONG-PREAMBLE
HEADER DETAIL
Unchanged
1 bit to denote OFDM mode.
1 bit of 5 to identify # bytes in last OFDM symbol.
Unchanged.
The Length Field is adequate, since measured in usecs.
OFDM proposal uses PSDU length in an integer number of usecs.

## Slide 18: Signal Field Bit Definitions
b0
b1
b2
b3
b4
b5
b6
b7
802.11b Signal Field
New 802.11 HRb OFDM Signal Field
b0
b1
b2
b3
b4
b5
b6
b7
Data Rate Mbps = 0.1 Mbps x ( b7 b6 b5 b4 b3 b2 b1 b0 ) base2
Rate
6.6 Mbps
9.9
13.2
19.8
26.4
39.6
52.8
59.4
b0-b3
1101
1111
0101
0111
1001
1011
0001
0011
25.5 Mbps maximum
Last Sym
Bytes
Resolve
Bit 0
Last Sym
Bytes
Resolve
Bit 1
Last Sym
Bytes
Resolve
Bit 2
Last Sym
Bytes
Resolve
Bit 3

## Slide 19: Service Field Bit Definitions
Reserved
b0
Reserved
b1
Locked
Clock Bit
0 = not
1 = Locked
b2
Mod. Selec-
tion Bit
0 = CCK
1 = PBCC
b3
Reserved
b4
Reserved
b5
Reserved
b6
Length
Extension
Bit
b7
b0
b1
b2
b3
Reserved
b4
b5
Reserved
b6
b7
Mod. Selec-
tion Bit
0 = not
1 = OFDM
Locked Timing/Carrier Clocks Mandatory
802.11b Service Field
New 802.11 HRb OFDM Service Field
Last Sym
Bytes
Resolve
Bit 4
Reserved
Locked
Clock Bit
0 = not
1 = Locked
Mod. Selec-
tion Bit
0 = CCK
1 = PBCC
Reserved

## Slide 20: Resolve Last-OFDM-Symbol Number-of-Bytes
OFDM Symbol Contains Multiple Data Bytes
Data bytes may not fill last OFDM symbol
Last symbol extended with scrambled zeros
802.11b
Rate Mbps Bytes/Symbol
6.6 3
9.9 4.5
13.2 6
19.8 9
26.4 12
39.6 18
52.8 24
59.4 27
Symbol
Symbol
Symbol
Symbol
Last Symbol
3.64 usecs
3.64 usecs
3.64 usecs
3.64 usecs
3.64 usecs
Signal
Extension
How Many
Information Bytes?
5 bits Needed to
Resolve 0 thru 27
Bytes in Last Symbol
for 59.4 Mbps

## Slide 21: Is Some Type of OFDM SYNC Desirable?
HEADER
48 BITS
@ 2 Mbps
PREAMBLE
72 BITS
@ 1 Mbps
HEADER
48 BITS
@ 1 Mbps
PREAMBLE
144 BITS
@ 1 Mbps
802.11 HRb LONG PREAMBLE
802.11 HRb SHORT PREAMBLE
96 usecs
192 usecs
Data Payload
OFDM
SYNC ?
OFDM
SYNC ?
? usecs
? usecs
PSDU SELECTABLE
OFDM Symbols
@ 6.6, 9.6, 13.2, 19.8, 26.4, 39.3, 52.8 or 59.4 Mbps
PSDU SELECTABLE
OFDM Symbols
@ 6.6, 9.6, 13.2, 19.8, 26.4, 39.3, 52.8 or 59.4 Mbps
Fine Tune Demod

## Slide 22: Function of 802.11a OFDM SYNC
PSDU
SELECTABLE
@ 6, 9, 12, 18, 24, 36, 48 or 54 Mbps
SIGNAL
SYMBOL
OFDM
SYNC
16 usecs
4 usecs
802.11a Packet Structure
8 usecs
8 usecs
Short
SYNC
Long
SYNC
Data Rate
# bytes of data
Data Payload
Signal Detect
AGC
Coarse Frequency
Timing Sync (FFT alignment)
Fine Frequency
Channel Estimation

## Slide 23: Is a SSYNC Desirable for Barker-to-OFDM Transition?
What is SSYNC used for in 802.11a?
AGC pull-in, etc
Coarse frequency estimate
Signal Detect
Time synchronization (FFT alignment)
Not Necessary
for HRb OFDM
Long/Short
Preambles

## Slide 24: Is a SSYNC Desirable for Barker-to-OFDM Transition?
Pulse
Shaping
Filter
Multipath
Channel
802.11b
Long/Short
Pream/HDR
HRb
OFDM
Symbols
0 freq
TX
Spectrum
0 freq
TX
Spectrum
Diversity loss for OFDM
Pulse shape for preamble?
CIR
Estimator
Guard
Interval
Align
T

Timing Align
Barker-to-OFDM
Transition
Barker CIR
time
time
OFDM CIR

## Slide 25: Is an SSYNC Desirable for Barker-to-OFDM Transition? . . . . YES
Propose using SSYNC
Enables different pulse-shaping options in transmitter. (Performance enhancement)
Allows independent guard interval alignment (Performance enhancement)
Only 4 usecs needed (5 short syncs) for sufficient SNR.

## Slide 26: Comparing 802.11a SSYNC to Long/Short Preamble HRb SSYNC
8 usecs
802.11a SSYNC
1
2
3
4
5
6
7
8
9
10
4 usecs
802.11 HRb Long/Short Preamble SSYNC
1
2
3
4
5

## Slide 27: Is an LSYNC Desirable for Barker-to-OFDM Transition?
What is LSYNC used for in 802.11a?
Fine frequency estimate
FEQ design (CIR estimate)
Not Necessary
for HRb OFDM
Long/Short
Preambles

## Slide 28: Channel Estimation: Comparing 802.11b’s and 802.11a’s Spectrum
Pulse
Shaping
Filter
Multipath
Channel
802.11b
TX
Signal
CIR
Estimator
Multipath
Channel
802.11a
TX
Signal
CIR
Estimator
0 freq
0 freq
Guard
Interval
Align
Affects Sub-carrier
Phase
TX
Spectrum
TX
Spectrum
Root Nyquist Like
Flat
802.11b
802.11a

## Slide 29: HRb Channel Estimation: OPTION with Barker/OFDM CIR Discontinuity
Pulse
Shaping
Filter
Multipath
Channel
802.11b
Long/Short
Pream/HDR
HRb
OFDM
Symbols
0 freq
TX
Spectrum
0 freq
TX
Spectrum
Diversity loss for OFDM
Pulse shape for preamble?
CIR
Estimator
Guard
Interval
Align
Affects Sub-carrier
Phase
This option requires a
separate channel estimate
for OFDM

## Slide 30: Is an LSYNC Desirable for Barker-to-OFDM Transition? . . . . YES
Propose using LSYNC
Enables different pulse-shaping options in transmitter. (Performance enhancement)
Provides freedom from maintaining strict gain/phase continuity in transmitter. (Simplification)
Frees receiver from maintaining strict gain/phase continuity during transition. (Simplification)
Allows reuse of 802.11a channel estimation algorithms. (Reuse)
Avoids total dependence upon channel estimation using Barker codes. (Simplification)
Allows independent guard interval alignment without extra compensation circuit. (Simplification)
8 usecs still needed for SNR enhancement.

## Slide 31: Carrier Offset
Retain +/- 25 PPM transmit or receive accuracy.
Long and short preambles provide plenty of time for carrier recovery before OFDM portion of packet occurs.
Essentially no performance loss.

## Slide 32: Timing Offset
Intersil proposes mandatory use of locked oscillators for all 802.11 HRb radios.
Timing offset then becomes a trivial tracking of the carrier offset.
Either polyphase filtering or FFT time-stepping can be used.
Essentially no performance loss.

## Slide 33: Antenna Diversity
The 802.11b preambles are sufficiently long to support antenna diversity with low-complexity AGC’s.

## Slide 34: Summary of Proposed Packet Structure Reusing 802.11b Long/Short Preambles
PREAM/HDR
72 BITS
@ 1 Mbps
PREAMBLE/HEADER
802.11 HRb LONG PREAMBLE
802.11 HRb SHORT PREAMBLE
96 usecs
192 usecs
Data Payload
10.9 usecs
PSDU SELECTABLE
OFDM Symbols
@ 6.6, 9.6, 13.2, 19.8, 26.4, 39.3, 52.8 or 59.4 Mbps
PSDU SELECTABLE
OFDM Symbols
@ 6.6, 9.6, 13.2, 19.8, 26.4, 39.3, 52.8 or 59.4 Mbps
OFDM
SYNC
OFDM
SYNC
10.9 usecs
~6 usecs
Signal
Extension
~6 usecs
Signal
Extension

## Slide 35: Throughput Impact (100 byte packet)
802.11b
Long
Preamble
802.11b
Short
Preamble
802.11 HRb
Short
Preamble
802.11 HRb
Long
Preamble

## Slide 36: Throughput Impact (1000 byte packet)
802.11b
Long
Preamble
802.11b
Short
Preamble
802.11 HRb
Short
Preamble
802.11 HRb
Long
Preamble