## Slide 1: Channelization for HRb OFDM
Mark Webster
Intersil Corporation

## Slide 2: HRb OFDM Channelization
In the USA, the channel spacing typically used is 25 MHz.
Here, the 2.4 GHz ISM band accommodates 3 channels.
802.11 DSSS and 802.11b have the same transmit spectral mask.
INTERSIL recommends the equivalent 802.11a mask for use with HRb OFDM with 25 MHz channel spacing.
The OFDM mask is less stringent.
What is the impact on (existing) 802.11b networks?
This question is analyzed by this submission.

## Slide 3: Recommended HRb OFDM 2.4 GHz ISM Band Channel Stack
25 MHz
25 MHz
freq
Same as 802.11b

## Slide 4: Co-Channel Interference
Performance roughly the same as 802.11b.
Packet-error-rate behavior is characterized using SNR curves for AWGN channel, where SNR becomes SIR.
See the AWGN SNR curves. Not repeated here.

## Slide 5: 802.11b Spectral Mask and PA Back-off
802.11 DSSS Barker
802.11b
mask
PA: Rapp Model
p = 2
Must Back-off PA 3.7 dB
from full saturation to
meet spectral mask.

## Slide 6: Recommended HRb OFDM Mask: Overbounds Worst-Case Spectrum
backoff=16.0dB
backoff=3.7dB
backoff=4.7dB
backoff=8.2dB
backoff=12.0dB
PA Backoff
from Full
Saturation
Equivalent
802.11a
Mask

## Slide 7: Key Question
Since the recommended HRb OFDM spectral mask differs from 802.11b’s spectral mask, what is the adjacent-channel-interference impact on existing 802.11b systems?

## Slide 8: How Does Adjacent Channel Interference Occur?
Cell layout for
3 frequency reuse.

## Slide 9: How Does Adjacent Channel Interference Occur?
INTERFERENCE LEVEL DEPENDS UPON
Separation distance.
Transmit power.
Transmit spectrum.
Receive filtering.
STA1 and STA2 are on adjacent channels.
STA1 is transmitting.

## Slide 10: KEY CONCEPT: OFDM Spectrum is Data-Rate Dependent
Approximate 0.5 dB
Implementation Loss
for 1000 byte 10% PER in
AWGN vs. PA Back-off
Bit Rate PA BO
6.6 Mbps 3.7 dB
13.2 3.7
26.4 4.7
59.4 8.3
Hence, adjacent channel
interference level is OFDM
data-rate dependent

## Slide 11: 802.11b Spectrum vs. HRb OFDM Spectrum at 3.7 dB PA Back-off
802.11 DSSS Barker
HRb OFDM
802.11b mask
QUESTION:
How does the adjacent channel interference compare?

## Slide 12: Simulation Description: Tx Baseband Processor to Rx Baseband Processor
TX
BBP
SAW
PA
SAW
RX
BBP
FREQ
SHIFT
25 MHz
Typical
Saw
Filter

## Slide 13: 802.11 TX Signal Characterization: Using DSSS Barker with 3.7 dB BO
TX
BBP
SAW
PA
SAW
RX
BBP
FREQ
SHIFT
25 MHz
CASE 1

## Slide 14: 802.11 Adjacent Channel Rejection: Measured with 3.7 dB BO
34.3 dB Adjacent Channel Rejection
TX
BBP
SAW
PA
SAW
RX
BBP
FREQ
SHIFT
25 MHz
CASE 1

## Slide 15: 802.11 HRb TX Signal Characterization: Using OFDM with 3.7 dB BO
TX
BBP
SAW
PA
SAW
RX
BBP
FREQ
SHIFT
25 MHz
CASE 2

## Slide 16: 802.11 Adjacent Channel Rejection: Empirically Measured with 3.7 dB BO
TX
BBP
SAW
PA
SAW
RX
BBP
FREQ
SHIFT
25 MHz
26.1 dB Adjacent Channel Rejection: Worst Case
CASE 2

## Slide 17: HRb OFDM Adjacent Channel Performance vs. 802.11b Signal’s Adj. Channel Perform.
BA BO Adj Chan Rej
3.7 dB 26.1 dB
4.7 29
6.4 33.1
8.2 38.4
10.1 43.3
12 46.6
Typical Operational Zone: 13.2 26.4 39.3 59.4 Mbps
802.11b
Adj. Chan.
802.11b
PA BO
Note:
Can trade range for
adjacent channel
rejection performance.

## Slide 18: Conclusions
At equivalent data rates to 802.11b with same PA backoff, HRb OFDM creates 8 dB worse adjacent channel interference.
At higher data rates, HRb OFDM creates no-worse adjacent channel interference than 802.11b.
802.11 HRb adjacent channel interference performance is better than 802.11a’s and HIPERLAN 2’s
OFDM is a viable candidate for HRb