## Slide 1: Implementation and Complexity Issues for OFDM
Steve Halford
Paul Chiuchiolo
Glenn Dooley
Mark Webster
Intersil Corporation
Palm Bay, FL

## Slide 2: Outline of Proposal Presentations
TGg Regulatory Approval Plan Speaker: Jim Zyren
Overview of OFDM for High Rate Speaker: Steve Halford
Reuse of 802.11b Preambles with OFDM Speaker: Mark Webster
Ultra-short Preamble with HRb OFDM Speaker: Mark Webster
OFDM System Performance Speaker: Steve Halford
Power Am Effects for HRb OFDM Speaker: Mark Webster
Channelization for HRb OFDM Speaker: Mark Webster
Phase Noise Sensitivity for HRb OFDM Speaker: Jim Zyren
Implementation and Complexity Issues for OFDM Speaker: Steve Halford
Why OFDM for the High Rate 802.11b Extension? Speaker: Jim Zyren

## Slide 3: Outline of Implementation Presentation
9.1 Main Issue for Complexity: Equalization
9.2 Baseband Complexity
9.3 Power Consumption
9.4 RF/IF Complexity
9.5 Time to Market

## Slide 4: 9.1 Main Issue for Complexity: Equalization
Main issue is complexity of Equalizer vs. FFT
“One of the main reasons to use OFDM is its ability to deal with large delay spreads with a reasonable implementation complexity. In a single-carrier system, the implementation complexity is dominated by equalization, which is necessary when the delay spread is larger than about 10% of the symbol duration. OFDM does not require an equalizer. Instead, the complexity of an OFDM system is largely determined by the FFT, which is used to demodulate the various subcarriers.”
Quote from pg. 48 of R. Van Nee & R. Prasad, OFDM for Wireless Multimedia Communications, Artech House Publishers, Boston, MA, 2000.

## Slide 5: 9.1.1 Equalizer and FFT Complexity
** Based on R. Van Nee & R. Prasad, OFDM for Wireless Multimedia Communications, Artech House Publishers, Boston, MA, 2000.
64 point FFT using radix-4 requires 96 complex multiplies
Equalizer then requires 48 complex multiplies
  Could simplify since all that is really needed is a phase rotation & soft-decision scale
Perform once every 80*(1/22 x 106) = 3.63 x 10 -6 seconds
Equivalent to (4 x 144)/(3.63 x 10 -6 ) = 158.4 x 106 real multiplies per second
Linear Equalizer of length L requires 4*L complex multiplies per symbol
Number of real multiplies = (4*L*11 x 106 ) = L * (44 x 106 )
Length L must be less than (158.4/44) = 3.6 to match complexity of FFT
Using pulse shaping makes this worse due to matched filter!
Doesn’t include the complexity of estimating the equalizer types
  Matrix inverse proportional to L
Alternative is a full Viterbi Equalizer with channel matched filter
Single Carrier Linear Equalizer Complexity
FFT for OFDM Equalization

## Slide 6: 9.2 Baseband Complexity Summary

## Slide 7: 9.2 Relative Complexity Estimate
NOTE 1. Estimates for the Basic CCK Demodulator & Basic CCK Demodulator with Equalizer are based on Intersil Baseband processors 3860B and 3863
Complexity (gate count) relative to a Basic CCK Demodulator

## Slide 8: 9.3 Power Consumption for OFDM
Assumptions & Notes about Power Estimates
0.35 m current estimates based on Intersil 3863 baseband processor
0.18 m current estimates based on 40% reduction from 0.35 m for digital functions
CCK functions can be powered down during OFDM operation
60% of current during transmit & 30% of current during receive is in analog
  This will not change for OFDM
  This will not change at 0.18 m
Does not include power for MAC functions
Power Estimates for Baseband Processor with CCK & OFDM

## Slide 9: 9.4 RF/IF Design Issues for OFDM
OFDM has different spectrum than CCK
Higher order modulations (e.g., 64-QAM) will require “cleaner” RF front end
Can we re-use current 802.11b RF front-ends?
Yes!
Detailed Simulations of Intersil’s Prism II indicate that 26.4 Mbps & 39.6 Mbps operate within 802.11a requirements for both transmitter & receiver performance

## Slide 10: 9.5 Time to Market Issues
OFDM is well established as a viable waveform for W-LAN applications
  Mature technology
  Proven to be practical for ASIC implementation
  RF technology exists to support at 2.4 GHz
Standards process can be accelerated by adopting large portions of existing 802.11a standard
FCC issue will drive the time to market