## Slide 1: Why OFDM for the High Rate 802.11b Extension?
Jim Zyren, Intersil
Notes: <number>
<footer>
<header>
<date/time>
This Style Guide is designed to facilitate the creation of presentations within Intersil graphic guidelines. These presentations may address an external audience, as in a product announcement or industry event, or an internal one, as in seminars or executive committee meetings. In any case, it is important to adhere to a corporate Style Guide. The Style Guide provides standards and guidelines to help project Intersil’s corporate identity. Projecting visual continuity is a key to the success of the company.
The Style Guide is based on the capabilities of Microsoft PowerPoint, one of our corporate standard software packages. The following slides and script describe the graphic standards and guidelines for these presentations.
This Style Guide will address four key areas:
  The overall Layout and Design
  Specifications for placement of text, logo, and graphic treatments (symbols, bar charts and table charts)
  Recommended Guidelines for using photography and illustration
  Recommended Color usage and standard palette

## Slide 2: Why OFDM in the 2.4 GHz Band?
Performance
  OFDM is a powerful and proven method
    OFDM independently selected by 802.11a and HiperLAN2
  OFDM provides excellent performance in multipath and AWGN
    interleaving and error coding result in extremely robust systems
  Single carrier systems do not scale well for very high rates
    Equalizer complexity fatally flawed HiperLAN1
    Why repeat this mistake?

## Slide 3: Why OFDM in the 2.4 GHz Band?
Data Rates
  Consumer demand for bandwidth is insatiable
    22 Mbps is better, but it is insufficient for many applications?
    5 GHz development is raising market expectations
  OFDM can scale data rates to >54 Mbps
    enough bandwidth to remain competitive
    enough to serve multimedia applications
  Do we want to go through standards process again in two years?
    What happens when consumers demand >20 Mbps?
    In a few years, consumers will demand 54 Mbps, they don’t care about the frequency of operation

## Slide 4: Why OFDM in the 2.4 GHz Band?
Upgrade Path
  OFDM is already used at 5 GHz
    IEEE 802.11a and HiperLAN2
  Selection of OFDM for 2.4 GHz band provides upgrade path to 5 GHz
  Dual Band radios become possible!
    2.4 GHz infrastructure does not become stranded
    2.4 GHz band remains competitive in terms of data rates
    One radio can work regardless of infrastructure!
  Good for customers, good for suppliers.

## Slide 5: FCC Issues
  All systems with >20 Mbps in current channel width have regulatory approval issues
    FCC public statements clearly indicate that spectral efficiency is a major issue
  FCC is publicly considering revision of 15.247
    Industry forum to be held in Jan-Feb timeframe
    FCC has requested input from IEEE 802.11/.15/.16 regarding issues to be placed on forum agenda
    FCC wants to work with industry to make ALL proposed high rate waveforms legal
    RAHG has drafted FCC response to be considered at 802.11 plenary tomorrow
  OFDM on same regulatory footing as other proposals

## Slide 6: Marketing Issues
What if we DON’T pick OFDM?
  Somebody else will…
    The technology is available
    Data rates are higher
    Performance in multipath and AWGN is outstanding
  But, who?
    HomeRF, proprietary solutions, etc.
    Many companies are developing OFDM capability
  IEEE 802.11 will not be a leader in 2.4 GHz band
    market won’t care about 22 Mbps if 54 Mbps is available from other sources
  Why concede the 2.4 GHz band to non-802.11 solutions?

## Slide 7: Marketing Issues
Some long-term thinking…
  in five years, consumers will be demanding higher data rates
  how long do we think 22 Mbps will be competitive?
    or, do we want to do this again next year?
If we pick OFDM …
  2.4 GHz band remains viable
  IEEE 802.11 does not “open the door” to competitors
  Dual Band radios will extend the life of 2.4 GHz infrastructure.

## Slide 8: Conclusions
We will not get a high rate (>20 Mbps) solution approved in the 2.4 GHz band without a rule change
OFDM is the right choice right NOW
  Standard can be in place when FCC gives green light
OFDM is the right choice for the future
  higher data rates
  great multipath and AWGN performance
  upgrade path to 5 GHz band