## Slide 1: Baseline D-QoS Proposal Greg Chesson- Atheros Wim Diepstraten- Lucent Technologies WCND Duncan Kitchin- Intel Harold Teunissen- Lucent Technologies Menzo Wentink- Intersil/NWN Prepared by: Wim Diepstraten

## Slide 2: QoS Requirements
The reigning network paradigm is IP - not ATM or circuit switching
IP performance is inherently variable
Multi-media applications for IP based networks include - or will include - pacing mechanisms to adapt to available capacity
  e.g. the new MPEG4 standard allows continuous adaptation of the encoder to available capacity
Distributed QoS is aiming to take advantage of these developments and focus on:
  maintaining [reasonable] performance in the presence of interference
  maintaining delivery rates rather than tight delay constraints per packet
  accommodate rate adaptation
Notes: Page <number>
        <footer>
<header>
<date/time>
- Take advantage of IP protocol capacity to work over a variable and congested network.

## Slide 3: Assumptions
The Enhanced DCF proposal is part of a total QoS proposal which is layered as follows:
  QoS Level 0: No QoS using DCF & PCF as in 802.11 1999
  QoS Level 1: Priority based QoS delivery using enhanced DCF
  QoS Level 2: Priority based QoS delivery using enhanced DCF & PCF
  QoS Level 3: Parameterized QoS delivery using enhanced DCF & PCF
Each successive level does support the full functionality of the level below.
Use priority based interface supporting 8 Priority classes according to 802.1d Annex H.2.
Notes: Page <number>
        <footer>
<header>
<date/time>
Use the same MAC interface for both DCF and PCF.

## Slide 4: D-QoS objective
Objective is to use a low complexity approach.
Provide priority driven service differentiation between a number of different traffic priority classes.
Provide mechanisms to limit the medium load in order to keep the delay of higher priority classes under control.
  While avoiding starvation of low priority classes.
The mechanism should be adaptive such that priority class differentiation mechanisms are only active when there is active traffic load in higher priority classes.
  If there is only “Best Effort” traffic load, then the throughput performance should be similar to the legacy throughput.
Should be able to provide priority differentiation also in the presence of legacy DCF devices, although effectiveness can be reduced.
Can be applied in both ESS and IBSS.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 5: Approach
Up to 8 priority categories are distinguished, each having a separate Q.
  Mapping to a limited subset of about 4 may be more practical.
Objective is to control the total medium load such that the delay of high priority classes are acceptable.
  There are no absolute limits, only relative.
By using the medium load feedback to control the distinction between service classes.
  By reducing the service rate of lower classes to assure better service of higher priority classes when load increases.
  If this load feedback is indicating the load per priority class on the medium, then the differentiation model can be adaptive to scale up the lower priorities, when no traffic is present for any of the higher priority classes.
    So that performance of “Best Effort” only traffic remains as is.
The same distinction in service within a station should work across the whole BSS.
Notes: Page <number>
        <footer>
<header>
<date/time>
- Subset of 4 enough?
- Rest of priroity classes can be aggregated on here?
- Possibly control other options with this like No-Ack, or “Reduced retry limit”
Comment:
- # priority classes = 8
- # access priorities need to be the same for all stations.
- # Q’s can still be different

## Slide 6: Basic model for example
Medium Access Control
Multi-media Traffic Source
System
Interactive
Stream
Best Effort
Drop Rate Control
Service Rate Control
System & Ntwrk Mant
Notes: Page <number>
        <footer>
<header>
<date/time>
System & Network Management highest? What do we mean by that?
Are those our own management frames?
Not only should this work between traffic classes within the station, but across the BSS.

## Slide 7: Model discussion
A limited number of Access Priority Q’s are defined, and 4 is considered a good limit.
  Standard will need to define min number of Q’s (3-4)
Two basic functions are provided:
  “Service Rate Control” mechanism that is to assure service differentiation between priority classes by using different access priorities.
    A Scheduling mechanism is to determine which priority category is going to use the next Transmit Opportunity, that is provided by the Access Control mechanism.
  A “Drop Rate Control” mechanism that is to regulate the “Offered Load” based on medium capacity limits.
    This is NOT considered a subject for standardization.
    Objective is to utilize the congestion control mechanisms in higher layers to control the “offered load”.
Apart from this there can be a “Submission Control” function above the MAC.

## Slide 8: Basic D-QoS concepts
A “Medium monitor” function does measure the “Load per Class” in terms of medium occupancy duration, over a period, of for instance a Beacon interval.
The “Medium monitor” function does translate the “Load per Class” into a set of COx,CWx parameters, which should be the same for all stations.
  The COx,CWx parameters are distributed in a ”Contention Control” element in every Beacon.
  How this translation takes place is assumed NOT to be standardized.
A “Virtual-DCF” (V-DCF) mechanism is used for each priority class within a station, each using a separate CWmin (CWx, a per class parameter), and a CO (Contention Offset) parameter.
  So in our example there are up to 4 DCF contenders within each station.
  The “V-DCF” mechanism does generate a separate backoff count per “Access Priority” level.
  Which individually decrement when the medium is not busy.
    A transmission starts when one of the counters decrements to zero.
  A collision between local accesses are resolved locally.
    The higher priority frame will be send first, while the lower priority it collided with should act as if it is to defer on a Tx-Opp, so would do an other backoff.
Notes: Page <number>
        <footer>
<header>
<date/time>
Skipping TxOpps affects the probability. No longer flat distribution of random numbers.

## Slide 9: ESS / IBSS
In ESS the “Monitor Function” is done in the AP.
  The translation from “Load per Priority” to the COx,CWx value per class, is NOT specified in the standard, and can be policy based.
    The Policy management only needs to be done in the AP, and applies identically in the whole BSS.
    So that the whole BSS uses the same COx,CWx values.
  A list of CWx parameters are distributed to each station in the Beacon.
There can still be a “Monitor function” active in a station, which can further tune the COx,CWx parameters to the locally monitored situation.
    The AP supplied parameters are considered the default.
    But only unidirectional CW changes (getting larger) are allowed from the AP supplied CWx values.
In an IBSS a default COx/CWx map is assumed, but a COx/CWx distribution by a “Load Monitor” function in any of stations will override the default.
  In IBSS a ‘Load Monitor” function is not mandatory, but if available will be used.

## Slide 10: General Framework
802,1q D-SAP,
3-bit traffic class
MPDU Scheduler
Number of Q’s depends on QoS level
Channel access function independent of scheduler
D-SAP
M-SAP
Scheduler
Access
Multiple Q’s mean:
That we need a Schedule
entity to select the next
transmit candidate
For the next transmit
opportunity as determined
by the access mechanism.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 11: V-DCF mechanism
Access differentiation controlled by a Contention Window (CWx) and a Contention Offset (COx) parameter per priority category x.
  Multiple DCF’s running in parallel, with conceptually an individual Backoff counter for Backoff and Post-Backoff.
    Formula for Backoff = COx+RND(CWx) (for legacy CO=0, and CW=31)
    Implementations based on a single Delta-Backoff counter are possible.
  The scheduling function is based on random number generated per access priority level, using individual COx/CWx parameters causing differentiation in access ratio
  At a local collision the highest priority frame is being transmitted, while the other DCF is deferring and generate a new Backoff.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 12: Contention Offset
Contention Offset allows more differentiation control
  with more predictable differentiation independent of the number of contenders.
  With better delay characteristics, because chance that lower priority will precede a higher priority packet is reduced.
    Can still be possible that a low priority frame already in backoff due to a previous contention can precede a new high priority frame.
Contention Window (CW) parameter can be chosen as function of the number of stations that are contending for medium access.
A Contention Offset (CO) parameter can be used to assure that different priority categories do get a distinct advantage over the others to get access to the medium.

## Slide 13: V-DCF example
AP can change the parameters when load increases, to reduce service for lower priorities, to keep the delay for high priority traffic within bounds.
  It also has knowledge of the number of contenders per priority category.
If no load is monitored by the AP, then the relative priority of lower categories will improve.
  So if only “Best Effort” traffic is present then performance is equal to legacy today.
Example:Low load All classes active High Load
  C3: CO3=0, CW3=15 Voice, short frames no backlog low load CO3=0, CW3=15
  C2: CO2= 8, CW2=15 Interactive, bursty, few stations medium load CO2=16, CW2=15
  C1: CO1=16, CW1=15 Streaming, bursty, few stations, high load CO1=24, CW1=15
  C0: CO0=32, CW0=31 Best Effort, bursty, more stations CO0=40, CW0=63
Example:Low load Only C3 and C0 active High Load
  C3: CO3=0, CW3=15 Voice, short frames no backlog low load CO3= 0, CW3=15
  C2: CO2= 8, CW2=15 Interactive, bursty, few stations medium load CO2= 8, CW2=15
  C1: CO1= 8, CW1=15 Streaming, bursty, few stations, high load CO1= 8, CW1=15
  C0: CO0= 8, CW0=31 Best Effort, bursty,more stations CO0=16, CW0=31
Example:Low load Only C1 and C0 active High Load
  C3: CO3= 0, CW3= 8 Voice, short frames no backlog low load CO3= 0, CW3= 8
  C2: CO2= 0, CW2= 8 Interactive, bursty, few stations medium load CO2= 0, CW2= 8
  C1: CO1= 0, CW1=15 Streaming, bursty, few stations, high load CO1= 0, CW1=15
  C0: CO0=16, CW0=31 Best Effort, bursty,more stations CO0=32, CW0=63

## Slide 14: V-DCF retry mechanism
Functional Goal:
  Exhaustive Retry is to be prevented, when there is higher priority traffic Q’d up.
  Objective of the retry mechanism is to temporarily reduce the load of the station on the medium for stability reasons.
    To improve the probability of contention resolution success under high load conditions.
    And to circumvent possible hidden interferers causing the failure.
vDCF mechanism:
  Therefore the whole station (all vDCF’s) need to back off, and not only the vDCF that experience a failure.
    So all DCF’s need to double their CW’s and generate a new backoff
    Preferred CO behavior to be determined.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 15: Legacy Device Handling
Legacy devices are assumed to use the CWmin=31 and contend with the priority traffic in a way that breaks the differentiation model.
  For those priority levels that do not use a lower then 31 CWmin.
However all traffic from legacy devices will go through the AP.
So an “Enhanced DCF” AP does put the down traffic in the lowest priority Q.
  Management frame responses could be an exception.
In most higher layer protocol environments this will automatically reduce the traffic in the up direction.
  AP’s could implement an even lower priority Q for its legacy traffic, so that it bandwidth is extra reduced to balance this further.
If we assume that the number of stations that generate high priority traffic is very limited, then a lower CWmin then 31 can be used, which improves the relative priority compared to legacy traffic.

## Slide 16: Burst mechanims
In order to improve the efficiency of the AP, the AP should be allowed to concatenate multiple frames in one Tx-Access Opportunity.
  A (MIB?) limited burst of frames are allowed per access opportunity with SIFS in between.
  This can be done in a similar way as specified for fragmentation.
    With the “Duration” field containing the proper values for the next exchange.
    So Ack contains the duration of the next data frame, and its associated Ack.
Also a station can be allowed to send a burst, but limited to a max size (2304 Byte) duration equivalent size.
  We probably need to limit this functionality only to a 2304 Byte duration equivalent for the highest Basic rate only.
    To prevent excessive jitter.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 17: Burst Control
A Tx-Opp limit mechanism can be used to reduce excessive medium occupancy situations, while allowing rate fallback.
  In both AP and Stations which could be different.
  The Tx-Opportunity Limit is a certain medium occupancy time limit per channel access.
    Dimensioned to define the Burst duration which could range to a number of max size frames when transmitted at the highest basic rate.
  If stations want to do rate fallback to for instance 1 Mbps for robustness, then that means that the station is forced to use fragmentation.
    But contend for the medium between each fragment.

## Slide 18: Framework
802.11 D-SAP
  with 3 bit Traffic Class.
Number of Q’s depends on QoS level.
MPDU scheduler
Channel Access function
  One or more, depending on Level.
D-SAP
M-SAP
Scheduler
Access
Select Transmit candidate
Generate Tx-Opportunities
either by Access Control (L1&L2)
or by PCF Poll (L2)
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 19: Basic frame work approach
Basic framework should conceptual work for both level 1 and level 2 station mechanism.
  During CFP the random number generation aspect of vDCF can be the schedule mechanism.
    While the PCF determines the Tx-Op
  During the CP the vDCF scheduling and access mechanism is active.
    Where the parallel DCF backoff mechanism is generating the Tx-Ops.
The State Machines are setup to allow the use of the same scheduler mechanism for both Level-1 and Level-2 operation.
  While the same differentiation control from the AP can be used also during level 2 operation during the CFP.
  But its use is not mandatory. Each implementer can chose its own scheduler while in Level 2.
The State Machines are described such that the behavior is becoming identical to the Legacy DCF when the number of Q’s is reduced to 1.
  Assuming CO=0 and CW=31
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 20: vDCF State Machine approach
Same Scheduler could be used for both Level 1 and Level 2
  Generating a “Scheduler Backoff” (SBOx) per Q entry
  The scheduler identifies the Tx candidate by choosing min(SBO[ ]).
    And adjusts SBO[ ]=SBO[ ]-min(SBO[ ])
  And a next “Delta-BO” BO= min(SBO[ ]) is calculated for use in a single Access Control Engine.
The Access Control engine is maintaining a single Backoff counter (BO)
  which is invoked unless CCA>=DIFS (CCA active longer then DIFS time), and decremented on Slot Events when CCA>=DIFS.
Individual Post Backoff SM’s (PBO counter only) per priority category.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 21: State Machines

## Slide 22: Scheduler
Scheduler with “Idle” and “Tx-Pending” states.
Action description:
  1: New arrival of a frame in a Q.
    Since Y is the first frame it is the Tx Candidate so generate BO=CO[y] + RND(CW[y]) unless still in Post Backoff, then BO=PBO[y].
    Transit to Tx-Pend(ing) state.
  2: New arrival of a frame in an empty Q, (while an other Tx already pending).
    Generate an SBO[y]=CO[y] + RND(CW[y]) unless still in Post Backoff, then SBO[y]=PBO[y].
    If SBO[y]<BO then this frame has higher priority then the current scheduled frame, so it can still use the next TxOpp. The SBO of the other priority categories need to be adjusted accordingly so SBO[ ]=SBO[ ]+(BO-SBO[y]), and BO=SBO[y].
  3: Succesfull transmission, while more traffic Q’d.
    3a: If more traffic in this Q then generate SBO[y]=CO[y] + RND(CW[y])
    else need to load the PBO[y]=CO[y]+ RND(CW[y]).
    Reset all CW[ ]=Cwmin[ ]
    3b: If More Q’d Then select a new Tx Candidate according to BO=min(SBO[x]).
      And adjust all SBO’s by SBO[ ]=SBO[ ] - min(SBO[ ])
      If lower priority SBO=0 then resolve this local collision by generating new SBO[z]=RND(CW[z])
  4: Transmit Failure
    If Retrycount[y] > limit then Flush frame and proceed with 3b action.
    Inc Retry count, make all CW[ ]=Limit.MaxCW(2*CW[ ]),
    and generate new SBO[ ]=CO[ ] + RND(CW[ ]) for all Q’s and proceed with 3b action.
  5: Transmit Done & no-More traffic Q’d:
    Generate Post Backoff by PBO[y]=CO[y] + RND(CW[y]), and transit to Idle state.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 23: Access Control SM’s
There is one “Access Control” State Machine
  when active is either in “Backoff” or “Tx & Wait” state.
  The interface from the Scheduler will be via the TxPend and BO variables.
There are multiple “Post Backoff” State Machines, one per priority category.
  Communicating with the Scheduler via the PBO[x].
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 24: DCF comparison
Legacy DCF
  1 Tx-Queue
    CW = fixed
  Access Control
    BO (Backoff counter)
    PBO (Post Backoff counter)
Level-1 D-QoS
  N Tx-Queues
  vDCF Scheduler
    CO[ ], CW[ ] from AP
  Access Control
    BO (Backoff counter)
    PBO[ ] (Post Backoff counter)
  Burst / Aggregation?
Level-3 (in CFP)
  N Tx-Queues
  Scheduler
  Access Control
    PCF
  Aggregation
Level-2 (in CFP)
  N Tx-Queues
  Scheduler
    v-DCF: CO[ ], CW[ ] from AP
    or other method
  Access Control
    PCF
  Burst / Aggregation

## Slide 25: Mechanisms needed
Priority in frame header
  a new field compatible with also the PCF approach needs to be defined.
D-QoS Element in the Beacon
  Containing the COx/CWx list per access priority level.
  Which can also provide the “Total Load” info, which can be used for “Load Balancing” purposes.
Rules to use CO/CW and retry change
  See elsewhere in this document.
Sequence# generation and Duplicate detection rule changes.
  To support the non-exhaustive retry approach in a station, it is needed to maintain a sequence# per SA.Class combination.
    So the sequencing rules need to change, such that individual S# is maintained per Class, and will increment.
    And AP’s and Station receivers need to maintain duplicate detection mechanism on a SA.Class basis, and expand its resources for that.
    Capability exchange mechanisms to determine service levels.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 26: EDCF Simulation
Objectives
EDCF Method
Environment
Scenarios
Results
Next Steps

## Slide 27: Objectives
Test CW-based access methods
  MAC algorithm correctness
Demonstrate differentiated service
  Does DQoS exercise real control?
Explore in overload and dynamic states
  How good is it?
  Is it “good enough”?

## Slide 28: Non-Objectives
100% high-fidelity real-life model
  Stimulus system less important than analysis
Overlapping BSS (though possible)
Mobile Stations
  Unused facility is available in the system
Full-function AP
  Needed later

## Slide 29: EDCF Access Method
Normal DCF window
Vary rhs (CW x)
Vary lhs (CO x)
EDCF: Adjust both
[0 ---------------- CW]
[0 ------------- CWx)
(CO x -------------- CW]
(CO x ----------- CWx)

## Slide 30: Environment
Berkeley Network Simulator (NS 2)
Modifications and additions
Tarball for Linux or Solaris: greg@atheros.com
What it does:
  Tcp/ip/udp stacks, various traffic generators
  Single priority stream per node, settable CW/CO
What it does not do at this time:
  Preserve priority when forwarding through AP
  Demonstrate VDCF collision resolution
  Change CW/CO settings dynamically
  Bursting or aggregation

## Slide 31: Scenarios
Model 1: Simple Uniform Traffic
  N nodes (plus AP)
  N tcp/ip streams as infinite sources/sinks
  4 access classes
  Adjust PHY bandwidth, N nodes, MTU size and the MAC parameters
Goal: observe differentiated service

## Slide 32: Scenarios
Model 2: phones plus streams
  4 “phones”: 120 Byte samples @ 10ms periods
    Pessimistic IP-phone
  Plus, 8 tcp/ip connections
    Infinite bandwidth sources/sinks, 1500Byte MTU
  Phones are given highest access class
  Tcp streams are assigned to lower classes
Goal: observe latency and diffserv

## Slide 33: Model 1 Examples
CWx only (CO is 0), bw, latency
CO only (CW is 31): bw, latency
Vary both CW and CO: bw, latency
Latency is measured from source enqueue to
Successful reception at destination MAC.

## Slide 34: Model 1 bw (CW)
Begin streams on 1 sec intervals
Mbytes/s
Simulation Time (secs)
EDCF Parameters
By priority (0,1,2,3)

## Slide 35: Model 1 lat (CW)
Priority 0
Priority 1
Priority 2
Priority 3
Latency per packet by priority

## Slide 36: Model 1 lat (CW zoom)
.5-1ms
1-2ms
.5-1.5ms
2-4ms

## Slide 37: Model 1 bw (CO)

## Slide 38: Model 1 lat (CO)

## Slide 39: Model 1 bw (CW+CO)

## Slide 40: Model 1 lat (CW+CO)

## Slide 41: Observations
Both CW and CO parameters control access
Differentiated BW and LAT are possible
Wide spread of CW/CO needed to support larger numbers of stations
  802.11a won’t scale well with CWMin of 15

## Slide 42: Model 2 Examples
4 phones, 8 tcp streams, CW only
  Observe bw, lat
CW+CO
  Observer bw, lat
  Closeup of 1 phone

## Slide 43: Model 2 bw (CW)
Tcp streams
phones

## Slide 44: Model 2 lat (CW)
tcp
other tcp’s start
phones

## Slide 45: Model 2 bw (CW+CO)

## Slide 46: Model 2 lat (CW+CO)

## Slide 47: Model 2 lat (CW+CO)

## Slide 48: Observations
CW+CO provides differentiated service in more complex scenario
Low latency for at least one class of service is possible
Unknowns
  Fine grain control (probably not possible)
  Adapt to changing load (possible)
  Exert control in overloaded state (poorly)

## Slide 49: Next Steps
Better scripts and automation
Validate against hardware, traces, Opnet
Simulate internal VDCF
Extend current AP model
  Forward based on access priority
  Dynamic adjustment of CW/CO values
Other scenarios