## Slide 1: A Network Enrollment Protocol
Duncan Kitchin, Intel

## Slide 2: Problem Statement
802.11 requires per-node configuration
  SSID
  encryption keys, mechanisms
This is too complex for many products and/or users
  TVs, VCRs, DVD players (no keyboard…)
  consumers expect these products to work out of the box
Security implications
  the greatest security flaw we could introduce is making the system too difficult to configure correctly

## Slide 3: Proposed Solution – What the User Sees
User sees “press a button at either end” enrollment
  same as used for garage door openers, cordless phones, cordless mice, keyboards
Pressing a button on the AP makes it temporarily “open for enrollment”
Two buttons at station, “scan” and “enroll”
  first “illuminates” APs, cycling through list
  second attempts enrollment in last AP illuminated

## Slide 4: New Packets
Use new generic management type & subtype, with action “enroll”
  subaction “illuminate”
  subaction “enroll request”
  subaction “enroll response”

## Slide 5: Scanning
Station determines available APs by existing active or passive scanning, and maintains a list
Each time the “scan” button is pressed, sends an enroll/illuminate packet to the next AP on the list
An AP receiving an enroll/illuminate packet emits an audible or visual indication

## Slide 6: Enrollment Process
Station and AP create a Diffie-Hellman tunnel
  Station creates DH value, sends to AP
  AP never advertises that it is open, but accepts an enrollment request if it is and responds with its own DH value and encrypted parameters
The tunnel is then used by the AP to send back to the station:
  credentials for future authentication
  other configuration parameters such as SSID

## Slide 7: Packet Formats
See 00/xxx for generic management frame type
enroll/illuminate
  no additional contents
enroll/request
  Diffie-Hellman element
enroll/response
  Diffie-Hellman element
  configuration data, plus encrypted-content security credential elements

## Slide 8: Process Summary
enroll/illuminate
enroll/illuminate
indication
indication
request
enroll/request
enroll/response