## Slide 1: FEC for QoS
Duncan Kitchin, Intel

## Slide 2: FEC for QoS
FEC can be used to improve MAC transfer properties
  improve bandwidth utilization
  eliminating need for retransmissions could permit multicasts

## Slide 3: Issues with FEC in the MAC
How do the upper layers in an IP/802 model communicate their requirements to the MAC?
What happens when the correction capacity is exceeded? Entire packets can frequently be lost
How can we deal with decoding latency?

## Slide 4: Proposed Solution
Use FEC for correction in multicast streams only
  cannot have MAC layer acknowledgements and multicast; natural place for FEC
  upper layers select acknowledgement policy by choice of address
Interleave across packets, and perform whole packet erasure decoding

## Slide 5: Proposed Solution
Check Digits
Treat this packet as an erasure
Interleaved Data

## Slide 6: Summary
Spans multiple packets
Defined at the transport layer, not the MAC
Interleaving can be reduced to span only a few packets, keeping latencies within specified bounds
Much work already done in IETF in defining these protocols (reliable multicast transport group)