## Slide 1: Suggested Approach for 22 Mbps 802.11b Implementation
Niels Van Erven
3Com Corporation
November 2000

## Slide 2: Overview
Recommends an approach to 802.11b using
QPSK @ 11Msps
Technical Summary
Benefits
Issues
Summary

## Slide 3: Technical Summary
QPSK
No special coding
11 Msps (22 Mbps theoretical)
Backward-compatibility with existing 802.11b
Interoperable with 802.11b
  Use common preambles
Logical extension to the current market

## Slide 4: Technical Summary (2)
Minimal MAC changes
  Minor state machine changes
  Some critical firmware timing issues
  Increased processing speed
Same interference characteristics as
encountered in 802.11b products
Typical QPSK characteristics
  Spectral
  Adjacent channel interference
  Co-channel interference
  RF PA backoff from 1dB
  compression point

## Slide 5: Technical Summary (3)
Complexity similar to 802.11b
  Increased processing speed
  No increased gate count
    Elimination / bypassing of correlators
  Equivalent RF/IF PHY complexity
  Simplified equalizer possible due to
  decreased range
Throughput almost double 802.11b
  slightly less in order to accommodate
  interoperability issues (preambles, etc)

## Slide 6: Benefits
Minimal regulatory impact
  Best coexistence strategy
Fastest time-to-market
  Mature technology
  Allows industry to leverage existing
  research and investment
Builds on existing customer confidence
  Minimizes market confusion while
  providing differentiation
  Will not be an anticipatory drag on the
  802.11b market

## Slide 7: Issues
Reduced range
  Common problem for all approaches
  Sufficient for home use
  Increased deployment of access points in
  business environments
  Potential for less interference when widely
  deployed
Increased processing power
  Common problem for all approaches
Streaming video will introduce higher
utilization rates - interference

## Slide 8: Summary
Best compromise for technology, regulatory,
industry and customer needs
Minimal regulatory impact
Best coexistence strategy with all 2.4GHz users
Fastest time-to-market
  Meets burgeoning customer need for speed
Mature technology
Level playing field for industry participants
Lowest risk/investment for best return