## Slide 1: Backward Compatibility of ‘Tiered Contention’ Multiple Access (TCMA)
Mathilde Benveniste
AT&T Labs, Research

## Slide 2: Backoff countdown procedure
Time
Node C
Node B
Node A
transmission
BCUT
BCPT
For legacy stations:
  BCPT=DIFS
  BCUT=slot time
Example
All nodes are legacy stations with backoff counters m at equal to:
  m(A)=3; m(B)=2; m(C)=1
End of last
transmission
BCPT = backoff counter preparation time
BCUT = backoff counter update time

## Slide 3: Urgency Arbitration Time (UAT) Differentiation by BCPT Contention resolution through backoff
TCMA Protocol Backbone
Each urgency class is assigned a different urgency arbitration time (UAT) whose length decreases with increasing urgency.
Arbitration Time = interval that the channel must be sensed idle by a node before decreasing its backoff counter.
In congestion:
  Higher urgency packets dominate the channel, as lower urgency packets get less of a chance to transmit - decrease their backoff counters.
  Lower urgency packets do not collide with higher urgency packets.
For stations with classification i= 0,1,...
Time
Node C
Node B
Node A
transmission
BCUT
BCPT
End of last
transmission
Example
The backoff counter m at is equal to 1 for all nodes; m(A)= m(B)=m(C)=1
Transmit urgency ranking: (C, B, A); hence,
UAT(A) >UAT(B)>UAT(C)

## Slide 4: Urgency Arbitration Time (UAT) Differentiation by BCPT Contention resolution through use of persistence probability
Time
Node C
Node B
Node A
transmission
BCUT
BCPT
End of last
transmission
Example
Every node got a ‘success’ when checking for permission to transmit after the first idle slot time
Transmit urgency ranking: (C, B, A); hence,
UAT(A) >UAT(B)>UAT(C)
TCMA Protocol Backbone
Each urgency class is assigned a different arbitration time (UAT) whose length decreases with increasing urgency.
Arbitration Time = interval that the channel must be sensed idle by a node before checking for permission to transmit.
In congestion:
  Higher urgency packets dominate the channel, as lower urgency packets get less of a chance to transmit - check for permission to transmit.
  Lower urgency packets do not collide with higher urgency packets.
For stations with classification i= 0,1,...

## Slide 5
Additional features
Other QoS-management features:
Assigns urgency class to access buffer packet by various QoS-driven scheduling algorithms that adapt to real-time conditions
Adapts to estimates of (class-specific) local congestion levels, which are obtained by broadcasting the number and age of (class-specific) transmission attempts.
Adjusts starting backoff counter to provide proper dispersion of traffic bursts and reduce contention.
Starts with traffic-adjusted backoff counter distribution, which may be made more persistent upon re-transmission to reduce contention and delay.
Use collision avoidance through backoff with similar benefits.
Cancels transmission retrials based on delay-related criteria that discriminate between traffic types.

## Slide 6: Requirements for backward Compatibility with IEEE 802.11
With arbitration time differentiation, for stations with classification i= 0,1,...
Backward compatibility with legacy stations requires:
1. for all i
2. ; the arbitration increment (AI) d must enable clear channel assessment.
3. ; the backoff counter update time must enable clear channel assessment.
Arbitration time differentiation thus permits a single class with urgency higher than legacy packets, since DIFS=PIFS+slot.time
In the short term: Use a ‘hybrid’ approach to increase the number of high urgency classes; this employs
  TCMA to generate a high-urgency class with UAT=PIFS; and
  differentiates further by varying the contention resolution parameters
Long-term approach: Changes in the PHY specification would accommodate shorter AI and BCUT times, thus yielding multiple UAT-differentiated classes with higher urgency.

## Slide 7: Hybrid differentiation (arbitration time and backoff distribution)
UAT differentiation generates a top-urgency class -- UAT(0)=PIFS.
Further differentiation is achieved through the probability distribution, from which backoff counters are drawn.*
  A lower mean value is used for higher priority packets.
  A higher variance is used for higher traffic intensity.
    Traffic intensity is determined by remembering the number and age of transmission attempts of packets in different classes by a station; and
    by listening to the same information, contained in the transmissions of other stations.
*v-DCF differentiates between all classes through the use of different backoff p.d.f.s that are uniform.

## Slide 8: Hybrid differentiation (arbitration time and backoff distribution)
Example: Uniform Backoff Distribution for each class.
Three classes are shown, with means and variances
Contiguous, non-overlapping uniform distributions are employed to obtain uniform envelop.
Their boundaries are determined from class-specific traffic estimates
,
where is the local congestion of class i, and is the window size needed for adequate dispersion of the composite congestion
X is determined from C.
The superposition of the probability density functions of the backoff counter distributions yields a uniform density function, thus achieving uniform dispersion of the contending stations’ backoff time.
Probability density function of initial backoff counter for the different class populations using the same UAT time.
L1
L2/U1
L3/U2
U3
class 1
class 2
class 3
x1
x2
x3

## Slide 9: Hybrid differentiation (arbitration time and persistence probability)
UAT differentiation generates a master urgency class -- UAT(0)=PIFS.
Further differentiation is achieved through the persistence probability, which is used to determine whether to transmit following an idle slot time.
  A higher persistence probability is used for higher priority packets.*
  The variance of the distribution will depend on the traffic intensity.
    Traffic intensity is determined by remembering the number and age of transmission attempts of packets in different classes by a station; and
    by listening to a broadcast of the same in transmissions from other stations.
*p-DCF differentiates between all classes through the use of different persistence probabilities that are higher for higher priority packets.

## Slide 10: Hybrid differentiation (arbitration time and persistence probability)
Example: Constant persistence probability for each class
A constant persistence probability is equivalent to drawing a backoff counter from a geometric distribution with mean and variance .
An upper bound on the number of retrials truncates the distributions on the right.
Probability density function of initial backoff counter for the different class populations using the same UAT time.

## Slide 11: Summary and conclusions
‘Tiered contention’ enables QoS management while achieving superior performance; as
in congestion, it prevents collisions between packets of different classes and allows high urgency packets to transmit before low urgency packets;
adapts to (class-specific) local congestion levels;
is backward-compatible with the current Standard
  through the use of Hybrid TCMA in the short term; and
  evolution into its pure form, following PHY specification of a shorter clear channel assessment time for new stations.