## Slide 1: An Enhanced-DCF Proposal Based on ‘Tiered Contention’ Multiple Access (TCMA)
Mathilde Benveniste
AT&T Labs, Research

## Slide 2: Key Benefits
This E-DCF proposal enables QoS management while achieving the following:
Is responsive to QoS performance with simple MAC protocol -- Software mapping of 8 traffic classes into a fewer urgency classes adapts in real time.
Reduces contention without starving low priority classes -- Minimizes collision probability between certain traffic classes, allowing high urgency packets to go first.
DCF remains a truly distributed protocol -- All nodes (APs and stations) are treated alike; the same DCF MAC protocol is used by both.

## Slide 3: Traffic classification
There are nPC=8 priority classes defined for all traffic packets which are permanently assigned to a packet once generated, according to 802.1d Annex H.2
There are nUC=N urgency classes employed for channel contention*
The urgency class of a packet is updated in real time so that it
  reflects both the priority class of the packet and the speed with which packets of different traffic classes and ages (the time since arrival at the queue) must be transmitted
  relies on the performance observed in real time
  *The value of N will be determined following further sensitivity analysis and optimization
PC1
PCn
Priority
Classes
Urgency
Classes
Traffic
Classification
(t2)
Urgency
Classes
UC1
UCm
...
Traffic
Classification
(t1)

## Slide 4: Class differentiation
Differentiation between urgency classes is achieved through differentiation w.r.t.
urgency arbitration times (UATs)
  shorter arbitration times are used for greater-urgency classes
parameters of the probability distribution for the backoff counters (for the same UAT values)
  the mean and variance will reflect the traffic intensity in the different classes
backoff retry adjustment functions
  govern the adjustment of the backoff distribution parameters on successive retries following transmission failure.
collision avoidance parameters
  govern the degree to which new arrivals defer to contending packets
packet age limits
  lead to cancellation of transmission if the age exceeds the threshold value
*S is an integer multiple of the slot time; its value will be determined following further sensitivity analysis and optimization

## Slide 5: Urgency Arbitration Times (UATs)
The minimum UAT value is PIFS
  Contention with the PCF is thus avoided
The different UAT values associated with different urgency classes differ by a time slot
  The carrier-sense mechanism thus has time to determine if the medium is busy
The probability that packets from classes with different UAT values will collide is minimized
  In congestion, when several nodes have packets of higher classifications with nearly expired backoff counters (that is, equal to 1) the possibility of collision is eliminated
  In congestion, higher urgency packets will be transmitted before lower urgency packets

## Slide 6: Backoff Counter Distribution
The random backoff counter will be drawn initially from a uniform distribution with range [rLower,rUpper]
The ranges of the backoff distributions are determined from estimates of traffic intensity
  A higher variance is used for higher traffic intensity
  Higher intensity in classes of greater urgency increase the mean of the distribution
The lower bound of the backoff range, rLower, will be greater than or equal to 1, for all classes with UAT=PIFS.
  Contention with the PCF is thus avoided
  Only legacy packets with initial backoff=0 will transmit before classes 1,2, and 3 in congestion [This occurs for 1/(aCWmin+1)=3% of the legacy packets; the remaining 97% will defer to the higher urgency classes]
Following transmission failure, adjustment of the backoff range (aLower,aUpper) will depend on
  the packet’s urgency class,
  the traffic intensity estimates, and
  the packet age
The new backoff range may lead to greater persistence (lower backoff counters) for aging packets

## Slide 7: Adaptation to Traffic Congestion
Packet headers and messages will be exchanged during reservation include
  the urgency class of the packet
  the number of the retrial attempts and
  the packet age
Class-specific traffic intensity estimates will be derived from information “remembered” by a node concerning its own packets and from information received about packets of neighbouring nodes
Traffic adaptation occurs when the parameters of the backoff distribution are determined initially and upon retrial*
The Distributed Coordination Function thus remains distributed, as estimation of traffic intensity and adaptation of the backoff distribution is performed in a decentralized manner.
*Formulas for the adaptation will be provided following further sensitivity analysis and optimization

## Slide 8: Scheduling of multiple streams*
Parallel queues shall be maintained for each class at a node, each adhering to backoff principles consistent with that class
  Packets will change queues when their urgency classifications are adjusted
  A packet will leave its queue if its transmission is cancelled due to excessive latency; the age threshold, aAgeLimit, will be class dependent
When a packet’s backoff counter becomes 1 it shall be placed in the node’s access buffer; in case of a tie, the higher urgency packet is selected
Packets generated by stations with multiple traffic types will thus not be disadvantaged
* This is similar to the approach in the V-DCF proposal with a modification
Packet Stream to Node A
Packet Stream to Node B
Access Buffer
Packet Stream to Node C
Contention
for access
CHANNEL
TRANSMISSIONS

## Slide 9: Fast adaptation to traffic with low latency jitter
If continuous adaptation to traffic is desired, the backoff counter is scaled up or down
The age of packets is thus respected
Leading to low latency jitter, which is desirable for real-time and isochronous traffic