## Slide 1
Contention-Free and Contention-Based Access in Contention Period
Jin-Meng Ho, Sid Schrum, Khaled Turki
Donald P. Shaver and Matthew B. Shoemake
Texas Instruments Incorporated
12500 TI Blvd.
Dallas, Texas 75243
(214) 480-1994 (Ho), (919) 463-1043 (Schrum), (214) 480-6908 (Turki)
(214) 480-4349 (Shaver), (214) 480-2344 (Shoemake)
jinmengho@ti.com, sschrum@ti.com, khaled@ti.com
shaver@ti.com, shoemake@ti.com

## Slide 2
Features of Hybrid Channel Access
Both contention-free and contention-based access in the “contention period (CP)” are provided under a hybrid coordinator (HC) located at the EAP
  Enables EAP/HC to use PIFS/SIFS for contention-free transmissions in CP
  Enables EAP/HC to use +CF-Poll for arranging contention-free transmissions in CP from wireless ESTAs
  Enables wireless ESTAs to use token-like mechanism for contention-free transmissions in CP
  Enables EAP/HC to use probabilities for adaptive and orderly control of contention activities in CP of all traffic categories
  Enables wireless ESTAs to use backoff counters for implementing adaptive contention in CP
  Enables wireless ESTAs to use (short) Poll Request for contention-free transmission in CP of data bursts
Piggybacked acks in CP, just as in CFP, are supported for better throughput

## Slide 3
Benefits of Hybrid Channel Access
Offers flexible alternating contention-free and contention-based transmissions in CP
Reduces access delay while serving a broad loading range
Mitigates inter-BSS interference while enhancing channel reuse
Allows EAP/HC and wireless ESTAs to access both CFP and CP by compatible mechanisms
  Same schedulers at EAP/HC and ESTAs work across CFP and CP
Facilitates consolidation of QoS conformance levels

## Slide 4
Advantages of p-Adaptive CSMA
Adjusts the contention intensities (via probabilities or backoffs) of all TCs (and hence ESTAs) in opposite to contention load changes
  With non-adaptive backoff contention, EAP/HC looses control over the contention of stations with running backoff timers, the loss deepening as congestion develops and when contention control is most needed
  With non-adaptive backoff contention, at any given time, the channel is loaded by a set of contending TCs with differing, indeterministic contention intensities, hence resulting in an unknown and uncontrollable load
  With adaptive backoff contention, the contention intensities of TCs are both predictable and controllable, lending to effective systematic optimization and simple recursive algorithms
  With adaptive backoff contention, adaptation is based on persistent attempt (memoryless geometrical distribution) and hence resetting backoffs does not prolong the contention of any TCs or ESTAs with leftover backoffs
Tunes collision avoidance in response to contention load changes
  Non-adaptive contention windows cause too many idles at light load and too many collisions at heavy load.
Performs collision resolution with respect to all contending TCs
  Collision backoffs by doubling CWs unfairly over-penalizes colliding (and co-locating) TCs while hardly alleviating the overall contention intensity at high load (by leaving the CWs of other TCs unchanged)
Achieves 30% throughput improvement over non-adaptive backoff

## Slide 5
Attainments of Fairness
Enables fair contention between TCs of equal priorities
  Fairness is maintained whether an ESTA has one or more queued TCs, and whether any of the queued TCs has experienced a collision
  Contention decision, local selection, and fairness realization are achieved concurrently with little extra computational effort
Controls channel access order and duration for TCs of unequal priorities by setting probabilities for various TCs (according to QoS requirements and loading conditions)
  Some TCs may be served via contention-free access, and some may be served via contention-based access, in accordance with QoS demands
  Not all TCs may be selected for contention over a certain period to have absolute (strict) priority access for meeting QoS requirements
  Some TCs may be forbidden from contending over a certain period for more effective collision avoidance and collision resolution, or for tentative restrictive access of those TCs
  TCs of unequal priorities are given unequal transmission probabilities for relative (non-strict) priority access to avoid starvation of low priority TCs

## Slide 6
Contention-Free Access: PIFS and SIFS for EAP/HC
After a PIFS following a frame exchange sequence, EAP/HC can send a directed or broadcast/multicast {QoS }Data frame
After a PIFS following a frame exchange sequence, EAP/HC can send a directed {QoS }{Data + }CF-Poll frame
  Setting the Duration field to the time, in µs, allocated to the TXOP of the addressed ESTA, plus one CF-Ack frame time, plus two SIFS intervals
  Setting the More Data field to 1 if the EAP/HC requires the polled ESTA to send a frame back to it, but not to another ESTA
After a SIFS following a frame addressed to itself, EAP/HC can send a directed or bc/mc {QoS }Data + CF-Ack frame, or an Ack
  Sending to a DA different from the SA of the received frame allowable
  Making piggybacked acknowledgment as in CFP allowable
After a SIFS following a frame addressed to itself, EAP/HC can send a directed {QoS }{Data + }CF-Ack + CF-Poll frame
  Sending to a DA different from the SA of the received frame allowable
  Making piggybacked acknowledgment as in CFP allowable
  Setting the Duration and More Data fields as stated above

## Slide 7
After a SIFS following a {QoS }{Data + }{CF-Ack + }CF-Poll frame addressed to itself, a wireless ESTA sends a directed {QoS }{Data + }CF-Ack frame, or a {QoS}Null frame
  Making piggybacked acknowledgment as in CFP allowable
  Sending to another ESTA allowable if the received More Data bit is set to 0
  Using a TXOP equal to the received Duration field value subtracted by one CF-Ack frame time and two SIFS intervals
  Piggybacking the remaining size of the TC from which a frame is being transmitted by a QoS Data + CF-Ack frame into the TCID field of that frame
After a SIFS following a non-fragmented {QoS }Data{ + CF-Ack} frame addressed to itself, a wireless ESTA may send a directed {QoS }Data + CF-Ack frame of at least same priority as the received frame (applicable in both BSS and IBSS)
  If this ESTA has not sent a frame within this frame exchange sequence
  Making piggybacked acknowledgment as in CFP then allowable
  Sending to another wireless STA then further allowable
  Piggybacking the remaining size of the TC being served then also allowable
After a SIFS following a {QoS }Data{ + CF-Ack} frame addressed to itself, a wireless ESTA may send an Ack frame
Contention-Free Access: Polls and Tokens for ESTAs

## Slide 8
A wireless ESTA sends a Poll Request (PR) frame to EAP/HC for contention-free access for a burst of local queued MSDUs
  Setting the Duration field to the time, in µs, required to send the first MSDU of the burst, a CF-Poll frame, and a CF-Ack frame, plus three SIFS intervals
  Setting the BSSID field as defined in the baseline proposal
  Setting the TCA field to the AID of the ESTA sending this PR, plus the priority of the queued TC for which the PR is sent
  Setting the TC Size field to the size of the queued burst in the 10 least significant bits (lsb), with the 6 most significant bits (msb) all set to 0
The ESTA may send a PR frame to the EAP/HC via contention-based or contention-free access
The EAP sends a {QoS }{Data + }CF-Ack + CF-Poll to the requesting ESTA one SIFS after receiving a PR frame
  Setting the implied TXOP limit to a value equal to or smaller than the time for transferring the TC size indicated in the PR frame
  Sending more + CF-Poll frames to the requesting station later on until the targeted TC is indicated to be empty
Contention-Free Access: Poll Requests by ESTAs
Frame
Control
Duration
BSSID
TCA
TC Size
FCS
Octets:
2
2
6
2
2
4
Poll Request (PR) frame
(Type 01, subtype 0011)

## Slide 9
Beacon
TBTT
CF-End
PIFS
{QoS }Data + CF-Poll
(EAP/HC  ESTA 2)
TBTT
Contention Period (CP)
SIFS
DIFS
{QoS }Data + CF-Ack
+ CF-Poll
(EAP/HC  ESTA 1)
{QoS }Data + CF-Ack
(ESTA 2  EAP/HC)
NAV
NAV
NAV
{QoS }Data + CF-Ack
(ESTA 1  ESTA 4)
{QoS }Data + CF-Ack
(ESTA 4  ESTA 5)
CF-Ack
CF-Ack
CF-Ack
NAV
CF-Ack
NAV
{QoS }Data
(EAP/HC  ESTA 3)
NAV
CF-Ack + CF-Poll
(EAP/HC  ESTA 3)
{QoS }Data + CF-Ack
(ESTA 3 EAP/HC)
NAV
NAV
SIFS
aSlotTime
PIFS
DIFS
Contention-
Free Period
(CFP)
More
Data
= 1
More
Data
= 0
More
Data
= 0
More
Data
= 1
More
Data
= 1
CF-Ack
{QoS }Data + CF-Ack
(ESTA 5  ESTA 1)
NAV
Contention
based
transmissions
PIFS
DIFS
Contention
based
transmissions
Contention-Free Access: Illustrations
PR
(ESTA3 EAP/HC)
CF-Ack
Data
(Max
Size)
CF-Ack
{QoS }Data + CF-Ack
(EAP/HC  ESTA 2)
CF-Ack
NAV
NAV

## Slide 10
EAP/HC assigns each traffic category (TC) a permission probability (PP), denoted TCPP, for coordinating TCs’ contention
  Always equal TCPPs for equal priority TCs (new or retried) across BSS
An active ESTA calculates a PP as sum of the TCPPs for the local queued TCs for conducting the ESTA’s contention
  Setting TCPPs for local empty TCs equal to 0
  Recalculating the PP when any of the constituent TCPPs changes, due to change of local TCs from queued to empty status or vice versa, or due to change of TCPP values
After the medium is idle for a DIFS following a frame exchange sequence, the ESTA transmits with a probability = PP as follows
  The ESTA draws a number, X, from a uniform distribution over (0, 1)
  If X  PP, the ESTA is not permitted to transmit
  If X  PP, the ESTA is permitted to transmit a frame
  The frame to transmit is selected from TCk if X falls into its TCPP range, i.e., if TCPP0 + TCPP1 + … + TCPPk-1  X  TCPP0 + TCPP1 + … + TCPPk
Contention-Based Access: Permission Probabilities
0
1
PP
TCPP0
TCPP1
TCPPk
TCPP7
X
...
...

## Slide 11
Following each successive idle slot, an active ESTA transmits with a probability = PP as specified above
  Recalculating PP if and only if any of the constituent TCPPs changes
After transmission of a frame, the ESTA may send a new or failed frame after the medium is idle for a DIFS following a busy status
  Recalculating PP if and only if any of the constituent TCPPs changes
  Treating a failed frame as a new frame for retry purposes
    The retried frames should not be discriminated now that they are to be retried
    The retry counts are still applicable, so are relevant QoS constraints on retries
  Selecting a frame for transmission as specified before
    This prevents repeated retries of the same frame at the cost of delaying frame transmissions from other local queued TCs
  Repeating the above procedures for more contention-based transmissions
Equivalently, an active ESTA transmits with a probability = current PP whenever a legacy STA with backoff count of 0 can transmit
  The NAV rule still applies
Contention-Based Access: Persistent Contention

## Slide 12
Contention-Based Access: Probability Update
EAP/HC updates TCPPs based on its contention control policy
  Broadcasting new TCPPs via a CP contention control (CCC) beacon element or a standalone CCC frame
    EAP/HC may send a CCC frame if need be, specifying in that frame whether contention by ESTAs commences after a PIFS or DIFS following the frame
    After a PIFS or DIFS following the CCC frame, ESTAs transmit by persistent contention using the TCPPs contained in that frame
ESTAs finding no CCC element in a beacon invoke default rules
  ESTAs in an IBSS or after a power save wake up use these rules
  Once a new CCC beacon element or standalone frame is received, ESTAs revert to the TCPPs specified therein for subsequent adaptive contention
Default rules for contention access in CP are specified as follows
  For TCPPi  0, it remains unchanged if TCi does not experience a collision
  TCPPi = TCPPi, min for TCi having a new frame at head
    TCPP0, min = 2/33, TCPPk, min = 2/17, k = 1, 2, …,7
  TCPPi is halved, subject to TCPPi  TCPPi, max, upon a collision of TCi
    TCPPl, max = 2/1056, l = 0, 1, …, 7
    Relevant retry counts, and QoS constraints on retries, still apply
Length
TCPP values
TCPP0 … TCPP7
Octets:
1
1
8
CP Contention Control (CCC)
element format
Element ID

## Slide 13
Contention-Based Access: Load Control (Example)
Control Criterion
  Channel is optimally utilized/loaded when time on idles = time on collisions
    Time on an idle = a slot time
    Time on a collision = longest transmission time of colliding stations + Ack transmission time + SIFS + DIFS
Control Mechanism
  EAP/HC decreases TCPPs if channel is overloaded and vice versa
  Contending ESTAs respond immediately to a change in TCPPs
    Full adaptation: +  30% throughput over non-adaptive backoff schemes
Control Procedure
  Preset numbers: 1, 2 ,…, m, m, D, R, 0, 1, …, 7, 0, 1, …, 7
  TI = 1 ·T1, I + 2 ·T2, I + … + m ·Tm, I , TC = 1 ·T1, C + 2 ·T2, C + … + m ·Tm, C
    Tk, I = time spent on idles over the kth latest update interval
    Tk, C = time spent on collisions over the kth latest update interval
    The 1st latest update interval = the update interval since last update
    1 + 2 + … + m = 1: update and smooth load changes
  D = TI - TC , R = TI / TC
  When D  D or R  R, or when a beacon is to be sent, update TCPPs
  TCPPk  TCPPk + k ·D or TCPPk  TCPPk  k ·R, k = 0, 1, 2, …, 7

## Slide 14
Active ESTAs may contend using backoff in lieu of probability
An active ESTA, upon obtaining a new PP, sets new backoff time
  The ESTA draws a number, X, from a uniform distribution over (0, 1)
  The ESTA sets new backoff time as N = log(X)/log(1  PP) slot times
    Y = largest integer not exceeding Y (i.e., truncating any fractional part of Y)
An active ESTA decrements its backoff timer as a legacy STA
An active ESTA sends a frame when its backoff timer reaches 0
  The frame to send is selected from TCk if C ·X falls into its TCPP range, i.e., if TCPP0 + TCPP1 + … + TCPPk-1  C ·X  TCPP0 + TCPP1 + … + TCPPk
    C = TCPP0 + TCPP1 + … + TCPP7
  A failed frame is treated as a new frame for retry purposes
    The retry counts are still applicable, so are relevant QoS constraints on retries
An active ESTA resets its backoff timer when its PP changes
  Due to change of local TCs from queued to empty status or vice versa
  Due to change of TCPP values based on EAP/HC updates or default rules
Contention-Based Access: Adaptive Backoff
0
C
TCPP0
TCPP1
TCPPk
TCPP7
C·X
...
...

## Slide 15
Contention-Based Access: Backoff Equivalence
Backoff Equivalence
  Given that an ESTA begins to transmit with a probability p = PP at slot started at t = 0 and continues to transmit with p at each successive slot
  The probability that the ESTA is not permitted to transmit until t = k slots is P(k = k) = p(1-p)k, k = 0, 1, 2, ...
  Equivalently, the ESTA chooses a backoff k = k slots for next transmission
  With X drawn from a uniform distribution over (0, 1), k is calculated by
    P(0) + P(1) + ... + P(k-1)  1- X  P(0) + P(1) + ... + P(k)
    1-(1-p)k  1- X  1-(1-p)k+1  (1-p)k  X  (1-p)k+1
    k log(1-p)  log(X)  (k+1) log(1-p)  k |log(1-p)|  |log(X)|  (k+1) |log(1-p)|
    |log(X)/log(1-p)| - 1  k  |log(X)/log(1-p)| 
    k = log(X)/log(1- p) slots = backoff time
Memoryless Property
  The ESTA may choose a backoff time k  j slots or k  j slots
  For k = k  j, resetting backoff timer at t = j with the same p = PP does not alter backoff expiration time probabilistically: P(k = k -j) = P(k = k | k  j)
    P(k =k | k  j) = P(k = k, k  j) / P(k  j) = P( k) /[ P( j) + P(j + 1) + … ] = p(1-p)k / (1-p)j = p(1-p)k-j = P(k = k - j)
  Resetting backoff timer with a larger p shortens backoff expiration time probabilistically, and vice versa
...
...
0
1
2
j
j+1
k
j
k-j
k

## Slide 16
Contention-Based Access: Illustrations
TBTT
Busy
transmissions
separated
by SIFS or
PIFS
TBTT
DIFS
PP = P1
aSlotTime
Ack
aSlotTime
P2  P1:
PP changes
due to a
new frame
arrival to an
empty TC
PP = P2
Busy
transmissions
separated
by SIFS or
PIFS
Frame
transmission
from a
selected TC
(collided)
CCC
Update
PP = P2
PP = P3
Ack
Frame
transmission
from a
selected TC
(successful)
P3  P2:
PP changes
due to a CP
contention
control
update
Beacon
with CCC
Beacon
with CCC
PP = P4
P4  P3:
PP changes
due to a CCC
update in beacon
and a TC
becoming empty
…
Start of CP
DIFS
DIFS
PIFS
Start of CP
DIFS
TBTT
Busy
transmissions
separated
by SIFS or
PIFS
TBTT
DIFS
aSlotTime
aSlotTime
Ack
aSlotTime
Busy
transmissions
separated
by SIFS or
PIFS
Frame
transmission
from a
selected TC
(collided)
CCC
Update
Ack
Frame
transmission
from a
selected TC
(successful)
Beacon
with CCC
Beacon
with CCC
Start of CP
DIFS
DIFS
PIFS
Start of CP
DIFS
Backoff with
PP = P1
Backoff with
PP = P2
Backoff
resumes
Backoff with
PP = P3
Backoff with
PP = P4
Backoff
is reset
after a
change in
PP
Backoff
resumes
Backoff
is reset
with
new PP
(after collision)
Backoff
is reset
with
new PP
(after success)
aSlotTime
Contention
resumes
with
the same
PP
Persistent Contention
Adaptive Backoff

## Slide 17
Fairness
  All TCs of equal priority transmit with the same TCPP
    Anytime -- before or after collision
    Anywhere -- at the same ESTA or at different ESTAs
Differentiation
  Relative differentiation: Higher priority TCs contend with larger TCPPs
    Access probability ~ TCPP
    Lower priority TCs not starved
  Absolute differentiation: Some TCs may be stayed from contention
    TCPPs for stayed TCs set to 0
    Higher priority TCs not impacted by lower priority TCs
    Collision resolution accelerated
    Minimum bandwidth guaranteed for selected TCs
    Maximum bandwidth imposed on certain TCs
    Transmission from “continuous” TCs served by contention-free access
Contention-Based Access: Fairness and Differentiation

## Slide 18
Contention-Based Access: Implementation Complexity
EAP/HC updates TCPPs of TCs by a control algorithm, e.g.
  TI = 1 ·T1, I + 2 ·T2, I + … + m ·Tm, I , TC = 1 ·T1, C + 2 ·T2, C + … + m ·Tm, C
  D = TI - TC , R = TI / TC
  When D  D or R  R, or when a beacon is to be sent, update TCPPs
  TCPPk  TCPPk + k ·D or TCPPk  TCPPk  k ·R, k = 0, 1, 2, …, 7
Wireless ESTAs (re)calculate their backoffs with updated TCPPs
  TCPPk = 0 for local empty TCk
  PP = TCPP0 + TCPP1 + … + TCPP7
  X = random number drawn from uniform distribution over (0, 1)
  Backoff = log(X)/log(1- PP) slots -- implemented via uniform distribution!
  Contention = legacy backoff contention
  Frame from TCk: sum(TCPP0, …, k-1)  sum(TCPP0, …, 7)·X  sum(TCPP0, …, k)
Legacy STAs (re)calculate their backoffs upon new arrival or collision
  X = random number drawn from uniform distribution over (0, 1)
  Backoff = X ·CWmin slots for new frames
  Backoff = X ·CW slots, CW = min[(2 ·CW + 1), CWmax], for retried frames
Comparable Complexity

## Slide 19
Contention-Based Access: Performance Improvement
 30% throughput improvement over non-adaptive backoff is reported in IEEE journals
  PP. 146-149 in F. Cali, et al., “Dynamic Tuning of the IEEE 802.11 Protocol to Achieve a Theoretical Throughput Limit,” IEEE INFOCOM’98.
  P. 1783 in . F. Cali, et al., “IEEE 802.11 Protocol: Design and Performance Evaluation of an Adaptive Backoff Mechanism,” IEEE J. Select. Areas Commun., vol. 8, Setp. 2000.
    Also shows that the probabilities need not be updated after each event (idle, success, or collision)
 Significant throughput, delay, and jitter improvement over non-adaptive backoff is also observed in our own simulation effort
  To be presented separately
Performance improvement becomes even more substantial in high population areas such as in enterprise environments
  Non-adaptive backoff begins to fail as user population increases

## Slide 20
Contention-Based Access: Simulation Result
Operation “recovered” from congestion as frames exceeding retry counts were discarded

## Slide 21
…
…
…
…
…
…
…
…
…
…
Contention-Based Access: Binary Exponential Backoff
Doubling CW for colliding TCs at low load unnecessarily delays frame transmission and decreases channel throughput
The leftover backoff times of various TCs are inestimable to EAP/HC at the time of setting new CWmins
Doubling CW for colliding TCs does not necessarily alleviate congestion state --collisions formed from past backoffs will still occur
Randomization without drastically increasing CW improves delay and throughput performance
Setting CWmins without knowing leftover backoff times causes new frames to collide with backoff frames
Each collision costs much channel time, aggravates congestion state, and result in more collisions in the future

Doubling CW for colliding TCs substantially downgrades the access priority for both retried and new frames of those TCs, compared to frames of TCs not undergoing collision resolution
Resetting CWmins cannot stop collisions developed in the past and bound to occur in the future
CWmin update for
new frame arrivals only
Contention-based
and contention-free
transmissions

Doubling CW for colliding TCs over-penalizes the colliding TCs, even more so for those that had collided before
Doubling CW for co-locating, but non-colliding TCs further distorts fairness, differentiation, and contention scales

## Slide 22
…
…
…
…
…
…
…
…
…
…
Contention-Based Access: Adaptive versus Binary Exponential Backoff
…
…
…
CWmin
update for
new frame arrivals only

TCPP update for
all TCs

CW
reset for
all TCs

CWmin
sete for
new frame arrivals only

Binary Exponential Backoff
Adaptive Backoff
Collision increases, and hence throughput decreases, dramatically with increasing population of contenders
Offered load increases with increasing population of contenders

Collision does not increase, and hence channel throughput does not decrease, with increasing population of contenders
Offered load is controlled to remain below a maximum level regardless of the population of contenders


## Slide 23
Concluding Remarks
Binary exponential backoff has been considerably criticized for its poor throughput and delay performance
Adaptive backoff significantly improves such performance with little additional implementation complexity
  Increasing bandwidth demand warrants such an upgrade
  QoS is better supported by an efficient protocol

## Slide 24
Sample References
Books:
1. D. Bertsekas and R. Gallager, Data Networks, 2nd ed., Prentice Hall, NJ, 1992, Chapter 4.
2. A. S. Tanenbaum, Computer Networks, 3rd ed., Prentice Hall, NJ, 1996, Chapter 4.
Papers:
1. L. Kleinrock and/or F. Tobagi's CSMA and CSMA/CD papers published between 1975-1985.
2. F. Cali, et al., “IEEE 802.11 Protocol: Design and Performance Evaluation of an Adaptive Backoff Mechanism,” IEEE J. Select. Areas Commun., vol. 8, Setp. 2000, pp. 1774-1786.
3. F. Cali, et al., “Dynamic Tuning of the IEEE 802.11 Protocol to Achieve a Theoretical Throughput Limit,” IEEE INFOCOM’98, pp. 142-149.