## Slide 1: IEEE 802.11 Security and 802.1X Dan Simon, Bernard Aboba, Tim Moore Microsoft Corporation
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2: IEEE 802.11
Attempts to provide “privacy of a wire”
RC4 stream cipher used for encryption
  Invented at RSA Laboratories
  RC4 encryption stream derived from WEP key + initialization vector
No per-packet authentication
  ICV provides integrity protection, but does not depend on the WEP key

## Slide 3: Types of Attacks
Physical
  Theft of hardware
Impersonation
  Attacker masquerades as another person
Integrity
  Undetected modification of data
Disclosure
  Unintended exposure of data
Denial of service
  Keep valid users from access

## Slide 4: Physical Threats
User loses 802.11 NIC, doesn’t report it
  Attacker with physical possession of NIC may be capable of accessing the network
    Implementation could encrypt WEP key on machine, require password to unlock before plumbing
    Creates problems for machines accessible by more than one user, users who move between machines
  With global keys, large scale re-keying required
Without user identification and centralized authentication, accounting and auditing, difficult to detect unusual activity
  Users who don’t log on for periods of time
  Users who transfer too much data, stay on too long
  Multiple simultaneous logins
  Logins from the “wrong” machine account

## Slide 5: Impersonation: User Identification
802.11 does not identify users, only NICs
Problems
  MAC may represent more than one user
    Multi-user machines becoming common; which user is logged on with which MAC?
  Users may move between machines
    Machine may allow logins by other users within the domain
    Issue for wireless kiosks, public use clusters
  Per-user or even machine authorization not possible
  Not possible to authorize guest and Administrator differently

## Slide 6: Impersonation: Rogue APs
802.11 shared authentication not mutual
  Client authenticates to Access Point
  Access Point does not authenticate to client
Enables rogue access points
  Denial of service attacks possible
Solution
  Mutual authentication
    Require both sides to demonstrate knowledge of key

## Slide 7: Integrity: Known Plaintext Attack
WEP supports per-packet encryption, integrity, but not per-packet authentication
  ICV not a keyed MIC
    Protects against random “bit flips”, but knowledge of WEP key not required to construct it
Given a known packet (ARP, DHCP, TCP ACK, etc.), possible to recover RC4 stream
  Enables spoofing of packets until IV changes
    Can insert a packet, calculate ICV, encrypt with known RC4 stream
    Must be able to insert or modify packets in the 802.11 stream
  Enables decryption of packets until IV changes
Solution
  Add a keyed message integrity check
  Change the IV every packet

## Slide 8: Disclosure: Passive Monitoring
By monitoring the 802.11 control and data channels information about the Access Point and client can be obtained
  Client and Access Point MAC addresses
    Needed to deliver packets; disclosed by all protocols
  MAC addresses of internal hosts
  Time of association/disassociation
Enables traffic analysis, long term profiling
  Unlike IP address, MAC address is static
    Makes it easy to attribute traffic to a user, albeit imperfectly
  Layer 3 traffic analysis more interesting than layer 2
Solution
  None

## Slide 9: Disclosure: Global Keys
Per-user keys enabled by WEP
  However, without dynamic key management, difficult to manage per-user keys
Problems with static global keys
  A secret shared by more than two is not a secret
  Enables rogue Access Point attacks
  Enables anyone with access to the global key to decrypt other conversations
  Global key change requires large scale re-key

## Slide 10: Denial of Service: Disassociation Attacks
802.11 associate/disassociate messages unencrypted and unauthenticated
  Enables forging of disassociation messages
  Creates vulnerability to denial of service attacks
Solution
  Keyed message integrity check

## Slide 11: Denial of Service: Integrity Verification
Message integrity check typically calculated on encrypted data
  Enables receiver to see if payload has been modified before decrypting it
  In 802.11, ICV is calculated, then payload is encrypted
  Not much of an issue for RC4, which is very efficient in hardware and software
  Would be an issue for more computationally intensive ciphers such as 3DES.

## Slide 12: Disclosure: Dictionary Attacks
In some implementations, WEP keys are derived from passwords
  Makes it much easier to break keys by brute force
Attacker uses a large list of words to try to guess a password and derive the key
  Two types of dictionary attacks: pre-computed and offline
  Pre-computed assumes fixed mapping between password and key
    Encrypted password compared against all words in list (also encrypted) until match found
  If an nonce is included in the key derivation, then pre-computed attack more difficult

## Slide 13: Dictionary Attacks (cont’d)
Most password-based authentication methods vulnerable
  Known vulnerabilities of Kerberos V
    AS_REQ includes PADATA encrypted with a password-derived client key, no nonces
      Enables rogue access point to mount dictionary attack
    AS_REP encrypted with password-derived client key, no nonces
      Enables passive attacker to mount offline attack
Solutions
  Use non-password authentication
  Don’t generate WEP keys from passwords
  If you need password-based key derivation, use EKE
    Password-derived key used to encrypt Diffie-Helman key exchange

## Slide 14: Password Entropy Issues
Keys derived from user passwords are likely to be weak
  If password is poorly chosen, the resulting key will be relatively weak and easy to break
  Even if password is well chosen, if password entropy < key length then effective key strength is reduced
English = 1.3 bits of entropy/character
  10 character password = 13 bit key!
  Dictionary attacks easy on English passwords
Passwords SHOULD mix upper/lower case letters, numbers, punctuation
Random passwords
  6.5 bits entropy/character = log2 (52 alpha + 10 numeric + 30 specials)
  20 random characters required for 128 bits of entropy (22 * 6.5 > 128)

## Slide 15: Summary of 802.11 Vulnerabilities

## Slide 16: How To Address Security Issues?
Addition of new 802.11 authentication methods
  Hardware changes needed for each new method
    Creates incentive to limit number of authentication methods supported, make new methods optional
    Result: No upgrade path to extended authentication
  “Hard coding” authentication methods makes it difficult to respond to security vulnerabilities
Lessons from the school of hard knocks
  Security vulnerabilities often found after the fact
  Quick rollout of fixes frequently required
  “Hard wiring” support for particular authentication technique a bad idea
    Drives up cost of hardware
    Prevents flexible response to security vulnerabilities
    Inhibits introduction of new security technologies

## Slide 17: 802.1X Security Philosophy
The solution: a flexible security framework
  Implement security framework in upper layers
  Enable plug-in of new authentication, key management methods without changing NIC or Access Point
  Leverage main CPU resources for cryptographic calculations
How it works
  Security conversation carried out between supplicant and authentication server
  NIC, Access Point acts as a pass through devices
Advantages
  Decreases hardware cost and complexity
  Enables customers to choose their own security solution
  Can implement the latest, most sophisticated authentication and key management techniques with modest hardware
  Enables rapid response to security issues

## Slide 18: How 802.1X Addresses 802.11 Security Issues
EAP Framework
User Identification & Strong authentication
Dynamic key derivation
Mutual authentication
Per-packet authentication
Dictionary attack precautions

## Slide 19: EAP Framework
EAP provides a flexible link layer security framework
  Simple encapsulation protocol
    No dependency on IP
    ACK/NAK, no windowing
    No fragmentation support
  Few link layer assumptions
    Can run over any link layer (PPP, 802.3, etc.)
    Does not assume physically secure link
      Methods provide security services
    Assumes no re-ordering
    Can run over lossy or lossless media
      Retransmission responsibility of authenticator (not needed for 802.1X or 802.11)
EAP methods based on IETF standards
  Transport Level Security (TLS) (supported in Windows 2000)
  Internet Key Exchange (IKE)
  GSS_API (including Kerberos)

## Slide 20: EAP Architecture
EAP
Layer
Method
Layer
EAP
TLS
Media
Layer
NDIS
APIs
EAP
APIs
PPP
802.3
802.5
802.11
IKE
GSS_API

## Slide 21: User Identification & Strong Authentication
802.1X users identified by usernames, not MAC addresses
  Enables user-based authentication, authorization, accounting
802.1X designed to support extended authentication
  Focus is non-password based authentication
    Public-key certificates and smartcards
    IKE
    Biometrics
    Token cards
  However, password-based authentication also supported
    One-time Passwords
    Any GSS_API method (includes Kerberos)

## Slide 22: Per-User Session Keys
802.1X framework enables secure derivation of per-user session keys
  Methods supporting dynamic key derivation and mutual authentication: TLS, IKE, GSS_API(Kerberos)
Makes per-user WEP keys easy to administer
  No longer need to store WEP keys on NIC, Access Point
Provides improved security
  Dynamic key derivation ensures that WEP key varies from session to session, makes attacks much more difficult
Provides ability to securely change global keys
  Global keys can be sent from Access Point to client, encrypted in session key

## Slide 23: Mutual Authentication
For use with 802.1X, EAP methods supporting mutual authentication are recommended
  Need to mutually authenticate to guarantee key is transferred to the right entity
  Prevents man-in-the-middle and rogue server attacks
Common EAP methods support mutual authentication
  TLS: server must supply a certificate, prove possession of private key
  IKE: server must demonstrate possession of pre-shared key or private key (certificate authentication)
  GSS_API (Kerberos): server must demonstrate knowledge of the session key

## Slide 24: Dictionary Attack Precautions
EAP created to support extended authentication
  Primary focus is non-password based authentication
  Token cards, Certificates, smartcards, one-time passwords, biometrics not vulnerable to dictionary attacks
  Cleartext authentication not supported
  EAP-MD5 included for minimum compatibility, but not useful for 802.11 (need mutual authentication)
EAP methods supporting password authentication should be carefully designed
  Use nonces to increase entropy of key space, provide immunity against pre-computed dictionary attacks
  Mutual authentication recommended
  EKE recommended for maximum security in password authentication
    Password-derived key used to encrypt Diffie-Helman exchange

## Slide 25: Authentication & Integrity Protection
EAP methods support per-packet authentication & integrity
  TLS, IKE derive session key
    TLS ciphersuite negotiations authenticated & integrity protected
    IKE ciphersuite negotiations are encrypted, authenticated, integrity protected
    GSS_API supports authentication, integrity protection for SPNEGO negotiated methods that support authentication and integrity protection
    Kerberos tickets are encrypted, authenticated and integrity protected
Authentication, Integrity protection not extended to all EAP messages
  Notification, NAK, messages not authenticated, integrity protected
  Identity authenticated, integrity protected in TLS, IKE (AM), Kerberos
  Identity encrypted, authenticated, integrity protected in IKE (MM)
  Possible to encrypt, authenticate and integrity protect Success, Failure messages using derived session key (via WEP)

## Slide 26: Address Spoofing Attacks
Rogue client can send EAP-Logoff message from another client’s MAC address
  Access-Point needs to ensure EAP-Logoff messages come from the MAC address associated with the client key
Rogue client can send EAP-Request messages to other STAs from Access Point MAC address
  Access-Point should not forward packets with a source address of the access point MAC
  Access-Point should not forward packets addressed to EAPOL multicast MAC address
    Required by 802.1X
Access point should check that unicast and shared keys are being used on the correct message types

## Slide 27: Remaining Attacks
Target Identification
  Passive Monitoring
    Identity messages not encrypted in EAP
    Identity also not encrypted in TLS, Kerberos
    Identity encrypted within IKE(MM) method so pre-method Identity disclosure not necessary in this case
Denial of Service
  “Bit flipping” attack on 802.11 data packets
      802.1X enables per-user session keys, but no keyed message integrity check in 802.11

## Slide 28: Summary of 802.11/802.1X Vulnerabilities