## Slide 1
Technical Feasibility of Spreading Codes for HRb
Mark Webster and Steve Halford
Intersil Corporation
May 2000

## Slide 2
802.11b 11 Mbps CCK vs. PBCC
PBCC is FEC-code based -- Rate 1/2, K=7, Viterbi with QPSK signaling
CCK is spreading code based.
What is the benefit of spreading codes?
Do the properties of CCK and FEC-Coded PSK extend to 22 and 33 Mbps for HRb?

## Slide 3
11 Mbps CCK vs. FEC-Coded QPSK
in Only Thermal Noise
FEC QPSK is ~3 dB better than CCK in thermal noise
FEC QPSK is ~1.5 dB better than 12 Mbps 802.11a OFDM in thermal noise
Good thermal noise is important, but multipath and multipath + noise are other dominate challenges
Multipath is almost always present in WLAN’s

## Slide 4
Multipath is a dominant WLAN impairment
Multipath exists at all signal-strengths
Baseband processor complexity driven by multipath
Both OFDM and CCK use transmit signal design to help combat multipath
OFDM uses guard intervals and narrowband multicarriers to combat multipath
CCK uses spreading codes to combat multipath
Spreading codes have optimized auto-and-cross correlation properties
Spreading codes maintain large signal distance in multipath -- Helps desensitize signal to multipath frequency notches
FEC-coded PSK signal sequences can be sensitive to multipath fading -- Short data patterns can be correlated with the multipath to produce some pattern-dependent fading. -- Equalization can be used to counter this effect.
Transmit Signal Design
for Multipath Mitigation

## Slide 5
CCK
Encode
11
Mbps
QPSK
Mod
11 MHz
Chips
Viterbi
Encode
QPSK
Mod
Multipath
Chan
QPSK
Demod
CMF
Fast
CCK
Transform
11
Mbps
11 MHz
Chips
Multipath
Chan
QPSK
Demod
CMF
Viterbi
Decoder
11
Mbps
11
Mbps
CCK vs. FEC QPSK w/CMF Receiver and No Equalization
Transmitter
Transmitter
Receiver
Receiver
CCK Link
FEC-coded QPSK
Channel
Matched
Filter

## Slide 6
CCK vs. FEC QPSK in Multipath-Only
CMF Receiver w/o Equalization
(Exponential Fading channel with 1 sample/chip)
CCK is 40% better in this scenario
Spreading codes provide the gain
Spreading codes are not just another form of FEC coding
In addition, CCK’s complexity is less in this scenario
Equalization can boost both CCK and FEC-coded PSK

## Slide 7
CCK vs. FEC-Coded QPSK Complexity
CMF Receiver w/o Equalization
Identical complexity except for decoders.
CCK decoder requires * Fast CCK Transform (efficient adds/subtracts) -- 60% reduction in correlator complexity * Compute FCT once every 8 chips (1.375 MHz).
FEC-coded QPSK decoder requires * Soft-decision generator for 2 bits (11 MHz) * Branch metric computation for 4 dibits (11 MHz) * Add-compare-select logic for 64 states (11 MHz) * Trellis-updating every chip (11 MHz) * Traceback memory required * Partial traceback output for PLL tracking

## Slide 8
11 Mbps CCK vs. FEC-Coded PSK Features
CCK FEATURES
Provides low-complexity option for quick to market.
Yet, provides higher-performance option when equalizer is added.
What about 22 and 33 Mbps?
FEC-Coded PSK FEATURES
Provides 3 dB more performance in noise-only environments.
Equalizer can be used to boost multipath performance.
What about 22 and 33 Mbps?

## Slide 9
Spreading codes can provide advantages. -- Help combat multipath interference
How CCK and FEC-coded PSK properties extend to 22 and 33 Mbps is currently under investigation.
Equalization requisite for very high performance
HRb should examine multiple signal types.
Summary