## Slide 1: Proposed Security Framework Requirements for 802.11
Steven Williams
Jesse Walker
Duncan Kitchin

## Slide 2: Two classes of requirements
Absolute requirements
  Any proposed framework must endeavor to meet
Relative requirements
  Used to break ties between two framework proposals that meet that absolute requirements

## Slide 3: Absolute requirements (1)
Security framework must prevent unauthorized authentication or re-authentication with an AP as those terms are defined within the 802.11 specification.
Security framework must be able to prevent unauthorized access by unauthenticated peers over the link
Security framework must protect network traffic from eavesdropping to a reasonable level compatible with the state of the art.

## Slide 4: Absolute requirements (2)
Security framework must allow for authentication of the source of each packet, to prevent link hijacking or undetected insertion of rogue packets into the link.
Security framework must allow for mutual authentication of STA and AP
Security framework must allow key distribution or derivation of per-link or per-session keys

## Slide 5: Absolute requirements (3)
Security framework must not compromise (i.e., break the security of) existing industry standard network user authentication methods and techniques used within the framework.
Security framework must coexist with existing industry standard network user authentication methods and techniques (e.g., RADIUS-based authentication).
Security framework must coexist with existing industry standard network user authentication methods and techniques (e.g., RADIUS-based authentication).

## Slide 6: Absolute requirements (4)
Security framework authentication mechanisms must fit within the designated multi-media authentication and re-authentication time budget.
Security framework must strongly protect keys and passwords from recovery by eavesdropper

## Slide 7: Absolute requirements (5)
Security framework must scale to:
  Simple, “self-managing” or “unmanaged” environments (etc., home, SOHO)
  Enterprise environments (e.g., office campuses, factories)
  Ad hoc wireless LANs
  Public environments (e.g., hotels, public services)
Any proposal that allows for more than one algorithm must support negotiation to a common algorithm

## Slide 8: Relative requirements (1)
Security framework should cause minimal computational expense consistent with meeting other requirements.
Security framework should use public and/or standard algorithms to the greatest extent possible
Security framework should minimize the number of mandatory cryptographic algorithms conformant

## Slide 9: Relative requirements (2)
Security framework should make no assumption whether peer authentication is machine or user authentication, as different organizations will establish different policies regarding who or what is authenticated