## Slide 1
QoS MAC Evaluation
Wim Diepstraten - Lucent
Amar Ghori -ShareWave
Steven Gray - NOKIA
Maarten Hoeben - No Wires Needed Bob Miller - AT&T
Gregory Parks - ShareWave
Harry Worstell - AT&T

## Slide 2
Suggested QoS MAC Evaluation Plan
Partition work into MAC performance evaluation and
system requirements activities
Choose simplistic approach for MAC evaluation---
  “Flat playing field” rather than real-world accuracy
  Accommodate widely varying MAC schemes
  Moderate and high loading excitations
    Low loading doesn’t need QOS
    Investigate “break points” of schemes
  Initially separate multi-BSS from QoS mediation tests
    Use media-based test results as “sanity check”
    for multi-BSS performance simulation output
    Allows both activities to proceed simultaneously
Use repeatable data sources (voice, streaming, best-effort)
using “canned” files with “drivers” emulating packet protocol

## Slide 3
Suggested Performance Envelope Bounds
Evaluate two speeds: 11 and 54 Mbps
Evaluate three data types:
  Voice - N 64Kbps PCM duplex channels (UDP-like)
  Streaming - N 3 Mbps MPEG channels (TCP-like)
  Streaming - N 128 kbps MP3 channels (TCP-like)
  Best-Effort - N 10 Mbps Internet channels (TCP-like)
Evaluate two loading points:
  50% of total raw PHY throughput
  85% of total raw PHY throughput
Incorporate multi-BSS extension as combination of
time-windowed QoS and time-division BSS @ S/N to
evaluate throughput
If access request is separate operation within the
protocol, test access success under above loading conditions.
Choose fixed number of stations (e.g.10)
Must specify STA/STA “side” traffic %

## Slide 4
Suggested Metrics
Throughput as % of raw PHY rate
Delay vs. Loading
  Voice
  Streaming
  Best-Effort
Throughput per Km2 (with specified overlap)