## Slide 1: 5-UP: A 5-GHz Unified Protocol
Proposed OFDM Extensions for Supporting Multiple Classes of Devices in 5 GHz Wireless LANs

## Slide 2: Agenda
Considerations for ensuring continued broad market appeal of existing 5-GHz WLAN standards
A concept for a future extension to 802.11a and Hiperlan2 that:
  Efficiently supports multiple classes of devices within a single unified wireless LAN
  Allows terminals of one type (Hiperlan2/5-UP or 802.11a/5-UP ) to participate in the other type of network
A proposal to further explore and standardize the concept

## Slide 3: A Vision for the Wireless Future
Transparent data, audio, and video connectivity between all computing and A/V devices in the office and the home
  Low cost
  High performance
  Simple and reliable
  Ubiquitous and standards-based
The vision for future wireless networking applications has the potential for strong appeal to a very broad market.

## Slide 4: Example: Home Network
Network
Interface Device
Broadband Access
To support the vision, it is desirable for a wireless LAN to provide a unified, multi-service network, supporting multiple device classes and usage models.

## Slide 5: 2.4GHz Protocols - Independently Developed for Specific Usage Models
802.11b HomeRF Bluetooth
Coded data rates 11 Mbps 1.6 Mbps 1.0 Mbps
End-user throughput 5.5 Mbps 0.8 Mbps 0.7 Mbps
Multimedia support No Audio Audio
Low-power operation No No Yes
Range 150ft. 150ft. 30ft.
True network Yes Yes No
Supports roaming Yes No No
Cost High Medium Low
Unfortunately, the protocols are incompatible with each other and can cause significant interference and inefficiencies if run simultaneously in the same location.

## Slide 6: 2.4GHz / 5GHz Industry Issues
2.4 GHz is being perceived as a band that will result in dissatisfied WLAN users as a result of spectrum overcrowding with incompatible protocols and interfering devices
At 5 GHz, Hiperlan2 and 802.11a have incompatible MAC/data link control (DLC) layers and neither adequately addresses the issue of low cost, low power, low speed devices
The entire WLAN industry loses if we let the 5 GHz band devolve into the same situation as the 2.4 GHz band.

## Slide 7: The Industry Opportunity - A Unified Protocol at 5GHz
Develop a single, compatible, evolutionary extension to both Hiperlan 2 and 802.11a that:
  Supports and extends both existing WLAN standards, and does not impede the delivery of first generation products based on those standards
  Allows for scalability in power, price and performance - 125 kbps through high rates (~100 Mbps)
  Allows devices with the extension to work in either an Hiperlan 2 or an 802.11a network
There is an opportunity to increase the appeal of existing standards today and expand their potential future applications.

## Slide 8: Goals for a 5-GHz Unified Protocol
Support high-rate WLAN applications (~100 Mbps)
Support a range of “low data rate” WLAN devices that trade data rate for low cost and power consumption
Support high and low speed multi-media traffic with guaranteed Quality of Service
Allow devices of all data rates to form ad-hoc networks
Operate as a single, backward-compatible enhancement to both 802.11a and HiperLAN2 so that existing development can proceed without delay

## Slide 9: 802.11a, HiperlanII
The unified protocol goals can conveniently be achieved by exploiting characteristics of the existing WLAN protocols
  802.11a and Hiperlan2 PHYs: Both 802.11a and Hiperlan II have nearly identical OFDM PHYs which use 52 carriers in a 20MHz BW
  802.11a and Hiperlan2 DLC/MAC features can be used to enable operation of the 5-UP protocol

## Slide 10: 802.11a/HiperLAN2 OFDM PHYs
802.11a and HiperlanII have very similar OFDM PHYs:
20 MHz channel is divided into 52 carriers (48 carry data, 4 are pilot signals) -- all 52 carriers are always used
Data rates from 6 Mb/s to 54 Mb/s are supported by varying modulation and error correction coding
Each carrier is ~300kHz wide, giving raw data rates from 125kb/s to 1.5Mb/s
...
20 MHz
52 Carriers total
One Channel (detail)
20MHz OFDM channels in 5 GHz band
Each carrier is ~300kHz wide

## Slide 11: Concept for Scalable Communications
+
The 5-UP concept extends the OFDM system to support multiple data rates and usage models.
  A device can easily omit selected carriers from the OFDM spectrum
  Low data rate devices can occupy the frequency slots that were omitted by other nodes
  OFDM frequency spacing provides excellent isolation between signals
64x64
complex
iFFT
and multiplexer
250kb/s
DAC
10 bits
DAC
10 bits
90
filter
filter
0
.
.
.
Laptop
0
250kb/s
250kb/s
0
52 Carriers
20 MHz
Carriers omitted by laptop
250kb/s
PDA
VoIP
Cordless Phone

## Slide 12: Examples for 5-UP Nodes
Data Rate Applications Carriers Modulation
125 kbps Cordless phone, 1 BPSK
remote control
1.5 Mbps High fidelity audio 2 or 4 16-QAM or QPSK
12Mbps MPEG2 video, DVD, 12, 16, or 32 64QAM, 16QAM, or QPSK
satellite, cable modem,
xDSL, data network
20Mbps HDTV, future cable 18, or 27 64QAM, 16QAM
modem and xDSL 13
The 5-UP approach provides options to efficiently meet data-rate requirements of key applications.

## Slide 13: Examples of Node Complexity and Power vs. Data Rate
The 5-UP approach also should achieve the desired objective of devices whose power and complexity scale with data rate.
* TX power based on lower 100 MHz of US UNII band

## Slide 14: 5-UP Operation and DLC/MAC Co-existence
A 5-UP time period supports nodes that might need fewer than 52 carriers
Allocation of 5-UP time periods is managed by the Primary MAC
Operation within the 5-UP time period is managed by the 5-UP MAC and beacon
Terminals with 5-UP can operate in any network that supports the 5-UP extension
time
5-UP beacon 52
5-UP beacon 51
5-UP beacon 1
...
carrier 1
...
carrier 51
carrier 52
...
52 frequency
channels
carrier 1
carrier 51
carrier 52
Downlink Period Uplink Period
one 5-UP time period
Primary
MAC
Primary
MAC
Notes: Page <number>
        <footer>
<header>
07/28/26 10:22 AM

## Slide 15: 5-UP Extension Summary
5-UP is a solution which can answer some of the key concerns with wireless LANs and help speed the expansion of the industry.
Scalability
  Channel is split into 52 dynamically allocated sub carriers
  Scalable cost, power, and bandwidth: 125kb/s to high rates
  Interoperability for all devices
  Efficient bandwidth utilization
Efficiently supports QoS for cordless phones to video applications
Addresses interoperability concerns - mobile terminals can work in either 802.11a or Hiperlan2 networks

## Slide 16: What are we Proposing?
Presentations to both the ETSI BRAN and IEEE 802 proposing study groups from each organization which would work together to develop a common extension to both standards
  ETSI BRAN Hiperlan2 plenary on 6/29/00
  IEEE 802.11/802.15 on 7/12/00
  IEEE 802.11 plenary on 7/13/00
  ETSI BRAN Hiperlan2 plenary 10/00