## Slide 1: 5-GHz Unified Protocol (5-UP) Proposal OFDM Extensions for 802.11a
Bill McFarland, billm@atheros.com
Greg Chesson, greg@atheros.com
Carl Temme, ctemme@atheros.com
Atheros Communications

## Slide 2: 5-UP Objectives
Expand Wireless LAN applications space
  Achieve 100 Mb/s data rate
  Enable low-cost, low-power, low-speed radios
  Improve QoS and scalability
Provide coexistence and interoperability
  Between low-end and high-end devices
  Between legacy and extended systems
  Compatible extensions to 802.11a and HiperLAN2

## Slide 3: Overview
More channels for more bandwidth
Carrier groups for bandwidth sharing
Single-carrier for low power/cost/speed
Unified MAC for range of applications

## Slide 4: Increased Bandwidth
No changes to existing PHY
  Identical carriers, OFDM, pilots, modulation, etc.
  Use 2 adjacent OFDM channels: 108 Mb/s
  Potentially more than 2 channels
Make compatible with single-channel systems
  Replicated beacons and protocols
  AP/Stations operate in both dual/single modes
  Build upon (expected) DFS extensions

## Slide 5: 5-UP Mode for 802.11a
Carrier groups
5-UP Beacon
Single-carrier devices
Range
Robustness
PHY issues: frequency lock, power
Topology
MAC protocol concepts

## Slide 6: Carrier Groups
Each group includes 1 or more carriers.
Group ID assigned by AP.
ID’s appear in beacon.
Multiple-carrier: OFDM with selected bins nulled.
Single-carrier: less complex, low-power/cost/speed.
Simultaneous transmission of carrier groups.
Downlink Uplink
5-UP
Beacon
}
}
}
}
}
}
Carriers Groups IDs
0
1
2
3
4
5
0
1
2
3
4
5

## Slide 7: 5-UP Beacon
PCF Beacon reserves media time for 5-UP mode.
5-UP Beacons control carrier group transfers.
Polled data transfers.
TDMA also possible.
Downlink Uplink
carriers
PCF 5-UP
Beacon Beacons
DCF Period
DCF Period

## Slide 8: One 5-UP Period
Downlink Uplink
1 carrier
1 carrier
1 carrier
1 carrier
20 carriers
24 carriers

## Slide 9: Proposed Carrier Usage
Hop on all carriers.
Same sequence for all carriers.
Several possible algorithms.
Hybrid of hopping and OFDM techniques
0
1
2
3
4
5
3
4
5
0
1
2
3
3
4
5
0
1
2

## Slide 10: Range
FCC rules limit power spectral density.
All devices scale power with the number of carriers.
Single carrier radios transmit with 1/52nd the power of standard 802.11a radios and would have similar range.
Use multiple carriers for greater range.

## Slide 11: Robustness
Multi-path does not generate intersymbol interference (with OFDM): rather, it creates fading.
Hopping of carriers can prevent long fades or interference problems.
Fading can also be reduced with antenna diversity.

## Slide 12: PHY Issues
Frequency Lock
  Need sufficient orthogonality for OFDM
  Transmitters lock to AP carrier frequencies
  Receivers track each carrier
Symbol Timing
  Alignment must preserve guard intervals
  Both open-loop and closed-loop solutions are possible
Power Control
  Needed for uplink
  Use open-loop control scheme

## Slide 13: Topology
5-UP mode controlled by AP.
5-UP stations communicate via AP.
Ad-hoc mode requires either master election, or a protocol subset profile.
Peer to peer (direct link) possible, but complex for multiple simultaneous pairs

## Slide 14: 5-UP MAC Concepts
Control Channel
  At least one logical carrier for DCF uplink
  Used for management and control
Data Channel
  (simplified) DATA frames on remaining carriers
AP assigns ID for device/carrier group
Poll via 5-UP Beacon (look for ID)
Potential for multiple 5-UP Beacons/PCF

## Slide 15: Summary
Carrier groups can be added to 802.11a
  Additional capabilities for OFDM radios
  Enable low-power/cost/speed devices
108 Mb/s data rate (or more)
Improved QoS
  Bandwidth assignments via carrier groups
  Fewer slots leads to lower jitter, less overhead
Unified approach to expand the market for wireless LANs