## Slide 1: IEEE 802.11e QoS Application Scenarios
Arun Ayyagari, Yoram Bernet, Tim Moore, Victoria Poncini
Microsoft Corporation

## Slide 2: Signaling Scenario
Quantitative applications
  indicate the type of service they need
  quantify resources at that service level
Network devices along the route
  review request
  check for resource availability
  may apply policy check
  may install state to recognize flow (RSVP)
  approve/deny request
  adjust resource availability

## Slide 3
SBM
Directory
Differentiated Service Network(s)
IEEE 802.11
Network
AP

## Slide 4
3. QoS service provider sends RSVP PATH message to network
1. Application indicates that it is a QoS sender
TCP/IP
NetCard
WinSock2 API
QoS-aware application
2. QoS SP invokes non-greedy traffic control
QoS SP
Traffic Control API
Packet Scheduler
MAC SAP
NDIS

## Slide 5
SBM
Directory
4. PATH message arrives at router
5. Router applies sender policy check against directory
Differentiated Service Network(s)
IEEE 802.11
Network
6. Sender approved, PATH forwarded to next router
7. Next router applies sender policy check against directory
8. Sender approved, PATH forwarded to Diff-Serv ingress router
9. Diff-Serv ingress router checks for admissibility against SLA
AP

## Slide 6
SBM
Directory
10. Resource request approved, PATH propagated transparently through Diff-Serv network
11. PATH arrives at campus network ingress router
Differentiated Service Network(s)
IEEE 802.11
Network
12. Router applies sender policy check against directory
13. Policy check approved, PATH forwarded to receiving host
AP

## Slide 7
15. Application indicates that it is a Qos receiver
14. PATH message arrives at QoS SP
16. QoS SP sends RSVP RESV message to network
QoS SP
TCP/IP
NetCard
WinSock2 API
QoS-aware application
NDIS
Packet Scheduler
MAC SAP

## Slide 8
SBM
Directory
Differentiated Service Network(s)
IEEE 802.11
Network
17. RESV message reaches first router
18. Router checks resource availability and admits resource request
20. Admitted RESV is forwarded to next router
21. Router checks resource availability and applies receiver policy check against directory
22. Checks approved, RESV forwarded
AP

## Slide 9
SBM
Directory
Differentiated Service Network(s)
IEEE 802.11
Network
23. RESV message forwarded transparently through Diff-Serv
24. Receiver policy check may be applied at Diff-Serv edge
25. RESV is forwarded to campus egress router
26. Router applies internal resource check and receiver policy check against directory
27. Checks approved, RESV forwarded
AP

## Slide 10
SBM
Directory
Differentiated Service Network(s)
IEEE 802.11
Network
28. Next router applies internal resource check and receiver policy check against directory
29. Checks approved, RESV forwarded to SBM
SBM applies resource check on behalf of AP (Note: SBM could be co-located with AP)
31. SBM approves resource check, RESV continues back to sender
AP

## Slide 11
32. RESV message arrives from network, indicating successful admission control
33. QoS SP indicates successful admission control to application
TCP/IP
WinSock2 API
QoS-aware application
34. QoS SP invokes greedy traffic control (marking)
Traffic Control API
QoS SP
NetCard
35. Transmitted data is marked high priority
Packet Scheduler
MAC SAP
NDIS
Packets tagged with DSCP by RSVP

## Slide 12
Differentiated Service Network(s)
IEEE 802.11
Network
Packets passing through AP and switch are allotted resources based on 802.1p marking
Packets passing through RSVP capable routers are allotted resources based on classification information conveyed in RSVP messages
Packets passing through Diff-Serv network are allotted resources based on DS-field (TOS) marking
AP/SBM

## Slide 13: What to Expect
Non-greedy traffic control (e.g. shaping) always applied immediately
Greedy traffic control (priority boost) applied after network approves
  unless overridden by network administrator
  best effort until then
Application will be notified upon network approval/denial
Denial of reservation does not prohibit sending, just means no QoS assurance

## Slide 14: Service Types
Best effort = DCSP of 0
  Default flow
  Not typically requested by applications
  Low priority
  Typically borrows from other flows
Controlled load = DCSP of 5 or 3
  Gets service equivalent to lightly loaded network
  Medium priority
Guaranteed service = DCSP of 5 or 3
  Guaranteed delay bounds
  Highest priority

## Slide 15: RSVP Token Bucket Parameters
Token bucket specification (TSpec)
  Token rate
    Bytes of IP datagrams per second (1 bytes per second to 40 terabytes per second)
  Bucket depth
    Bytes (1 byte to 250 gigabytes)
  Peak traffic rate
    Bytes of IP datagrams per second (1 byte per second to 40 terabytes per second)
Minimum policed unit
  Bytes
Maximum packet size
  Bytes
Resource specification (RSpec) – for guaranteed service
  Required service rate
    Greater than or equal to token rate
  Slack term
    Difference between desired delay and the delay obtained using the required service rate

## Slide 16: QoS for Qualitative Applications

## Slide 17
For qualitative QoS, traffic is marked for high priority without negotiating with the network = DCSP of 5 or 3
  no a-priori knowledge of traffic routes
  no knowledge of traffic volume
Example, use IEEE 802.1p marking

## Slide 18
Network management applications call TC API = DCSP of 7
  configure priority, shaping on behalf of application
    classification according to port, address, protocol
  open loop - must be based on estimates of traffic patterns, statistics, and heuristics
Example, use average rate, peak rate, and burst size

## Slide 19
TCP/IP
NetCard
WinSock2 API
QoS-aware application
QoS SP
Traffic Control API
Packet Scheduler
MAC SAP
NDIS
TCP/IP
NetCard
QoS-aware application
Packets tagged with DSCP by RSVP
Packets tagged with DSCP by Application can be 802.1p or BE
RSVP Signaled Quantitative and Qualitative: Guaranteed or Controlled Load or BE
Non-RSVP Signaled Qualitative: 802.1p or BE