## Slide 1: Transmitter Power Control (TPC) for 802.11 WLAN - Rev.1
Mika Kasslin and Antti Lappeteläinen
Nokia Research Center

## Slide 2: Outline
Why a TPC?
The ERC requirements
TPC for 802.11
  A method for PCF
  A method for DCF
  Frame format modifications

## Slide 3: Why a TPC?
RLANs can be deployed in 5 GHz band in CEPT countries under certain conditions
  European Radiocommunications Committee (ERC) decision ERC/DEC/(99)23
    Power limitations, indoor vs. indoor+outdoor
    Transmitter Power Control (TPC)
    Dynamic Frequency Selection (DFS)
STA power dissipation, system capacity, etc.

## Slide 4: The ERC requirements
Designated bands
  5150-5350 MHz for indoor use, mean EIRP limited to 200 mW
  5470-5725 MHz for indoor and outdoor use, mean EIRP limited to 1 W
TPC process required
  both in up- and downlink to reduce the interference effect caused by RLANs under the coverage area of a satellite
  to ensure a mitigation factor of at least 3 dB on the average output power

## Slide 5: Proposed method
Different schemes for CP and CFP
  A common power limit for CP
  STA-specific power limitation for CFP
  Apply mainly to uplink
In downlink AP's transmission power has to be adjustable
  Algorithm beyond the scope of the standard
  Relatively slow adjustments with small steps preferred

## Slide 6: TPC for CFP (1/2)
New control signals conveyed in
  BeaconTxP in Beacon management frames
  TxP in Poll data frames
AP
STA
AP's transmission power
- broadcasted regularly
Normal frame transmission
- "background" process
STA-specific power correction
- unicast frame
TPC process
TPC process
- Adjust own
TxPower
- Determine
STA-specific
correction
term
- Determine
own TxPower
as
AP_TxP + Corr

## Slide 7: TPC for CFP (2/2)
AP determines its own transmission power "freely"
  accuracy requirements in the standard?
TxP determination
  RSSI
  PER
  QoS
  etc.

## Slide 8: TPC for CP
Only upper power limit
  BeaconTxP in beacons
  Power adjustment needed also in IBSS
AP/1st STA
STA
AP/1st STA's transmission power
- broadcasted regularly
TPC process
TPC process
- Adjust own
TxPower
- Determine
own TxPower

## Slide 9: Frame format modifications (1/2)
No new frames required
New fixed field for BeaconTxP in beacon frames
How about defining BeaconTxP as AP_TxP in HIPERLAN/2?
  -15-30 dBm covered by 4 bits

## Slide 10: Frame format modifications (2/2)
Duration/ID field used to signal TxP
  Data + CF-Poll, Data + CF-Ack + CF-Poll and CF-Poll

## Slide 11: Adjusting TxP in DL
A mechanism to adjust AP's transmission power in a range of few decibels, e.g. 6 dB
Totally up to the manufacturer to decide how many power levels and which ones are used

## Slide 12: Adjusting TxP in DL - cont.
Basic rules:
  adjustments on a frame-by-frame base (i.e. in the beginning of the CFP)
  max 3 dB between consecutive frames
  upper limit (e.g. 9 dB) for the cumulative power changes over several frames

## Slide 13: Summary
TPC required in 5 GHz in CEPT countries
  both up- and downlink
  3 dB mitigation
TPC tailored for 802.11
  STA-specific power control for PCF
  Common power limitation for DCF
  Modifications to the existing frames
Basic rules for TPC in DL