## Slide 1: TGe Metrics & Criteria Ad Hoc Group Summary Report
Gregory H. Parks
ShareWave, Inc.
Greg.Parks@ShareWave.com

## Slide 2: Participants over five teleconferences
Peter Ecclesine
Greg Chesson
Keith Amann
Mathew Sherman
Tim Godfrey
TGe Functional Requirements ad hoc group
  Various participants

## Slide 3: Contents
References & Objectives
General Considerations
Traffic Models & Priorities
Topological Models
Static and Dynamic Loading and Handoff
Throughput, Latency & Jitter
Other Considerations
Next Steps

## Slide 4: References
Companion Document
  00/143r3
Other references tbd

## Slide 5: Objectives
Come up with a set of Metrics and Criteria which will serve as a uniform set of simulation cases against which we can compare proposals
Desire to create the smallest set of cases that cover the broadest range of capabilities in order to limit simulation cases and time spent simulating cases
(tbd) Use some portion of the set of Metrics and Criteria as functional requirements that any proposal must meet

## Slide 6: General Considerations
Simulation model
  OpNet-based common model
  Common parameterization pre-determined
Traffic generator
  Common to OpNet and to empirical testing
    Allows validation of simulation model through empirical testing
Measurement points
  Utilization & Throughput: On the channel
  Latency & Jitter: At the receiving STA

## Slide 7: Physical Layer
802.11b 11 Mbps
  Using optional short headers
802.11a 54 Mbps
  Qualifiers tbd
Error rates and distributions will be determined from the simulation channel model chosen by the Simulation ad hoc group and approved by the Metrics and Criteria ad hoc group

## Slide 8: Traffic Models
Voice stream
  CBR: Two simultaneous opposite-directional (duplex) ADPCM streams each 50 64-byte pps (20ms framing) or 100 32-byte pps (10ms framing)
MP3/low quality video stream
  CBR: 1000 128-byte pps (simplex 128Kbyte/s)
MPEG2/medium quality video stream
  CBR: Tbd 1504-byte pps (simplex 4Mbit/s)
  VBR: 0 – 4 Mbit/s sinusoidal(?) 5 sec period, CBR additive

## Slide 9: Traffic Models (cont.)
High quality video stream (~20Mbps)
  Need as separate from MPEG2 is tbd
  Substitute with 2 MPEG2 streams(?)
Bulk data stream
  CBR: 60% 64-byte packets
  CBR: 20% 568-byte packets
  CBR: 20% 1500-byte packets
  Issued rate varies with desired overall MAC load
1394 traffic stream
  Need as a separate traffic model is tbd

## Slide 10: Priorities & Admittance
It is assumed that 8 priorities can be specified
Tagging of traffic models with priority information is tbd
Use of these priorities is up to the MAC proposal
Response to bandwidth available RSVP/SBM requests is up to MAC proposal

## Slide 11: Topological Models
BSS Topologies
Node Topologies
Stream Topologies

## Slide 12: BSS Topologies
Three BSSs with APs arranged along a line segment
Each BSS is partially overlapped (to an extent tbd) with any adjacent BSS
The two BSSs at the extremes of the line along which they are arranged are overlapped to the extent that each can detect as interference the others’ headers and preambles but not the others’ data
Each BSS is loaded with the same traffic type and amount with the exception of the traffic incurred during implementation the handoff loading model

## Slide 13: Node Topologies
Model 1:
  1 AP, 2 STAs, and 1 open STA location equally spaced around the periphery of a circle of radius tbd with the AP located at the center (?) of the circle
Model 2:
  1 AP, tbd STAs, and 1 open STA location equally spaced around the periphery of a circle of radius tbd with the AP located at the center (?) of the circle
    The number of STAs is determined from the number of streams to be transported, where no more than 2 simplex or duplex streams are allowed between any one pair of STAs

## Slide 14: Stream Topologies
Stream Topology 1:
  Distributed evenly amongst 3 STAs except for the MPEG2 streams, if required, one of which is to be distributed between any two non-AP STAs and the other two(?) of which are to be multicast from the AP to any two non-AP STAs
Stream Topology 2:
  No more than 2 simplex or duplex streams between any two STAs; the exact topological distribution is tbd except for the MPEG2 streams, if required, one of which is to be distributed between any two non-AP STAs and the other two(?) of which are to be multicast from the AP to any two non-AP STAs

## Slide 15: Loading Models
Static Loading
Dynamic Loading
Handoff Loading

## Slide 16: Static Loading Models
All models include 50%, 85% & 125% loading
50%, 85% loading are defined as the amount of combined loading at each STA which is expected to result in an air time occupancy of close to the specified amount given an estimate of the efficiency of the MAC.
Primary control of loading is variability of bulk data
50% is required(?); 125% loading is pathological case
Differences between measured occupancies will indicate differences in efficiency between proposals

## Slide 17: Static Loading Models (cont.)
Model 1: 11 Mbps #1 (some enterprises)
  6 duplex voice, 0(?) MP3, 0(?) MPEG2
  remainder is bulk data distributed equally between STAs
Model 2: 54 Mbps #1 (some enterprises)
  6 duplex voice, 0(?) MP3, 0(?) MPEG2
  remainder is bulk data distributed equally between STAs

## Slide 18: Static Loading Models (cont.)
Model 3: 11 Mbps #2 (some homes)
  3 voice, tbd MP3
  1 MPEG2 between 2 non-AP STAs
  remainder is bulk data distributed equally between STAs
Model 4: 54 Mbps #2 (some homes)
  3 voice, tbd MP3
  1 MPEG2 between 2 non-AP STAs
  2 MPEG2 multicast from AP to two STAs
  remainder is bulk data distributed equally between STAs

## Slide 19: Dynamic Loading Models
Static Loading Model, quiescent @85%
  Add a new STA to the BSS (authenticate and associate)
  Add a new bi-directional voice stream between the newly associated STA and a different non-AP STA
Determine
  Can the connection be made
  How long does the connection take to be made
  How does the addition of this STA and stream affect the rest of the quiescent system

## Slide 20: Handoff Loading Models
Dynamic Loading Model, quiescent @85%
  Move the dynamically added STA from the current BSS to an adjacent BSS, also moving the voice stream currently associated with that STA (disassociation, authentication, reassociation)
  Move with the BSS on the same channel, and with the BSS on a different channel (?)
Determine
  Can the handoff be made
  How long does the handoff take to be made
  How does the deletion and addition of this STA and stream affect the handed-off stream and the rest of the quiescent systems

## Slide 21: Throughput
Stream throughput determined by type of traffic issued to and delivered by STA
  Voice – defined by traffic model
  MP3 – defined by traffic model
  MPEG2 – defined by traffic model
  Bulk Data – measured, not defined
Overall throughput (MAC efficiency) will be determined from the data carried during packet rate achieved at defined loadings measured on the channel

## Slide 22: Latency
Latency is defined to be the duration between the time a packet is enqueued at the input to the source STA and dequeued at the output from the destination STA
  Voice – 20mS max for STA-to-STA in BSS, 300ms overall round-trip delay budget (ITU)
  MP3 – tbd mS max
  MPEG2 – tbd mS max
  Bulk Data – no requirement

## Slide 23: Jitter
Jitter is defined to be the statistical distribution of variation in the arrival time of an individual packet at the destination. Jitter applies largely to constant packet rate traffic and should generally be no greater than ½ the time between adjacent packets in a stream assuming the packet under study is centered in time between the two adjacent packets
  Voice – Gaussian distribution, +/- tbd mS @ 2 sigma
  MP3 – Gaussian distribution, +/- tbd mS @ 2 sigma
  MPEG2 – Gaussian distribution, +/- tbd mS @ 2 sigma
  Bulk Data – no requirement

## Slide 24: Other Considerations
Overlapping BSSs
  See BSS topologies
Dynamic Frequency Selection
  No expected need to be simulated
Transmit Power Control
  Need for simulation should be discussed

## Slide 25: Next Steps
Decide whether this document and companion document #143 will serve as baseline documents
  If so, decide what remains to be modified or completed in these documents, and with what process and priority, in order to move toward a complete document
  If not, decide how else to proceed to baseline documents
    Either continue to modify this document
    Or, create a new document