## Slide 1
Technical Feasibility of OFDM for HRb
Mark Webster, Steve Halford and Carl Andren
Intersil Corporation
July 2000

## Slide 2
Why Consider OFDM for 802.11 HRb?
OFDM was selected as the best high-rate waveform by both IEEE 802.11a and HIPERLAN BRAN
OFDM was considered superior for providing multiple high-data-rates with reasonable complexity while providing good performance for both high-multipath and low-SNR conditions.
FCC processing-gain capability for OFDM is equivalent to other modulations being considered for HRb.
Reuse of 802.11a would speed HRb to market.
Provides standards harmonization: 802.11a, HIPERLAN and, now (?), 802.11 HRb

## Slide 3
Multiple HRb OFDM Options Exist
Options
1. Use the 802.11a symbol structure and 20 MHz timing unmodified. This requires a 802.11b/HRb clock change from 11 MHz to 20 MHz.
2. Use the 802.11a symbol structure, but use 22 MHz timing.
This requires a 802.11b/HRb clock change from 11 MHz to 22 MHz.
3. Change the # of pilots from 52 to 48 and use 22 MHz timing. This reduces the spectral occupancy slightly.
4. Use 22 MHz sampling but change guard interval from 16 to 24 samples. This maintains the 802.11a’s data rates.
5. Etc.
This presentation addresses only option 2,
since it appears to be the simplist for HRb.

## Slide 4
Key Features
Use 802.11a’s OFDM symbol structure unmodified.
Stay consistent with 802.11b’s chip rate of 11 MHz.
For HRb OFDM, increase 802.11a’s 20 MHz sample rate by 10% to 22 MHz, which is double the 802.11b chip rate.
Provides data rates 10% higher than 802.11a’s: 6.6, 9.9, 13.2, 19.8, 26.4, 39.6, 52.8, 59.4 Mbps.
Spectrum is 10% wider than 802.11a’s.

## Slide 5
802.11a and 802.11 HRb Comparison Matrix
Modifications to 802.11a’s parameters are shown in red.
Trade Matrix

## Slide 6
OFDM Symbol Using
20 MHz Sampling Fundamental
16
Samples
64
Samples
IFFT/FFT SPAN
Guard
Interval
4 usecs OFDM Symbol
312.5 KHz Tone Spacing
52
Subcarriers
. . .
frequency
time
802.11a OFDM Symbol
20 MHz x 4 usecs = 80 samples
IEEE 802.11a
~16.25 MHz
Notes: Page <number>
        <footer>
<header>
<date/time>
This slides describes the OFDM waveform for the first idea for generating OFDM as appended to an 802.11b preamble. Here the OFDM symbol structure is totally identical to the 802.11a standard, where the fundamental sample rate is 20 MHz.
Notice that this scheme has 16 samples in the guard interval. The guard interval is discard in the receiver, since it is only a buffer between successive OFDM symbols. The buffering allows the receive to not use an equalizer. Equalizers are very complex, which motivates the use of OFDM.

## Slide 7
OFDM Symbol Using
22 MHz Sampling Fundamental
16
Samples
64
Samples
IFFT/FFT SPAN
Guard
Interval
343.75 KHz Tone Spacing
52
Subcarriers
. . .
frequency
time
HRb OFDM Symbol
3.63 usecs OFDM Symbol
80 samples / 22 MHz = 3.63637 usec
IEEE 802.11a
but 22 MHz
clock
~17.875 MHz
Notes: Page <number>
        <footer>
<header>
<date/time>
This is a second idea which uses a fundamental sample rate of 22 MHz, which is different than 802.11a’s 20 MHz.
The motive for this is the 802.11b signal uses a sampling fundamental to 11 MHz, or integer multiples thereof. In this OFDM case, both signals are related to 11 MHz sampling, which simplifies the baseband processor.
To handle the change to 22 MHz OFDM, the simplest idea is to merely put 8 extra samples in the guard interval. These 8 extra samples can be merely discarded in the receiver, with the rest be identical to 802.11a encoding/processing.

## Slide 8
fc
9
20
30
11
-11
-9
-30
-20
-20 dBr
-28 dBr
-40 dBr
SPECTRAL MASKS
802.11b
Spectral
Mask
802.11a
Spectral
Mask
802.11b is
Slightly More
Restrictive
Spectral Masks Appear Compatible
Out-of-band regulatory restrictions are extra
Comparing 802.11a and 802.11b’s Spectral Masks
Notes: Page <number>
        <footer>
<header>
<date/time>
The big question remains before making this proposal to use OFDM sound. Are the spectrums compatible. This impacts cell layout within a building, and we do not want to harm existing cell plans within buildings designed around the 802.11b spectrum. Adjacent channel interference is the key concern.
Shown is the spectral mask for 802.11a and 802.11b. This shows they are nearly identical. No significant harm should result from the use of OFDM.

## Slide 9
fc
9.9
22
33
12.1
-12.1
-9.9
-33
-22
-20 dBr
-28 dBr
-40 dBr
SPECTRAL MASKS
Corresponding HRb OFDM Spectral Mask

## Slide 10
20 MHz
25 MHz
802.11b
Channel
Spacing
802.11a
Channel
Spacing
Channel Spacing
802.11b is
More
Loose
Channel Spacings Appear Compatible
frequency
frequency
2.4 GHz Frequency
Plans Remain
Unmodified
Comparing 802.11a and 802.11b’s Channel Spacings
Notes: Page <number>
        <footer>
<header>
<date/time>
The 802.11a and 802.11b standards suggest usable channel spacings. 802.11b suggests 30 MHz, but in practice folks generally use 25 MHz in the USA. 802.11a suggests 20 MHz, which is tighter than the 25-30 MHz of existing 802.11b systems.
Again, no harm should result from using OFDM as the high-rate waveform to extend 802.11b to higher data rates.

## Slide 11
HEADER
48 BITS
@ 2 Mbps
PREAMBLE
72 BITS
@ 1 Mbps
PSDU
SELECTABLE
@ 2, 5.5 OR 11 Mbps
HEADER
48 BITS
@ 1 Mbps
PREAMBLE
144 BITS
@ 1 Mbps
PSDU
SELECTABLE
@ 1, 2, 5.5 OR 11 Mbps
802.11b LONG PREAMBLE
802.11b SHORT PREAMBLE
96 usecs
192 usecs
1 and 2 Mbps uses 11 chip BARKER codes.
5.5 and 11 Mbps uses 8 chip CCK codes.
Chipping is at 11 MHz.
IEEE-802.11b PACKET STRUCTURE
Data Payload
CURRENT 802.11b PREAMBLES
Notes: Page <number>
        <footer>
<header>
<date/time>
802.11b already has a defined preamble/header structure for WLAN packets. We propose that the preamble/header be reused as is. We propose only modifying the payload portion of the packet with higher rate OFDM. This provides interoperability and coexistence with already deployed equipment. New highest-rate systems can communicate with existing older systems at 1, 2, 5.5 and 11 Mbps. However, new highest rate systems can communicate at the higher data rates without harm to older units, since the preamble is common.
The data rate and packet length is listed in the header. All units can receive the header.

## Slide 12
HRb OFDM PACKET STRUCTURE
HEADER
48 BITS
@ 2 Mbps
PREAMBLE
72 BITS
@ 1 Mbps
HEADER
48 BITS
@ 1 Mbps
PREAMBLE
144 BITS
@ 1 Mbps
802.11 HRb LONG PREAMBLE
802.11 HRb SHORT PREAMBLE
96 usecs
192 usecs
Data Payload
OFDM
SYNC
OFDM
SYNC
16 usecs
16 usecs
Service Field Bit
Denotes Switch to OFDM
Service Field Bit
Denotes Switch to OFDM
K usecs
PSDU SELECTABLE
OFDM Symbols
@ 6.6, 9.6, 13.2, 19.8, 26.4, 39.3, 52.8 or 59.4 Mbps
PREAMBLES for 802.11 HRb:
Reuse 802.11b preambles
Use 802.11a’s OFDM
sync pattern
Data rate
# bytes of data
OFDM
Signal
4 usecs
OFDM
Signal
4 usecs
PSDU SELECTABLE
OFDM Symbols
@ 6.6, 9.6, 13.2, 19.8, 26.4, 39.3, 52.8 or 59.4 Mbps
Notes: Page <number>
        <footer>
<header>
<date/time>
To run the current rates of 1, 2, 5.5 and 11 Mbps, everything remains as in 802.11b.
To operate at the new data rates, the header denotes the higher mode. After the header would follow the 802.11a sync pattern, which is only 16 usecs long. This sync pattern is used for initialization of the key OFDM subsections. The 802.11a waveform has a segment called SIGNAL to convey data rate and packet length. This is not necessary, since the 802.11b header conveys the same information at a robust 2 Mbps. The payload would be the same as the 802.11a DATA waveform segment.

## Slide 13
802.11b
HEADER
802.11b
PREAMBLE
OFDM
SYNC
16 usecs
OFDM
Signal
4 usecs
t1 t2 t3 t4 t5 t6 t7 t8 t9 t10
G12
T1
T2
8 usec
8 usec
802.11b Premable/Header OFDM Sync Detail
Short Sync
Long Sync
Signal Detection
AGC
Diversity
Coarse Freq Estimation
Timing Synchronization
Channel Estimation
Fine Freq Estimation
Channel Estimation
Signal Detection
AGC
Diversity
Coarse Freq Estimation
Timing Synchronization
QUESTIONS
1. Are short and
long OFDM
syncs necessary?
2. Are they
preferred?

## Slide 14: Packet Structure for Long Preamble with OFDM Header: Standard Mode
Sync
SFD
Header
MPDU: X Bytes
Ack
# Bits:
Rate:
Time:
128 bits
1 MBPS
128 usec
16 bits
1 MBPS
16 usec
48 bits
1 MBPS
48 usec
8*X bits
R MBPS
8*X/R usec
3 symbols
6 MBPS
12 secs
This mode uses both IEEE 802.11b Long Preamble
and IEEE 802.11a Preamble to acquire all
necessary OFDM parameters
Throughput = 8*X Mbps/ (128+16+48+20 + 8*X/R+10+128+16+48+ 20 +12) usec
10 usec
IFS
Standard IEEE802.11b
header
OFDM
Data Symbols
DATA BURST
ACK BURST
Short
Sync
Long
Sync
Signal
Standard
IEEE802.11a
Header
20 usec
Sync
SFD
Header
128 bits
1 MBPS
128 usec
16 bits
1 MBPS
16 usec
48 bits
1 MBPS
48 usec
Standard
IEEE802.11b
header
Short
Sync
Long
Sync
Signal
Standard
IEEE802.11a
Header
20 usec
OFDM
Ack
(Uses 3
OFDM symbols)

## Slide 15: Packet Structure for Long Preamble without OFDM Header: Fast Mode
Sync
SFD
Header
MPDU: X Bytes
Ack
Sync
SFD
Header
# Bits:
Rate:
Time:
128 bits
1 MBPS
128 usec
16 bits
1 MBPS
16 usec
48 bits
1 MBPS
48 usec
8*X bits
R MBPS
8*X/R usec
128 bits
1 MBPS
128 usec
16 bits
1 MBPS
16 usec
48 bits
1 MBPS
48 usec
3 Symbols
6 MBPS
12 secs
This mode uses IEEE 802.11b Long Preamble only to acquire all
necessary OFDM parameters
Throughput = 8*X Mbps/ (128+16+48+8*X/R+10+128+16+48+12) usec
10 usec
IFS
Standard IEEE802.11b
header
OFDM Data Symbols
DATA BURST
ACK BURST
Standard IEEE802.11b
header
OFDM Ack
(Uses 3 OFDM symbols)

## Slide 16
With-and-Without OFDM Sync
Long-Preamble Throughput Comparison

## Slide 17: Packet Structure for Short Preamble with OFDM Header: Standard Mode
Sync
SFD
Header
MPDU: X Bytes
Ack
# Bits:
Rate:
Time:
56 bits
1 MBPS
56 usec
16 bits
1 MBPS
16 usec
48 bits
1 MBPS
48 usec
8*X bits
R MBPS
8*X/R usec
3 symbols
6 MBPS
12 secs
This mode uses both IEEE 802.11b Short Preamble
and IEEE 802.11a Preamble to acquire all
necessary OFDM parameters
Throughput = 8*X Mbps/ (56 +16+48+20 + 8*X/R+10+56 +16+48+ 20 +12) usec
10 usec
IFS
Standard IEEE802.11b
header
OFDM
Data Symbols
DATA BURST
ACK BURST
Short
Sync
Long
Sync
Signal
Standard
IEEE802.11a
Header
20 usec
Sync
SFD
Header
56 bits
1 MBPS
56 usec
16 bits
1 MBPS
16 usec
48 bits
1 MBPS
48 usec
Standard
IEEE802.11b
header
Short
Sync
Long
Sync
Signal
Standard
IEEE802.11a
Header
20 usec
OFDM
Ack
(Uses 3
OFDM symbols)

## Slide 18: Packet Structure for OFDM Only Header: Super Fast Mode
Short Sync
Long Sync
MPDU: X Bytes
Ack
# Bits:
Rate:
Time:
8 usec
8 usec
8*X bits
R MBPS
8*X/R usec
3 Symbols
6 MBPS
12 usec
10 usec
8 usec
8 usec
Signal
IFS
4 usec
Short Sync
Long Sync
Signal
4 usec
This mode uses IEEE 802.11a Preamble to acquire all
necessary OFDM parameters
Standard IEEE802.11a
header
OFDM Data Symbols
DATA BURST
ACK BURST
Standard IEEE802.11a
header
OFDM Ack
(Uses 3 OFDM symbols)
Throughput = 8*X Mbps / (8+8+4+8*X/R+10+8+8+4+12)

## Slide 19
With-and-Without OFDM Sync
Short-Preamble Throughput Comparison

## Slide 20
HEADER
48 BITS
Signal Field only accommodates rates up to 25.5 Mbps ( 8 bits x 100 Kbps, so use a Service Field bit to denote data-rate extensions)
SIGNAL
8 BITS
SERVICE
8 BITS
LENGTH
16 BITS
CRC
16 BITS
HEADER DETAIL FOR HRb
Use a Service Field bit to denote OFDM mode.
Use a Service Field bit to denote data-rate extensions.
The Length Field is adequate, since measured in usecs.
OFDM proposal uses PSDU length in an integer number of usecs.
HRb SHORT/LONG-PREAMBLE
HEADER DETAIL
Unchanged
Notes: Page <number>
        <footer>
<header>
<date/time>
The header is identical in structure to 802.11b’s. 802.11b’s header already provides fields providing provision for extended data-rate performance. The field modifications are shown, and they are compatible with existing equipment.
The packet length field is fine unmodified, since the proposed OFDM packet length is an integer number of usecs. Free bits in the service can be defined to denote OFDM, recognizable to all equipment conforming to a new standard. Existing equipment is not harmed, since they can still decode the packet length.
The signal field only has 8 bits which cannot quantify a data rate above 25.5 Mbps. To achieve higher rates, the service field bit denoting OFDM can be used to denote the higher rates as quantified by the signal field.

## Slide 21
Data Payload
PSDU
SELECTABLE
@ 6, 9, 12, 18, 24, 36, 48 or 54 Mbps
SIGNAL
SYMBOL
Data Rate
# bytes of data
HRb OPTIONAL MODE: OFDM ONLY
OFDM
SYNC
16 usecs
4 usecs
Not interoperable/coexistent with 802.11b
PREAMBLES for 802.11 HRb:
Super-Short OFDM-only Preamble Option
Notes: Page <number>
        <footer>
<header>
<date/time>
If one wants to run purely OFDM at 2.4 GHz in a WLAN network which ignores (not coexistent and interoperable) with 802.11b equipment, a very short preamble can be defined as in 802.11a. The preamble would not be recognizable by existing 802.11b equipment.
With super-short preamble, the 802.11a SIGNAL segment is needed to denote packet length and data rate.

## Slide 22: Packet Structure for OFDM Only Header: Super Fast Mode
Short Sync
Long Sync
MPDU: X Bytes
Ack
# Bits:
Rate:
Time:
8 usec
8 usec
8*X bits
R MBPS
8*X/R usec
3 Symbols
6 MBPS
12 usec
10 usec
8 usec
8 usec
Signal
IFS
4 usec
Short Sync
Long Sync
Signal
4 usec
This mode uses IEEE 802.11a Preamble to acquire all
necessary OFDM parameters
Standard IEEE802.11a
header
OFDM Data Symbols
DATA BURST
ACK BURST
Standard IEEE802.11a
header
OFDM Ack
(Uses 3 OFDM symbols)
Throughput = 8*X Mbps / (8+8+4+8*X/R+10+8+8+4+12)

## Slide 23
Throughput of Super-Short Preamble

## Slide 24
Realistic Impairments and Considerations Not Included in This Throughput Analysis
Packet Errors cause retransmission.
Packet collisions
Integer data length requirement
Time for backoff to avoid collision
MAC Enhancements

## Slide 25
SIMULATION RESULTS
PERFORMANCE IN AWGN
1000 byte packet-error-rate vs. EbNo

## Slide 26
SIMULATION RESULTS
PERFORMANCE IN AWGN
1000 byte packet-error-rate vs. SNR

## Slide 27
Pa Backoff Example
Rapp Model p = 2
16 QAM Subcarriers
OBO 3.9 dB
PA BACK-OFF for OFDM
OFDM has Reasonable PA Backoffs
It is fairly easy to meet
the spectral mask.

## Slide 28
OFDM’s Large Peak Deviations are Rare
16 QAM Subcarriers
Theoretical Max
Peak-to-Ave Pwr:
22 dB
22 MHz sample rate