## Slide 1: Traffic Classes
Menzo Wentink
No Wires Needed,
An Intersil Company
menzo@nwn.com
The Netherlands

## Slide 2: Contents
IETF Subnet Bandwidth Manager (SBM)
QoS Taxonomy
Flow Aggregation
Additional MAC Enhancements for Traffic Class Support
Coexistence of TC and VSID Systems
Appendix A: The RSVP TCLASS object
Appendix B: Enhancements to Duration/ID field
Appendix C: Enhancements to Capability Information field
Appendix D: Coexistance of VSID’s and AID.TC’s
Appendix E: Advantages of using Traffic Classes

## Slide 3: In Short
This proposal describes a QoS system based on Traffic Classes (TC’s), in combination with the RFC 2814 SBM.
The DSBM controls the TC labeling through the RSVP TCLASS object (explicit TC mapping). Signalling and classification for TC’s take place outside the MAC and need not be standardised in 802.11e.
A polling based QoS system can be realised within the TC system, with small modifications to the Duration/ID field of FC-Poll and To-DS frames. No new frames are required. The polling based system can be enhanced with the mechanims of the joint proposal.
TC’s with SBM offer a lightweight QoS platform for priorities or a flow based QoS system.
This proposal ties into the Joint Proposal by interpreting the AID.TC as a VSID, which is a unique flow ID within a BSS. In particular, this means that the CC, TxOP, Multipoll, Delayed Ack, VSS, etc. can be applied in the TC system without changes.

## Slide 4: 1a. IETF Subnet Bandwidth Manager
SBM RFC’s
  RFC 2814 ‘SBM (Subnet Bandwidth Manager): A Protocol for RSVP-based Admission Control over IEEE 802-style networks’
  RFC 2815 ‘Integrated Service Mappings over IEEE 802 Networks’
  RFC 2816 ‘A Framework for Providing Integrated Services over Shared and Switched IEEE 802 LAN Technology’
SBM Functions
  Insert DSBM into the RSVP path
    The DSBM-Client redirects RSVP messages to the DSBM.
  Admission Control
    The DSBM decides if enough resources are available to accept a reservation.
  Traffic Class Signalling
    The DSBM can decide which TC label must be used by the sender, by adding a TCLASS object RESV messages (see Appendix A).

## Slide 5: 1b. RSVP without DSBM
AP
RESV
Data
PATH
Data
STA 2
STA 1
Sender
Receiver

## Slide 6: 1c. RSVP with DSBM
AP
PATH
Data
PATH
Data
RESV
RESV
DSBM-Client
STA 2
STA 1
DSBM-Client
Sender
Receiver
DSBM
Default TC Mapping
NC = 7
GS = 5
CL = 3
BE = 0
The default mapping is used. Communication between DSBM and AP is not required.

## Slide 7: 1d. SBM with Traffic Class Signalling
AP
PATH
RESV
DSBM
DSBM-Client
Data
PATH
RESV
+
TCLASS
STA 2
STA 1
DSBM-Client
Data
Sender
Receiver
The default TC Mapping is overruled by the DSBM.
The DSBM and the AP communicate about TC’s, FlowSpecs and available resources..

## Slide 8: 1e. SBM Properties
The SBM system consists of a DSBM with associated DSBM-Clients.
The DSBM-client inserts the DSBM into the RSVP path.
The DSBM performs Admission Control and prevents oversubscribtion of the Traffic Classes.
The DSBM can signal the TC which a sender must use, through the RSVP TCLASS object.
SBM can be used for priorities by using the default mapping and for flow based QoS systems by signalling the TC to the station.

## Slide 9: 2. QoS Taxonomy
Based on the desired complexity of the QoS system there are several scenario’s possible:
Priorities based system
  Solution: SBM with default TC mapping. The DSBM does not have to reside in the AP.
Per Flow QoS system with up to 7 upstream flows per station
  Solution: SBM with explicit TC mapping through TCLASS object.
Per Flow QoS with more than 7 upstream flows per station
  Solution 1: SBM with explicit TC mapping and flow aggregation.
  Solution 2: SBM with VSID’s

## Slide 10: 3. Flow Aggregation
The aggregate flow spec is the ‘sum’ of individual flow specs.
The definition of the ‘sum’ is implementation specific.
  Could be sum of mean rates and burst rates
The aggregate is scheduled according to the aggregate flow spec. Policing is performed at higher layers.
Not all flow types should be aggregated
  delay sensitive voice and bursty MPEG traffic do not combine very well inside an aggregate. The MPEG flow may influence (delay) the transmissions of voice frames.

## Slide 11: 4. Additional MAC Enhancements for Traffic Classes
Modifications to the Duration/ID field are needed to support TC’s in a polling based QoS system (see Appendix B).
  Stations must piggyback queue state information to the AP.
  AP’s must specify which TC is polled and for which TC more info is requested.
To-DS frames
  TCx-More-Data contains the queue state for TCx.
  TQ/NF-size provides detailed queue state for the requested TC, based on the TC-Info and TQ/NF fields of the preceding poll frame (see below).
CF-Poll, Data+CF-Poll, Ack+CF-Poll frames
  TC-Polled indicates which TC is polled.
  TC-Info indicates for which TC detailed info is requested by the AP.
  TQ/NF specifies whether Total Queue size or Next Frame size is required.

## Slide 12: 5. Coexistence of TC’s and VSID’s
TC systems can coexist with VSID systems if
  Flows in the TC system can be uniquely identified  AID.TC
  the VSID numbering scheme is designed to contain an AID.TC range (see Appendix D).
  the STA can indicate it’s capabilities (TC-capable or VSID-capable).
TC systems thus tap into the mechanisms of the Joint Proposal
  The VSID is chosen as AID.TC.
  Transmit Opportunities, Centralized Contention, Side Streams, Delayed Acknowledgements, etc. can all be applied without modifications.
  These channel access mechanisms of the Joint Ptoposal can be applied to enhance the proposed polling based TC system.

## Slide 13: Appendix A: The RSVP TCLASS Object
The TCLASS object specifies the TC value to be used for the particular traffic stream (taken from RFC 2814, Appendix B).
B.3.7. TCLASS Object
TCLASS object (traffic class based on IEEE 802.1p) uses object
class = 165.
0 1 2 3
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Length | 165 | 1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| /// | /// | /// | /// | PV |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Only 3 bits in data contain the user_priority value (PV).

## Slide 14: Appendix B: Enhancements to the Duration/ID field
Enhancements to the Duration/ID field in a TC and polling based QoS system
  The station piggybacks the queue state of each TC inside the sation on To-DS frames (TCx-More-Data).
  The station piggybacks on To-DS frames the Total Queue size or Next Frame size of one specific TC (TQ/NF-Size).
  The AP indicates on CF-Poll frames which TC is polled within the station (TC-Polled).
  The AP indicates for which TC it requests more detailed information (TC-Info).
  The AP indicates which information it needs, Total Queue size or Next Frame size (TQ/NF).
b0
b1
b2
b3
b4
b5
b6
b7
0 – 32767
b13 - b8
b14
Usage
DCF Duration.
0
TQ/NF-Size
(0 – 63)
TC0-
More-
Data
TC1-
More-
Data
TC7-
More-
Data
TC6-
More-
Data
TC5-
More-
Data
TC4-
More-
Data
TC3-
More-
Data
TC2-
More-
Data
1
To-DS frames (PCF)
TCx-More-Data signals the queue state for TCx. (0 = no data queued,
1 = data queued.)
TQ/NF-Size contains the Total Queue size or Next Frame size based
on TC-Info and TQ/NF values in polling frames (see below).
CF-Poll, Data+CF-Poll, Ack+CF-Poll frames
- TC-Polled indicates which traffic class is polled.
- TC-Info indicates for which traffic class queue state info is requested.
- TQ/NF indicates whether the requested info is the Total Queue size or
the Next Frame size (0 = Total Queue, 1 = Next Frame).
TC-Polled
(0 – 7)
0
1
b15
0
1
1
1 – 2007
AID in PS-Poll frames.
1
1
TC-Info
(0 – 7)
TQ/NF

## Slide 15: Appendix C: Enhancements to the Capability Information field
Stations indicate their QoS capabilities in the Capability Information field
  b5 and b6 not set: Station is not QoS capable
  b5 set: Station is TC Capable
  b6 set: Station is VSID Capable
  b5 and b6 set: reserved
b0
ESS
b1
IBSS
b2
CF
Pollable
b3
CF Poll
Request
b4
Privacy
b5
TC
Capable
b6
VSID
Capable
b7-b15
Reserved

## Slide 16: Appendix D: Coexistence of TC’s and VSID’s
The AID.TC value is a unique identifier of flows within a BSS, similar to the VSID. By defining the AID.TC range as a subset of the VSID range, both systems can coexist and use all of the channel access mechanisms of the Joint Proposal.
AID.TC is a 14 bits identifier (AID 11 bits + TC 3 bits = AID.TC 14 bits).
VSID
16384 – 65535
b13-b0
AID.TC
0 – 16383
b15-b14
0
b13-b3
AID
0 – 2007
b2-b0
TC
0 – 7
The AID.TC occupies 16383 ID’s. VSID’s occupy the remaining 16384 – 65535 ID’s.
  IF VSID < 16384
  THEN interpret field as AID.TC identifier
  ELSE interpret field as VSID identifier

## Slide 17: Appendix E: Some Properties of a TC system
The TC system makes optimal use of what SBM offers and introduces minimal extra functionality for stations and AP’s. Duplication of flow classifications and ID signalling is avoided.
Small modifications to the Duration/ID field alow for creating a polling based TC system. The mechanisms from the Joint Proposal can be used to further improve this system.
Using flow aggregation makes the TC system scale to systems with high flow counts.
Flow classification and TC labeling occur outside the station.
The TC system requires no explicit higher layer filtering information to be conveyed to stations through MAC management frames. The MAC and upper layers remain strictly separate.
The TC system ties into an IETF/SBM environment, while it can also tap from the mechanisms in the Joint Proposal (TxOPs, CC, VSS, etc.).
The maximum number of individual upstream QoS flows from one station is 7. If more flows are required then aggregation is necessary, or VSID’s if such aggregation is not desired.
The AP needs no internal DSBM if the default TC mapping is used.
The AID.TC uniquely identifies a flow within a BSS, similar to the VSID. Through the AID.TC, the TC system ties directly into the channel access mechanisms offered by the Joint Proposal.
Flow classification in a TC system is based on L2 information only. The standard will be therefore be independent of (changes in) higher layer protocols.
No scheduling intelligence is required inside the client.
No duplicate flow state is introduced in the client.
The RFC 2814 DSBM is a standard component of Windows 2000, ME, 98, NT.

## Slide 18: TGe References
0071r18E-IEEE_802_11 MAC Enhancements-Joint-ProposalR1.ppt
01138E-Suggested-802.11-PCF-Enhancements-and-Contention-Free-Bursts.doc
01138E-Suggested-802.11-PCF-Enhancements-and-Contention-Free-Bursts.ppt
01208E-Joint-Proposal-for-802.11e-QoS-Enhancements.doc
01848E-MS_QoS_Scenariosfor80211eMacEnhancements.ppt