## Slide 1: IEEE 802.1X for IEEE 802.11
David Halasz, Stuart Norman, Glen Zorn,
Cisco Systems, Inc.
Bernard Aboba, Tim Moore,
Microsoft

## Slide 2: Outline
Introduction, Goals
Description
  Authentication Transport
  Authentication
Implementation
  Informational
  Proposed changes to 802.11
Summary

## Slide 3: Introduction
Follow up to document 00/035
IEEE 802.1X, Port based Network Access Control
IETF RFC 2284, PPP Extensible Authentication Protocol (EAP)

## Slide 4: Goals
Extensible system
Modular
Authentication done at higher layer protocol
Session encryption at IEEE 802.11 layer
Promote multi-vendor interoperability
Minimize changes to IEEE 802.11

## Slide 5: Goals cont.
System should apply to different PHY’s.
  System should scale to Ethernet, dial-up, etc.
  System should fit in to existing systems
Ability to add new authentication methods easily (without changing 802.11)
  e.g. EAP authentication type can change with no change to station, driver or AP

## Slide 6: Description
IEEE 802.1X mutually authenticatable supplicant resides above IEEE 802.11 layer
IEEE 802.1X authenticator resides in AP
Authenticator resides in AP
  e.g. 802.1X authenticator and Radius client
Authentication server gets strongly authenticated to the client.
  e.g. Radius server

## Slide 7: Description
Allow for different authentication types
  TLS
    RFC2716
  Kerberos
    draft-aboba-pppext-eapgss-01.txt
  Others can be added

## Slide 8: Description cont. 802.11 to 802.1X adaptation layer
Supplicant
Authenticator
Supplicant
1 . . . N
One IEEE 802.11 physical port becomes 1 to N virtual IEEE 802.1X ports.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: Description cont. IEEE 802.1X Terminology
Controlled port
Uncontrolled port
Supplicant
Authentication Server
Authenticator
Pieces of the system.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Description cont.
Normal Data
Authentication traffic
Wireless laptop
Authentication Server
Access Point
802.1X traffic
Authentication traffic
Wireless client assoc. at 802.11 layer. Data blocked by AP.
Access Point blocks everything except 802.1X to authentication traffic.
Authentication traffic is allowed to flow. Access point encapsulates 802.1X traffic into authentication server traffic and vice versa.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: Description cont.
Normal Data
Authentication traffic
Wireless laptop
Authentication Server
Access Point
802.1X traffic
Authentication traffic
Wireless client mutually authenticates with Authentication Server
Access Point blocks everything except 802.1X to authentication traffic.
In the authentication process the supplicant securely obtains a WEP key.
The authentication server also sends the WEP key in the success packet to the AP. AP uses the WEP key to send the broadcast WEP key.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: Description cont.
Normal Data
Authentication traffic
Wireless laptop
Authentication Server
Access Point
802.1X traffic
Authentication traffic
Wireless client and AP use WEP key. AP allows traffic to flow.
After successful EAP authentication, the Access Point allows all traffic to the Wireless laptop.
The Wireless laptop sets the WEP keys through the MLME interface. (e.g. NIC driver)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Description cont.
Wireless laptop
Radius Server
New EAP authentication types gets added in Supplicant and Authentication Server
Station and AP are aware of the authentication transport. But, they are unaware of the authentication type.
Therefore, new authentication types can be added without modifying the station or the AP.
Authentication points
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Description cont.
Wireless laptop
Authentication Server
New EAP authentication type benefits everybody
Vendor A AP
Vendor B AP
Vendor C Switch
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: Description cont. Dynamic Key Distribution
Key gets delivered to the supplicant depending on the EAP authentication type (e.g. EAP-TLS)
Per client session key gets delivered to the authenticator. (e.g. via MS-MPPE-Send-Key attribute: RFC 2548)

## Slide 16: Description cont. Broadcast Key Distribution
Broadcast key(s) gets securely delivered to the station via IEEE 802.1X EAPOL-Key.
Dynamic session key is used to encrypt the broadcast key.
Authentication server timer gets configured to re-authenticate/re-key the client.

## Slide 17: Implementation outline
Informational
  IEEE 802.11 layer
  Supplicant
  Supplicant to station MLME (NIC driver)
  Station
  AP authenticator
  Authentication server

## Slide 18: Implementation outline cont.
IEEE 802.11 proposed changes
  Encrypted/Non-encrypted changes
  WEP data formats

## Slide 19: Implementation: 802.11 layer
Initial client authentication
  Open authentication used, since dynamically derived WEP key not yet available
  After 802.1X authentication and setting dynamic key, run with WEP
  AP needs to be able to support a mixture of WEP/non-802.1X and non-WEP/802.1X data
  Station needs to be able to run WEP/non-802.1X and non-WEP/802.1X

## Slide 20: Implementation: Supplicant
Supplicant, that mutually authenticates with authentication server, resides at higher layer than IEEE 802.11
Create modular interface to port easily
Station is unaware of EAP authentication type

## Slide 21: Implementation: Station MLME (e.g. NIC driver)
Indication of roam to different AP to supplicant
Ability of supplicant to set the keys

## Slide 22: Implementation: Station
MLME interface to set the keys
  e.g. NIC driver ability to set the keys.
802.1X packets sent without WEP
non-802.1X packets sent with WEP

## Slide 23: Implementation: AP Authenticator
Communicates with station via IEEE 802.1X
Communicates with Authentication server
  e.g. Radius client in AP
Encapsulate EAP in Authentication server traffic.
  e.g. RADIUS attributes
AP is unaware of EAP authentication type

## Slide 24: Implementation: Authentication Server
EAP support can be added to Authentication server
  e.g. EAP and RADIUS defined by RFC’s
EAP easily extensible to different EAP authentication types

## Slide 25: Implementation: Current 802.11 Privacy capability
From 7.3.1.4 Capability Information
APs set the Privacy subfield to 1 within transmitted Beacon, Probe Response, Association Response and Reassociation Response Management frames if WEP encryption is required for all Data Type frames exchanged within the BSS. If WEP encryption is not required, the Privacy subfield is set to 0.
STAs within an Independent BSS set the Privacy subfield to 1 in transmitted Beacon or Probe Response Management frames if WEP encryption is required for for all Data Type frames exchanged within the IBSS. If WEP encryption is not required the Privacy subfield is set to 0.

## Slide 26: Implementation: Proposed change to 802.11 Privacy capability
Addition to 7.3.1.4 Capability Information
STAs set the Privacy subfield to 1 in transmitted Probe Request and Association Request Management frames if WEP encryption is required for all Data Type frames exchanged. If WEP encryption is optional the Privacy subfield is set to 0.

## Slide 27: Implementation: 802.11 proposed change
Broadcast/Multicast data in mixed 802.1X cell run with WEP. If run broadcast without WEP, then encrypted traffic open to attack.

## Slide 28: Implementation: 802.11 proposed change
WEP data formats should be expanded upon. Refer to the following paper,
  00/037 Proposal for Enhanced Encryption, Duncan Kitchen, Jesse Walker
This should be followed up in the standard. This will allow for implementation in hardware.

## Slide 29: Summary
This proposal will promote multi-vendor interoperability by making authentication an upper layer function. Authentication should reside at an upper layer where knowledge of the user is available. EAP authentication types can be created with no changes to the IEEE 802.11 specification. Changes to the IEEE 802.11 specification should be made to allow for mixed WEP cells and for more secure WEP data packets.