## Slide 1: The PIFS Ambiguity A tutorial on some practical limitations to the use of PIFS in the 802.11 MAC
Michael Fischer
CHOICE-Intersil
4242-3 Medical Drive
San Antonio, TX 78229
+1-210-614-4096 x107
mfischer@choicemicro.com

## Slide 2: The Problem
The 802.11 MAC defines PIFS as a "Priority" Inter-Frame Space, longer than SIFS and shorter than DIFS
    PIFS is intended to provide the AP with priority access to the medium when contending with DCF stations that wait for DIFS
    PIFS is supposed to permit a point coordinator to retain "control" of the medium, when a station does not respond, without leaving the medium idle for a DIFS period
Since the formation of TGe there have been numerous proposals to expand the use of PIFS
Unfortunately, PIFS is more useful paper (or on a wired medium) than in an 802.11 BSA:
    In the expected/common case, PIFS works well, but in the alternate case, PIFS can be ambiguous, and may result in more collisions
    The ambiguity results in part from the way several PHYs are specified

## Slide 3: PCF case: SIFS-PIFS Ambiguity
From clause 9.3.3.1:
  If a CF-Pollable STA does not respond to a CF-Poll (of any type) within the SIFS period following a transmission from the PC, or a non-CF-Pollable STA does not return the ACK frame within a SIFS period following a transmission from the PC that requires acknowledgment, then the PC shall resume control and may transmit its next frame after a PIFS period from the end of the PC's last transmission.
There is one CCA measurement prior to the PIFS Tx-decision point:
  CCA(busy) after SIFS is reasonable evidence that a response has started,
  But the CCA must react to the very beginning of the transmission, and
  PHYs with multiple antennas are allowed to check only one per slot time,
  So CCA(idle) after SIFS is much weaker evidence that no response has started, and can lead to a destructive collision.
Recommendation: Only use PHYs that sample all antennas every slot and have fast-reacting CCA for point coordinators.

## Slide 4: SIFS-PIFS Ambiguity Details
(+)CF-Poll
Wireless
Medium
Point Coordinator
Addressed Station
transmit
PHY-TXEND .indication
PHY-RXEND
.indication
PHY-TXSTART .request
RxRF+ RxPlcp
M1
Rx/ Tx
SIFS
PHY-CCA.indication(busy) here says response has begun, and prevents transmission after PIFS; but, lack of CCA(busy) does NOT necessarily mean response has not begun.
Tx/ Rx
CCA
M2
Rx/ Tx
SLOT
PIFS
transmit after SIFS
transmit after PIFS
(preamble of) response to CF-Poll
Collision!
receive
First CCA reading after SIFS boundary

## Slide 5: DCF case: PIFS-DIFS Ambiguity
The AP could, in theory, gain priority access to the medium during the contention period by starting transmissions after PIFS.
There is one CCA measurement between the PIFS Tx-decision point and the DIFS Tx-decision point:
  CCA(busy) after PIFS causes station to defer to AP,
  But the CCA must react to the very beginning of the transmission, and
  PHYs with multiple antennas are allowed to check only one per slot time,
  So CCA(idle) after PIFS is much weaker evidence that no transmission has started, and can lead to a destructive collision.
Recommendation: Be careful about using PIFS during contention period. Unlike the PCF case, this requires fast, multi-antenna CCA at all contending stations.
  But a collision only occurs if some station has backoff count =1.

## Slide 6: PIFS-DIFS Ambiguity Details
Other frame
Wireless
Medium
Station
Access Point
PHY-RXEND .indication
receive
PHY-RXEND
.indication
PHY-TXSTART .request
RxRF+ RxPlcp
M1
SIFS
Occurrence of PHY-CCA.indication(busy) here prevents transmission after DIFS; but lack of CCA(busy) does NOT necessarily mean that no other transmission has begun.
CCA
(idle)
SLOT
PIFS
transmit after DIFS
Collision!
SLOT
CCA
(idle)
M2
Rx/ Tx
receive
RxRF+ RxPlcp
M1
CCA
M2
Rx/ Tx
DIFS
preamble of frame
transmit after PIFS
First CCA reading after PIFS boundary