## Slide 1: Models for MPEG2 and Video Conferencing
Sachin Deshpande
Srinivas Kandala
Sharp Laboratories of America, Inc.
Camas, WA 98607

## Slide 2: MPEG 2 VBR Source Model
Scene 1
Scene 2
GOP 1
GOP 2
GOP d
I
B
B
P
B
B
P
B
B
P
B
B
P
B
B
I
N Frames (typically N=15 or 12)
GOP = Group of Pictures
Frame rate = 30 frames/sec
d is geometrically distributed
I frames are log-normally distributed
i.i.d or AR process
B & P frames are iid log-normal
Scene Length= N*d frames

## Slide 3: MPEG 2 Parameters

## Slide 4: Video Conferencing Parameters
Video-conferencing typically use H.263 or H.261 standards for video coding.
CBR is usually employed, by the application using a rate control algorithms. In certain situations frames may be dropped to meet the target bit-rate. Typically no B frames are used due to low latency requirement.
Packet size - typically can be 576 bytes/ 1000 bytes/ 1500 bytes for Internet.
  -Usage of smaller packet size (576 bytes) is more conservative since there is a less chance of getting fragmented.
  -Latency is not an issue for high rates even if we use 1500 bytes.

## Slide 5: Appendix: A Brief tutorial on Video Conferencing Standards

## Slide 6: Introduction
H.320,321,322,323,324 – Umbrella standards for multimedia communications (video conferencing)
H.323: multimedia communication over packet switched networks that do not provide a guaranteed QoS
  H.261, H.263(+) : video coding standards used with H.323
  G.711, G.722, G.723, G.728, G.729 : audio coding standards used with H.323

## Slide 7: Video Conferencing Modes
Point-to-point / Multi-point conference
Multipoint conference:
  Centralized Multipoint control unit (MCU)
  Distributed multipoint
Unicast / Multicast

## Slide 8: Video Coding for Video Conferencing
Interactive nature:
  Stringent requirements on latency (150-400 ms)
  No B frames
QCIF (176x144), CIF (352x288) typical frame resolutions (also possible : SQCIF, 4CIF, 16CIF)
Frame rates : 5 to 30 frames per second

## Slide 9: Video Coding for Video Conferencing
Bit-rates (including audio): mostly CBR geared towards different client speeds
  < 56 Kbps (modem) (typically use H.263 at 5-15 fps, G.723 at 5.3/6.3 Kbps)
  < 128 Kbps (ISDN) (typically use H.263 at 10-20 fps, G.723 at 5.3/6.3 Kbps)
  (256 Kbps-1.5 Mbps) Higher bitrate (DSL, cable modem, T1)

## Slide 10: Video Coding for Video Conferencing
Packet sizes :
  RTP payload for H.261, H.263, H.263+
  Group of blocks (GOB) based packetization
  Typically for Internet environment packet size can vary from 200-1500 bytes
  Overhead of 40 bytes header (RTP+UDP+IP) per packet, so keeping packet size close to maximum transfer unit (MTU) of network desirable (taking into account latency requirement)

## Slide 11: H.261, H.263 (+)
H.261 :
  P x 64 Kbps (P=1,2,3...30)
  Older standard, H.263(+) outperforms it
H.263(+) :
  H.263 : baseline standard, 4 optional annexes
  H.263+ : baseline standard, 16 optional annexes

## Slide 12: Sample References for Video Conference Traffic Models
Heyman D., Tabatabai A., Lakshman T.V., “Statistical analysis and simulation study of video teleconference traffic in ATM networks,” IEEE J Sel. Areas in Comm, 2(1), pp. 49-59, 1992.
Yegenoglu F., Jabbari B., Zhang Y.Q., “Motion-classified autoregressive modeling of variable bit-rate video,” IEEE Trans. CSVT, 3(1), pp. 42-53, 1993.
Reibman A., Berger A.W., “Traffic descriptors for VBR video teleconferencing,” IEEE/ACM Trans. Networking, 3, pp 329-339, 1995.