## Slide 1
Project: IEEE P802.11b Working Group for Wireless Local Area Networks (WLANs)
Submission Title: [Sequence Coded Modulation for the Higher Rate Extension to 802.11b Standard]
Date Submitted: [ 6 November 2000 ]
Source: [ T. O’Farrell, L.E. Aguado & C. Caldwell] Company [Supergold Communication Ltd. ]
Address [ 2-3 Sandyford Village, Sandyford, Dublin 18, Ireland ]
Voice:[ +44 113 233 2052 ], FAX: [ +44 113 2332032 ], E-Mail:[ tim.ofarrell@supergold.com ]
Re: [ Physical layer modulation proposal for the Higher Rate Extension to 802.11b Standard]
Abstract: [ This contribution is a presentation of Supergold’s sequence coded modulation proposal for the Higher Rate Extension to 802.11b Standard]
Purpose: [ Proposal for the Higher Rate Extension to 802.11b Standard]
Notice: This document has been prepared to assist the IEEE P802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.11.

## Slide 2: Outline of the Presentation
Supergold’s approach
M-ary Bi-Code Keying
System Specifications
Performance Curves
Conclusions

## Slide 3: M-ary Bi-Code Keying
The critical principle behind Supergold’s solution for WLANs is to:
Meet the performance criteria by
A straight forward application of direct sequence techniques
With minimal implementation complexity

## Slide 4: M-ary Bi-Code Keying
The PHY architecture evaluated is based on
A heterodyne radio architecture
Incorporating RF, IF and BB processing functions
And minimal external filtering functions
MBCK with equalisation and RS Coding are implemented in the BB processing unit

## Slide 5
RF
IF
PHY Architecture Evaluated
BPF
BPF
BPF
BPF
LNA
IF
Amp
PA
RF
Synthesiser
IF
Synthesiser
0o / 90o
LPF
LPF
LPF
LPF
ADC
ADC
DAC
DAC
ADC
BB
Processing
AGC
Rx I
Rx Q
Tx Q
Tx I
RSSI
44 MHz
Oscillator
Band
Filter
Image
Reject
Filters
MAC
BPF
BB
IF
Filters

## Slide 6
M-ary Bi-Code Keying
This is an established principle:
DSSS for 802.11c, M-ary Bi-Orthogonal Keying (MBOK) and CCK for 802.11b are schemes that
Benefit from processing gain and inherent coding gain that
Give robust performance in noisy channels, flat fading channels, and ISI channels
Code and Go

## Slide 7
M-ary Bi-Code Keying
M-ary Bi-Code Keying is a member of the family of direct sequence coding schemes that specifically
Addresses the issue of high data rates
By carrying more bits per symbol
But retains low sequence cross-correlations
Hence robust performance in interference, flat fading and ISI channels

## Slide 8
M-ary Bi-Code Keying
By packing more bits per symbol, M-ary Bi-Code Keying uses more symbols which nominally increases a conventional receiver’s complexity.
Supergold’s detection scheme solves the complexity bottleneck
By using unique decorrelating techniques
And simple Fast Correlator Transform processing which is similar to the Fast Hadamard Transform
Supergold’s 64-ary Bi-Code Keying is less complex than CCK, but can carry 3 times as much data in the same bandwidth.

## Slide 9
Reed Solomon Coding
Supergold concatenate M-ary Bi-Code Keying with a Reed-Solomon code to:
Enhance the overall coding gain,
Protect against random and burst errors and
Provide rate adaptation – more coding gain at low data rates
Supergold use an RS(63,k) code, where k=21, 41 and 57, which is matched to the MBCK symbol set.

## Slide 10
MBCK-RS Encoding Chain
Fast Correlator Transform
Maximum Likelihood Detector
RS Decoder
6
1
1
1
Rx I IN
Rx Q IN
rI
rQ
c’
DATA OUT
y
64-ary BCK
Select 1 of 64 Sequences
RS Encoder
DATA IN
1
d
c
6
xI
xQ
8
I OUT
Q OUT
1
1

## Slide 11
The MBCK block code maps to a 16-QAM constellation
The I&Q multilevel chips are masked by two length 16 orthogonal binary Structured Codes
16-QAM

## Slide 12
Protocol Stack
MAC
30 Mbps
High Rate
Mode
16-QAM
MMSE Equaliser
MBCK
RS(63,57)
22 Mbps
Base
Mode
16-QAM
MMSE Equaliser
MBCK
RS(63,41)
11 Mbps
Low Rate
Mode
16-QAM
MMSE Equaliser
MBCK
RS(63,21)

## Slide 13
PLCP Packet Format
Sync
2*16 * 16 Chips
SFD
16 bits
PSDU
PLCP Short Preamble
PLCP Header
Signal
8 bits
Service
8 bits
Length
16 bits
CRC
16 bits
PPDU
T1
22 Mchip/s QPSK
T2
22 Mchip/s QPSK
Tpsdu
11, 22, 30 Mb/s
QAM
T1 + T2 = 512/22e6 + 64*8/22e6 = 46 us
aSIFSTIME = 10 us
aSLOTTIME = 20 us
Uses HR/DSSS PHY Long and Short PLCP Preamble and Header and proposed preamble:

## Slide 14
Alternative Coding Arrangements
MBCK can be used with other FEC schemes:
Convolutional codes
Turbo codes
Trellis coded modulation
And alternative masking codes such as the length 11 Barker code

## Slide 15
PHY System Specification
Parameter | Symbol | Test Condition | Value | Units
Frequency band |  | 2400 – 2483.5 MHz ISM Band | 2.4 | GHz
Channel frequencies | fc | 2412, 2417, 2422, 2427, 2432, 2437, 2442, 2447 2452, 2457, 2462, 2467, 2472, 2483 |  | MHz
Channel spacing | f |  | 5 | MHz
Number of Channels | N |  | 14 | 
Channel bandwidth | B | Null-to-null, 25% root raised cosine filter | 14 | MHz
Chip rate | Rchip |  | 11 | Mchip/s
Data rates | R | Low-rate mode Base mode High rate mode | 11 22 30 | Mb/s Mb/s Mb/s
Processing gain | G | Conforms to FCC 15.247, ETSI 300-328 and MPT (evaluation incomplete) | >10 | dB
Spectral efficiency |  | 22 Mb/s Base mode 30 Mb/s High rate mode | 79 108 | % %
Delay Spread Tolerance | Trms | RMS delay spread for 0.1 PER for an amount of AWGN set by a 0.01 PER | 50 | ns

## Slide 16
PHY Encoding Specification
Parameter | Symbol | Test Condition | Value | Units
Sequence coding | MBCK | 64-ary bi-code keying Quaternary sequences of length 4 chips |  | 
DSSS Scrambling Code | b | Structured Code SI and SQ (different code per I and Q) | 16 | Chips
Coded bits/sequence | k |  | 6 | 
FEC scheme |  | Reed Solomon RS(63,k) |  | 
Coding rates | r | Low rate mode Base mode High rate mode | 1/3 2/3 10/11 | 
Coding gain | g | Over 16-QAM at 10-6 BER, AWGN channel 22 Mb/s base mode 30 Mb/s high rate mode | 6 4 | dB dB
Detector Implementation |  | Fast correlator transform and greatest peak detector |  | 

## Slide 17
PHY RF Specification
Parameter | Symbol | Test Condition | Value | Units
Modulation |  |  | 16-QAM | 
PA back-off |  | From 1 dB compression point | 6-to-9 | dB
Carrier frequency accuracy |  | PER is not substantially degraded for frequency offsets caused by this inaccuracy | 20 | PPM
IF frequency | fIF |  | 280 | MHz
IF bandwidth | fIF |  | 17 | MHz
Radio compatibility and interoperability |  | Common radio architecture with HR/DSSS Supports all legacy modes |  | 
Clear channel assessment | CCA | Same as HR/DSSS | Yes | 
Co-channel rejection | CCI | Tolerance to an other co-located, in channel, MBCK user | -7 | dB
Adjacent channel rejection | ACI | 25 MHz separation between active channels | >50 | dBc
Spectral mask requirement | RF-mask | At 11 MHz At 22 MHz | -30 -50 | dBc dBc
Phase noise penalty | n | At 0.5o rms phase noise | <0.5 | dB

## Slide 18
PHY-BB Specification
Parameter | Symbol | Test Condition | Value | Units
Clock rates | clk bb | Master BB processing | 44 11 | MHz MHz
Samples/chip | Ts | To meet root raised cosine filter spec. | 4 | 
RRCF |  | Root raised cosine filter, 25% excess B/W | 22 | taps
ADC precision |  | 44 Msamples/s | 6 | bits
DAC precision |  | 44 Msamples/s | 6 | bits
RSSI ADC |  | 11 Msamples/s | 6 | bits
BB processing |  | MBCK (implemented in a demonstrator) RS(63,41) MMSE Equaliser (16 tap) Root raised cosine filter (22 tap) | 10k 7k 15k 20k | gates

## Slide 19
PHY-Throughput Specification
Parameter | Symbol | Test Condition | Value | Units
PHY header duration | TLP TSP TPP | Long preamble Short preamble Proposed preamble | 192 96 46 | us
MAC overhead | TMAC | MAC header and FCS | 34 | bytes
ACK payload | TSIF | As used in 802.11b | 19 | bytes
SIFs | TSIF | As used in 802.11b | 10 | us
DIFs | TDIF | As used in 802.11b | 50 | us
Aggregate Throughput | S | Proposed preamble, without ACK, 3 LANS 22 Mb/s x 3 simultaneous channels 30 Mb/s x 3 simultaneous channels | 58.68 79.26 | Mb/s Mb/s
Throughput = Data Rate x Payload Duration/(Payload Duration+Overhead)
Payload Duration = Payload Bits/Data Rate
Overhead = PHY Hdr Duration + MAC Hdr, FCS Duration + SIFS + ACK Duration + DIFS
Airtime= Payload Duration + Overhead

## Slide 20
PHY-Throughput at 22 Mb/s
With ACK
Parameter | Symbol | Test Condition | Value | Units
Throughput with long preamble | SLP | 100 B 1000 B 2346 B | 1.75 10.21 14.75 | Mb/s
Throughput with short preamble | SSP | 100 B 1000 B 2346 B | 2.84 13.14 17.09 | Mb/s
Throughput with proposed preamble | SPP | 100 B 1000 B 2346 B | 4.20 15.45 18.63 | Mb/s

## Slide 21
PHY-Throughput at 22 Mb/s
Without ACK
Parameter | Symbol | Test Condition | Value | Units
Throughput with long preamble | SLP | 100 B 1000 B 2346 B | 2.90 13.27 17.18 | Mb/s
Throughput with short preamble | SSP | 100 B 1000 B 2346 B | 4.25 15.51 18.67 | Mb/s
Throughput with proposed preamble | SPP | 100 B 1000 B 2346 B | 5.60 17.01 19.56 | Mb/s

## Slide 22
PHY-Throughput at 30 Mb/s
With ACK
Parameter | Symbol | Test Condition | Value | Units
Throughput with long preamble | SLP | 100 B 1000 B 2346 B | 1.81 11.73 18.03 | Mb/s
Throughput with short preamble | SSP | 100 B 1000 B 2346 B | 2.99 15.77 21.66 | Mb/s
Throughput with proposed preamble | SPP | 100 B 1000 B 2346 B | 6.13 21.59 25.73 | Mb/s

## Slide 23
PHY-Throughput at 30 Mb/s
Without ACK
Parameter | Symbol | Test Condition | Value | Units
Throughput with long preamble | SLP | 100 B 1000 B 2346 B | 3.04 15.90 21.77 | Mb/s
Throughput with short preamble | SSP | 100 B 1000 B 2346 B | 4.55 19.23 24.22 | Mb/s
Throughput with proposed preamble | SPP | 100 B 1000 B 2346 B | 7.18 22.76 26.42 | Mb/s

## Slide 24
PHY – Power Consumption
Transmitter | Power mW | Receiver | Power mW
PA* | 2300 | LNA | 25
RF up-mixer | 30 | RF down-mixer | 30
RF Synthesiser | 25 | RF Synthesiser | 25
IF up-mixer | 20 | IF Amp | 10
IF Synthesiser | 15 | IF down-mixer | 20
Smoothing Filters (I&Q) | 10 | IF Synthesiser | 15
DACs (I&Q) | 40 | Anti-aliasing Filters (I&Q) | 10
BB Processing (ASIC) | 125 | ADCs (I&Q) | 40
 |  | ADC (RSSI) | 20
 |  | BB Processing (ASIC) | 150
Tx Total | 2565 | Rx Total | 345
* 18 dBm, 33% eff, 9dB back-off, 2 dB band filter loss

## Slide 25
Performance Curves
PER performance versus AWGN with non-ideal power amplifier (criteria 17) requires rerun of simulation results

## Slide 26
Pulse Shaped-Waveform Power Spectrum Response at the Input of the PA
Frequency (Hz)
Power (dB)

## Slide 27
Power Spectrum Response for RF PA Back-Off from 1dB Compression Point – p = 2
6 dB back-off
9 dB back-off
14 dB back-off
Frequency (Hz)
Power (dB)

## Slide 28
Power Spectrum Response for RF PA Back-Off from 1dB Compression Point – p = 3
6 dB back-off
9 dB back-off
14 dB back-off
Frequency (Hz)
Power (dB)

## Slide 29
BER v. Eb/N0 in the AWGN channel for 1000 B/packets

## Slide 30
PER v. Eb/N0 in the AWGN channel for 1000 B/packets

## Slide 31
PER v. SNR in the AWGN channel for 1000 B/packets

## Slide 32
PER v. Eb/N0 in the flat fading channel

## Slide 33
PER v. SNR in the flat fading channel

## Slide 34
PER v. Eb/N0 in the fading ISI multipath channel

## Slide 35
PER v. SNR in the fading ISI multipath channel

## Slide 36
PER v. Eb/N0 in the ISI only multipath channel

## Slide 37
PER v. SNR in the ISI only multipath channel

## Slide 38
PER v. Eb/N0 in the AWGN channel in the Presence of 10% Timing Offset

## Slide 39
Maturity of Solution
Supergold’s solution uses well established concepts with proven technical maturity
MBCK works on the same principles as MBOK
MBCK has been extensively simulated and demonstrated in an FPGA device
The RF subsystem is almost identical to current 802.11b products
The baseband processor performs similar functions as the 802.11b baseband processor

## Slide 40
Conclusions
MBCK is a low complexity code that
meets the WLAN robustness criteria
Complements DSSS and CCK
is implementable using existing chips sets
is an inexpensive solution for WLANs
A road map exists to achieve even higher data rates with MBCK
Adoption of MBCK by 802.11 and industry will be fully supported by Supergold.