## Slide 1
p-DCF for Prioritized MAC Service
Jin-Meng Ho, Sid Schrum, and Khaled Turki
Texas Instruments Incorporated
12500 TI Blvd.
Dallas, Texas 75243
(214) 480-1994 (Ho), (919) 319-1890 (Schrum), (214) 480-6908 (Turki)
jinmengho@ti.com, sschrum@ti.com, khaled@ti.com

## Slide 2
Features of p-DCF
Access control: use probability, rather than backoff
Implementation: simple
  Comparable to, or simpler than, backoff
Performance: suitable to optimization and prioritization
  With backoff access, once a backoff value has been chosen, the corresponding contention is prescribed--regardless of channel status changes (e.g., even if channel becomes less busy or idle, transmission is not allowed until the corresponding backoff timer decrements to 0).
  With probability access, all contentions are adaptable to channel status changes and performance optimization is feasible (e.g., there exist simple algorithms that yield statistically one transmission out of multiple contenders at a given time).
  With probability access, contention can be limited to certain priorities as seen fit by AP, thus achieving better access control.

## Slide 3
Probabilistic versus Backoff Access
A station contends at time t with probability p
  Generates a number, z, from a uniform distribution over [0, 1)
  Obtains channel access at time t if and only if z <= p
  Executes generation and decision process prior to time t
A station contends at time t with contention window CW
  Generates a number, z, from a uniform distribution over [0, 1)
  Obtains access at time t* = t + round(z x CW) x aSlotTime
t
Transmits iff z <= p
t
Cannot transmit
t*
Transmits
round(z x CW) x aSlotTime
Probabilistic Access
Backoff Access

## Slide 4
v-DCF from Doc. 361
Access differentiation controlled by a CWx parameter per priority category.
  Multiple DCF’s running in parallel, with conceptually an individual Backoff counter for Backoff and Post-Backoff.
    Implementations based on a single Delta-Backoff counter are possible.
  The scheduling function is based on random number generated per access priority level, using individual CWx parameters causing differentiation in access ratio according to: 1/CW3 : 1/CW2 : 1/CW1 : 1/CW0
At a local collision the highest priority frame is being transmitted, while the other DCF is deferring and generate a new Backoff.
“If the MAC sublayer
association supports optional
prioritized quality of service,
the MAC will endeavor to
deliver MSDUs of higher
priority in preference to other
MSDUs of lower priority
that may be queued for
delivery throughout the BSS.” (from proposed 6.1.1)
?

## Slide 5
p-DCF Operation--Without AP Control
Determination of Contention Probability
When a priority category, PCi, requires a new (not retry) access opportunity, the sending station, x, initiates a PCi probability pix = pi,0 or otherwise sets pix = 0.
  For 802.11b: p0,0 = 1/32, p1,0 =2 p0,0, p2,0 = 4 p0,0, p3,0 = 8 p0,0
When a priority category, PCi, is determined to be involved in a collision, the sending station, x, immediately halves the pix.
  Other priority categories coexisting in the same station will not see their probabilities changed, as would be the case were they queued in other non-colliding stations, and as is needed in order not to disadvantage their access opportunities in comparison with priority categories that are solely queued in other stations.
An active station, x, calculates its contention probability
, and recalculates px whenever any pix is changed.

## Slide 6
Determination of Transmission
After a busy medium becomes idle for a DIFS period, an active station, x, contends with its updated contention probability px, whether the station was transmitting into the busy medium and whether the transmission, if any, was successful or not.
  If the station obtains channel access, it may choose to serve (send) any active local priority category (a 911 call should be allowed to be deemed more important than fairness).
  If the station obtains no channel access, it contends with the same probability px one time slot later if that time slot was found to be idle, with the same process repeated until either the station obtains channel access or the medium becomes busy.
  If the station collides with others, it halves the probability for the (unsuccessfully) served priority category, and contends again after a DIFS time with an updated contention probability, as stated above.
  There is no need to determine the transmission qualification for each individual priority category within the same station, and hence no need to resolve “local collision”--which would never occur.
Operation--Without AP Control (Cont)

## Slide 7
Determination of Contention Probability
All constituent probabilities pix are determined and updated by the AP based on its load estimation, and broadcast by the AP either via the beacon frame and/or other new frames.
Active stations obtain their contention probabilities px by summing their respective constituent probabilities pix.
AP may further limit channel access to certain priority categories (such as high priorities) in any time period.
Determination of Transmission
The rules are the same as for operation without AP control, provided the contention probability and local traffic selection at any active station are based on AP’s decision.
p-DCF Operation--With AP Control

## Slide 8
AP may use PIFS/SIFS, instead of DIFS, for channel access in CP
AP may choose to send traffic in CFP to alleviate contention
  Same frame formats are used in both CFP and CP.
  No polls will be sent by AP in CFP for “level one conformance”.
  Frames sent by AP in CFP can be received but non-AP stations implementing no PCF.
  No additional complexity is added to AP for CFP transmission.
AP Traffic Delivery

## Slide 9
From Doc. 361:
  We converged on the “Fairness” definition.
    Statistical equal Tx-Op probability across the whole BSS within a traffic category as in standard DCF.
Question 1:
  Why “equal Tx-Op probability”, but not “equal Rx-Op probability”?
    Some queues are transmitted to single destinations, while some other queues of the same priority are transmitted to multiple destinations (all data frames of the same priority but of different destinations are put into the same queue at the transmitting station). If “equal Tx-Op probability” is maintained per transmit queue, no “equal Rx-Op probability” is achieved per receive queue (for the same priority)!
    It may be the receiver, rather than the transmitter, that pays for priority service and hence cares about “equal” treatment within the same priority.
Question 2:
  Why “equal Tx-Op probability”, but not “equal bandwidth usage”?
    Stations may have traffic of the same priority but of disparate inherent source rates, and hence will not feel “equal” treatment even if they are given “equal Tx-Op probability”.
    A given priority at station x (high source rate) may feel “unfair” service while already using more bandwidth than those of the same priority at other stations (low source rates).
“Answer”:
  Welcome to DCF/D-QoS on wireless medium!
Fairness Discussion

## Slide 10
Probability based DCF (p-DCF) is compared and contrasted with backoff based DCF.
p-DCF is described in terms of its operation with and without AP control.
p-DCF is simple for implementation and ready for optimization.
Simulation on both p-DCF and v-DCF is in progress and intended to be reported in the near future.
Summary