## Slide 1
p-DCF for Prioritized MAC Service (Expanded version based on decision in Tampa of allowing CF-Polls in prioritized QoS levels)
Jin-Meng Ho, Sid Schrum, Khaled Turki
Donald P. Shaver and Matthew B. Shoemake
Texas Instruments Incorporated
12500 TI Blvd.
Dallas, Texas 75243
(214) 480-1994 (Ho), (919) 319-1890 (Schrum), (214) 480-6908 (Turki)
(214) 480-4349 (Shaver), (214) 480-2344 (Shoemake)
jinmengho@ti.com, sschrum@ti.com, khaled@ti.com
shaver@ti.com, shoemake@ti.com

## Slide 2
Features of Channel Access
Provides contention-free and contention-based transmissions within the “contention period (CP)”
  Allows the EAP to use PIFS/SIFS for contention-free transmission in CP by EAP
  Allows the EAP to use +CF-Poll for contention-free transmission in CP by wireless ESTAs
  Requires wireless ESTAs to use probability for contention-based transmission in CP by wireless ESTAs
  Requires wireless ESTAs to use (short) Poll Request for contention-free transmission in CP of data bursts
Supports piggybacked acks in CP for better throughput
Enables EAP and wireless ESTAs to access both CFP and CP by compatible mechanisms
  Same schedulers at EAP and ESTAs work across CFP and CP
Mitigates overlapping BSS interference as effectively and as simply as legacy DCF

## Slide 3
Elements of Enhancements (1)
EAP supports 8 traffic categories (TCs) in both CFP and CP for each associated ESTA
  Each wireless ESTA also supports 8 TCs
EAP uses PIFS to gain contention-free access to CP after completion of a frame exchange sequence
  ESTAs (including EAP), when addressed, use SIFS to gain contention-free access to CP amid a frame exchange sequence
EAP sends +CF-Poll frames in CP (just as in CFP except for different Duration field setting) to wireless ESTAs that are known to EAP to have data for transmission
  Wireless ESTAs send frames in response to a + CF-Poll in CP (just as in CFP except for TXOP limit calculation)

## Slide 4
Elements of Enhancements (2)
A wireless ESTA gains contention-free access to CP within a SIFS of receiving a non-fragmented MSDU
  If the ESTA is the destination STA of the received frame
  If the ESTA can send a frame of priority no less than the received frame, and
  If the ESTA has not sent a frame within this frame exchange sequence
A wireless ESTA gains contention-based access to CP by a permission probability (PP), i.e., by
  Contending with PP (i.e., probability of transmitting = PP) once the channel is determined to be idle for a DIFS duration
  Re-contending with the same PP aSlotTime later if channel remains idle over that slot (wherein no transmission occurred from this or any other station in range), with the process repeated until channel becomes busy (due to a transmission from either this or any other station in range)

## Slide 5
Elements of Enhancements (3)
A wireless ESTA calculates its PP by summing all of its constituent TC permission probabilities (TCPPs)
  Using TCPPs as last updated by EAP
  With TCPPs for empty TCs (no queued frames) set to 0, and
  With TCPPs being the same across all associated ESTAs in the same BSS (i.e., TCPPs differ by TCs, not by ESTAs)
A wireless ESTA resends a collided frame
  By contention-based access to CP, i.e., by repeating the contention procedure with PP updated as stated above
    Retry occurs one DIFS after the end of the expected but failed acknowledgment frame
    Constituent TCPPs remain the same if they are not updated by EAP
  By contention-free access to either CFP or CP, as applicable with the enhanced channel access mechanisms

## Slide 6
Elements of Enhancements (4)
A wireless ESTA sends a short Poll Request (PR) frame by contention with a PP in CP for contention-free transmission of a burst of queued MSDUs
  The ESTA sends the PR with a PP in CP according to enhanced DCF procedure, where PP is the sum of the ESTA’s TCPs
  The ESTA may also send the PR by contention-free access in CP when available
  The EAP polls the ESTA upon receiving the PR, repeatedly (but not necessarily consecutively) until the ESTA has no queued data for transmission
A wireless ESTA sends a RTS frame with PP, in the same way as it sends a PR frame
  The addressed station responds with a CTS frame as usual
A wireless ESTA gaining channel access to either CFP or CP has the right to serve any locally queued TC
  Unless stated otherwise, either explicitly or implicitly
  Subject to the applicable TXOP limit

## Slide 7
Elements of Enhancements (5)
An EAP determines and updates TCPPs based on its load estimation, i.e., the number of various queued TCs and hosting stations
  Which may be in turn estimated from the observation of “idle”, “successful”, and “collision” events occurring on the channel over a preceding interval, such as the preceding CP
The EAP may further change the TCPPs based on the load estimates to preclude the contention of certain TCs (the TCPPs for the forbidden TCs being set to 0)
  Which reduces the collision probability in case of heavy loading, and hence the access delay of higher priority traffic
  Which avoids the contention of periodic traffic (such as voice known through TC mapping) that will be served by CF-Polls
The EAP broadcasts the new values of TCPPs in a CP Contention Control (CCC) element inserted in a beacon
Length
TCPP values
TCPP0 … TCPP7
Octets:
1
1
8
CP Contention Control (CCC)
element format
Element ID

## Slide 8
Rules of Frame Usage in CP (1)
{QoS }Data + CF-Poll
  These frames are sent by an EAP
  The EAP uses one of the frames to send an MSDU{/MMPDU} with a CF-Poll to a wireless ESTA, setting the Duration field to the time, in µs, allocated to the TXOP of the addressed ESTA, plus one {QoS} CF-Ack frame time, plus two SIFS intervals
  The addressed ESTA uses the TXOP, calculated from the Duration value subtracted by one {QoS }CF-Ack frame time and two SIFS intervals, to send an MSDU{/MMPDU} to the EAP or another station, using frame fragmentation if appropriate, one SIFS after the end of the received frame
  The addressed ESTA acknowledges the reception of the frame by using a {QoS}{ Data + }CF-Ack data frame, just as in CFP
{QoS }Data + CF-Ack + CF-Poll
  These frames are sent by an EAP
  The EAP uses one of the frames to acknowledge the reception of an immediately preceding frame addressed to the EAP
  The other rules are the same as for {QoS }Data + CF-Poll

## Slide 9
Rules of Frame Usage in CP (2)
{QoS }Data
  These frames are sent by an ESTA (EAP or wireless ESTA)
  An ESTA uses one of the frames to send an MSDU{/MMPDU} to another ESTA, setting the Duration field to the time, in µs, required to transmit one {QoS }CF-Ack frame, plus one SIFS interval
  The addressed ESTA may send an MSDU{/MMPDU} to any other station, using frame fragmentation if appropriate, one SIFS after the end of the received frame
    If the received frame is not fragmented
    If the addressed ESTA has not sent a frame within this frame exchange sequence, and
    If the addressed ESTA can send a frame of priority no less than the received frame
  The addressed ESTA acknowledges the reception of the frame by using a {QoS}{ Data + }CF-Ack data frame, just as in CFP
{QoS }Data + CF-Ack
  These frames are sent by an ESTA (EAP or wireless ESTA)
  An ESTA uses one of the frames to acknowledge the reception of an immediately preceding frame addressed to the ESTA
  The other rules are the same as for {QoS }Data

## Slide 10
Poll Request (PR)
  This frame is sent by a wireless ESTA to an EAP
  A wireless ESTA uses the frame to request the EAP for arranging contention-free transmission of a burst of queued MSDUs, with the priority and size of the burst specified in the TCA and TC Size fields
    The Duration field is set to the time, in µs, required to transmit the first MSDU of the pending burst, plus one CF-Poll frame, plus one QoS CF-Ack frame, plus three SIFS intervals
    The BSSID is defined as in the baseline proposal
    The TCA field carries the AID of the ESTA sending this PR, and the priority of the queued TC for which the TC Size is specified
    The TC Size field specifies the size of the queued burst in the 10 least significant bits (lsb), with the 6 most significant bits (msb) all set to 0
  The EAP sends a {QoS}{ Data + }CF-Poll to the requesting ESTA, where the implied TXOP limit may be set to be equal to or less than the requested TC size, one SIFS after receiving the PR frame.
Frame
Control
Duration
BSSID
TCA
TC Size
FCS
Octets:
2
2
6
2
2
4
MAC Header
Rules of Frame Usage in CP (3)
Poll Request (PR) frame
(Type 01, subtype 0011)

## Slide 11
Procedures of Contention in CP (1)
A wireless ESTA first determines which frame to send next from its locally queued TCs
If the selected frame (new or retried) is to be sent by contention in CP, the ESTA first calculates its permission probability (PP) using the latest values of TCPPs
  PP = sum(TCPP0 … TCPP7)
  TCPi is set to 0 if the ESTA has no queued data of priority i
In the case where the ESTA has not been transmitting for more than a DIFS interval preceding intended contention
  If the ESTA is attempting to send the selected frame by contention with probability in CP for the first time since the channel becomes idle, it waits until the channel is determined to have been idle for a DIFS interval, and then contends with the calculated PP
  The ESTA transmits the selected frame if it draws a number from a uniform distribution over [0, 1) that is less than PP
  Otherwise (repeated attempt), the ESTA contends again with the same PP over each successive idle slot
    Until the channel becomes busy or the ESTA transmits the selected frame

## Slide 12
Procedures of Contention in CP (2)
In the case where the channel becomes busy not due to a transmission from the ESTA, the above procedures are repeated
In the case where the ESTA does transmit
  If an acknowledgment is received at the end of the expected acknowledgment, the selected frame has been successfully sent
  Otherwise, the selected frame has not been successfully sent
  In either case, the ESTA waits for at least one more DIFS before initiating another contention (for sending the failed frame or a different frame)
Beacon
TBTT
CF-End
Channel never
idle for one
DIFS due to
other stations
TBTT
DIFS
DIFS
Contends
with PP = P1
but does not
transmit
aSlotTime
aSlotTime
Ack
Contends
with PP = P2
but does not
transmit
Contends
with PP = P2
but does not
transmit
Channel never
idle for one
DIFS due to
other stations
DIFS
Transmits
a selected
frame
aSlotTime
Channel never
idle for one
DIFS due to
other stations
DIFS
Contends
with
PP = P3
Beacon
CF-End
P2 may not be
equal to P1
if the queues of the TCs
have changed
The transmitted frame
may differ from the one
previous selected
if the queues of the TCs
have changed
P3 may not be
equal to P2
if the queues of the TCs
or the TCPPs in
the latest beacon
have changed

## Slide 13
Examples of Load Estimation
Cf D. Bertsekas and R. Gallager, "Data Networks," 2nd ed., Prentice Hall, NJ, 1992, Sec. 4.4.
   = aSlotTime/FrameSize
  , = fraction of bandwidth used for contention
  Update of estimated number of contending stations

## Slide 14
Illustrations of Frame Transmissions
Beacon
TBTT
CF-End
PIFS
QoS Data + CF-Poll
(AP  STA 2)
TBTT
Contention Period (CP)
aSlotTime
SIFS
DIFS
DIFS
QoS Data + CF-Ack
+ CF-Poll
(AP  STA 1)
QoS Data + CF-Ack
(STA 2  AP)
NAV
NAV
NAV
QoS Data + CF-Ack
(STA 1  STA 4)
QoS Data + CF-Ack
(STA 4  STA 1)
QoS CF-Ack
QoS CF-Ack
QoS CF-Ack
NAV
QoS CF-Ack
NAV
Data (STA 5  AP)
PR (STA 3  AP)
NAV
CF-Poll ( STA 3)
QoS Data + CF-Ack
(STA 3  STA 4)
PR (STA 3  AP)
QoS Data + CF-Poll
(AP  STA 3)
NAV
QoS Data + CF-Ack
(STA 3  AP)
QoS CF-Ack
QoS CF-Ack + CF-Poll
(AP  STA 2)
QoS Data + CF-Ack
(STA 2  AP)
QoS Data + CF-Ack
(STA 3  AP)
NAV
QoS CF-Ack + CF-Poll
(AP  STA 3)
QoS CF-Ack
(AP  STA 3)
NAV
NAV
NAV
NAV
SIFS
aSlotTime
PIFS
DIFS
Contention
Free Period
(CFP)
t = t1
DIFS

## Slide 15
Comparison of Contention By Probability and By Backoff (1)
Optimization Criterion and Realization
  Maximize frame departure rate (i.e., rate of successful transmissions)
  Derive transmission probabilities (i.e., TCPPs and PPs) accordingly
Probabilistic Contention
  All TCPPs are updated by EAP and effective immediately
    All ESTAs use the updated TCPPs in calculating their PPs, regardless of the TCPP values they used before
  Uniform distributions of TCPPs are achieved across contending stations
    TCPPESTA1 = TCPPESTA2 = TCPPESTA3 = … for traffic of same TC
    EAP need not track individual contention/collision histories of ESTAs
  TCPPs, and hence PPs, are determinable once the number of queued TCs is estimated
    The properties of instant update and uniform distributions of TCPPs greatly simplify the estimation process of queued TCs

## Slide 16
Comparison of Contention By Probability and By Backoff (2)
Backoff Contention
  TCPP = 1/(CW+1) for a TC (constrained by CW) at a given station
  CWs are set before initial transmissions and retransmissions
    Otherwise remain unchanged (subsequent updates by EAP do not effect the previous updates)
  Nonuniform distributions of TCPPs result across contending stations
    CW ESTA1  CWESTA2  CWESTA3  … for traffic of same TC (in general)
    TCPPESTA1  TCPPESTA2  TCPPESTA3  … for traffic of same TC (in general)
    EAP need to track individual contention/collision histories of ESTAs and provide different updated values of CWs at different ESTAs--too complex
    EAP, in fact, cannot even know what ESTAs were involved in a collision or collisions and hence nor the CWs being used by the ESTAs
ESTA1
ESTA2
ESTA3
aSlotTime
aSlotTime
PESTA1
PESTA3
PESTA2
PESTA1
PESTA3
PESTA2

## Slide 17
Backoff Implementation Of Probabilistic Contention (1)
Contention window (CW) adaptation
  Multiple backoff timers per ESTA
    TCPP = 1/(CW+1) for a TC (constrained by CW) at a given station
    CW = 1/TCPP1-1 for a TC (constrained by TCPP) at a given station
    CWs for all TCs are changed following an update of TCPPs by EAP
    Backoff timers for all queued TCs are reset accordingly
  Single backoff timer per ESTA
    PP = sum(TCPP0 … TCPP7)  CW = 1/PP-1 at a given station
    CWs for all ESTAs are changed following an update of TCPPs by EAP
    Backoff timers for all queued ESTAs are reset accordingly

## Slide 18
Beacon
aSlotTime
Beacon
aSlotTime
aSlotTime
All ESTAs reset backoff timers
based on broadcast TCPPs
All ESTAs reset backoff timers
based on broadcast TCPPs
DIFS
DIFS
DIFS
Channel busy
Channel busy
Channel busy
Backoff timers expire
Backoff timers expire
Backoff Implementation Of Probabilistic Contention (2)
CP Contention Control (CCC) Update
  TCPPs, and hence CWs, remain unchanged over an update interval
    Equilibrium state: # of new frames = # of transmitted frames 
    # of queued TCs and values of TCPPs unchanged over an update interval
    1st slot--5 queued TCs of same priority, TCPP = 1/15, none transmitted
    2nd slot--still 5 queued TCs and TCPP = 1/15, two collided
    3nd slot--still 5 queued TCs and TCPP = 1/15 --unchanged
  update interval may be set equal to beacon interval

## Slide 19
Frame Transmissions in IBSS
Contention-free transmission
  {QoS }Data + Ack: An ESTA receiving a non-fragmented MPDU{/MSDU} may send a frame by contention-free transmission, while acknowledging that reception, within a SIFS of that reception
    If that ESTA has not sent a frame within this frame exchange sequence, and
    If that ESTA can send a frame of priority no less than the received frame
Contention-based transmission by probabilistic contention
  The values of TCPPs for new transmissions are set to TCPPmaxs
  The values of TCPPs following a collision are reduced, e.g., by half
  The values of TCPPs are not to be smaller than TCPPmins
  The values of TCPPs remain unchanged if they were not involved in a collision (even if some of its colocating TCs were)
Backoff implementation of probabilistic contention
  The values of CWs for new transmissions are set to CWmins
  The values of CWs following a collision are increased, e.g., by twice
  The values of CWs are not to be larger than CWmaxs
  The values of CWs remain unchanged if they were not involved in a collision (even if some of its co-locating TCs were)
  The implementation is the same as for contention by backoff

## Slide 20
Sample References
Books:
1. D. Bertsekas and R. Gallager, "Data Networks," 2nd ed., Prentice Hall, NJ, 1992, Chapter 4.
2. A. S. Tanenbaum, "Computer Networks," 3rd ed., Prentice Hall, NJ, 1996, Chapter 4.
Papers:
1. L. Kleinrock and/or F. Tobagi's CSMA and CSMA/CD serial papers published between 1975-1985.
2. R. L. Rivest, "Network Control by Bayesian Broadcast," IEEE Trans. Inform. Theory, vol. IT-33, May 1987, pp. 323-328.
3. P. E. Cantrell, W. K. Tsai, and J-F. Tuan, "Stability and Performance of Pseudo-Bayesian Controlled CSMA-CD" (published in an IEEE conference proceeding).