## Slide 1: TGg Regulatory Approval Plan
Notes: <number>
<footer>
<header>
<date/time>
This Style Guide is designed to facilitate the creation of presentations within Intersil graphic guidelines. These presentations may address an external audience, as in a product announcement or industry event, or an internal one, as in seminars or executive committee meetings. In any case, it is important to adhere to a corporate Style Guide. The Style Guide provides standards and guidelines to help project Intersil’s corporate identity. Projecting visual continuity is a key to the success of the company.
The Style Guide is based on the capabilities of Microsoft PowerPoint, one of our corporate standard software packages. The following slides and script describe the graphic standards and guidelines for these presentations.
This Style Guide will address four key areas:
  The overall Layout and Design
  Specifications for placement of text, logo, and graphic treatments (symbols, bar charts and table charts)
  Recommended Guidelines for using photography and illustration
  Recommended Color usage and standard palette

## Slide 2: OFDM: Regulatory Compliance
High rate systems (>20 Mbps in same channel width) do not comply with current FCC rules
FCC definition of DSSS and Spread Spectrum
Can we work with FCC to get more flexible rules?
Can we get a rule change under 99-231?
    Maybe trade power for relaxing processing gain requirement
    Working within 99-231 would save time

## Slide 3: Current Situation
No high rate solution (>20 Mbps in same BW) complies with current rules
  Wi-LAN was denied equipment authorization for an OFDM system
  FCC letters denying authorization have been made public
  Basis of denial appears to cover all high rate systems, not just OFDM
Basis for Denial of Authorization

## Slide 4: Basis for Denial of Authorization
Spectral Efficiency
  “By nature, a DSSS emission utilizes an occupied bandwidth much greater than the occupied bandwidth necessary to transmit the information”
    Joe Dichoso, OET Engineer, Letter of May 12, 2000
  “... a spread spectum utilizes an occupied bandwidth much greater than the occupied bandwidth necessary to transmit the information”
    Dale Hatfield, Chief of OET, Letter of August 18, 2000

## Slide 5: Basis for Denial of Authorization
Use of a Classic Correlator Structure
  “In addition, processing gain…is the gain realized by the spreading / despreading function, after the received signal is filtered to the information bandwidth. Implied is a classic correlator used to collapse the spread waveform”
    Joe Dichoso, OET Engineer, Letter of May 12, 2000

## Slide 6: FCC Definitions (47 CFR Section 2.1)
DSSS
  “A spread spectrum system in which the carrier has been modulated by a high speed spreading code and an information data stream. The high speed code sequence dominates the “modulating function” and is the direct cause of the wide spreading of the transmitting signal.”
Spread Spectrum System
  “A spread spectrum system is an information bearing communications system in which: (1) Information is conveyed by modulation of a carrier by some conventional means, (2) the bandwidth is deliberately widened by means of a spreading function over that which would be needed to transmit the information alone. (In some spread spectrum systems, a portion of the information being conveyed by the system may be contained in the spreading function.)”

## Slide 7: We Have Two Clear Choices
Choose a solution, then talk to FCC...
  Should we ignore Commission’s rejection of Wi-LAN based on SPECTRAL EFFICIENCY?
  Approval of >20 Mbps waveform requires Commission to reverse public position
    not very likely
  Ignoring the Commission in the selection process sends the wrong message
    FCC is well aware of TGg activity
    What if we pick a waveform & Commission just says “no”?
    Most probable outcome without a rule change

## Slide 8: We Have Two Clear Choices (cont’d)
…or, we can work WITH the FCC
  ET Docket 99-231 (processing gain test) is open
  FCC wants to clarify DSSS rules
    current rules are a big problem for FCC
    FCC would like to let industry be creative
    FCC does not want to play “traffic cop”
  However, current rules are a real problem
    FCC objections to systems proposed to date are based largely on definitions of DSSS and Spread Spectrum Systems
  FCC looking for Industry input
    Good chance issues can be addressed in 99-231
    maybe trade power for processing gain

## Slide 9: How should we proceed?
If we do not get a rule change
  No system providing >20 Mbps in the current channel scheme will be approved
If we work with the FCC
  Possibly get this issue addressed in 99-231
  All high rate systems could be authorized
    then we just pick the best technical solution
Working with FCC is fastest path to market
  …because it’s the ONLY path to market.