## Slide 1: Ultra-Short Preamble Option for HRb OFDM
Mark Webster
Intersil Corporation

## Slide 2: Preambles Shorter than 802.11b’s
Is it possible to run preambles shorter than 802.11b’s?
What degree of 802.11b backward compatibility is guaranteed?
What is the coexistence behavior?
Impact of non-friendly interference.
This submission examines these issues.
A new optional ultra-short preamble for HRb OFDM is proposed.
The compatibility with 802.11b is described.

## Slide 3: The Wireless Medium is a Shared Resource
The wireless medium is shared.
Many stations exist in a cell, only one can transmit at a time.
Collisions create a packet-error near probability 1.
Hidden nodes can exist.
802.11b deferral mechanisms ensure “the many” remain silent while “the one” transmits.
For interoperability and coexistence, HRb proposals must provide deferral mechanisms.
Deferral mechanisms allow a transmitter to seize-the-channel.

## Slide 4: 802.11b Deferral Mechanisms
HIGHEST-to-LOWEST NETWORK LEVEL
PCF Point Control
Network Allocation Vector (NAV) control
SIFS, PIFS, DIFS and EIFS
Successful Header Reception
Clear Channel Assessment (CCA)

## Slide 5: Preambles Shorter than 802.11b’s Short Preamble Sacrifice Deferral Mechanisms
HIGHEST-to-LOWEST NETWORK LEVEL
PCF Point Control
Network Allocation Vector (NAV) control
SIFS, PIFS, DIFS and EIFS
Successful Header Reception
Clear Channel Assessment (CCA)
Is CCA Sacrificed?

## Slide 6: Two Aspects of CCA
10
usecs
SIFS
Data
ACK
Noise Floor
Rcvd
Power
dBm
First Aspect
Detect Packet Onset
Slot contention
Second Aspect
Detect Packet Body
Prevent Interference

## Slide 7: How Short Can the Barker Codes Be And Still be 802.11b CCA Compliant?
HEADER
48 BITS
@ 2 Mbps
PREAMBLE
72 BITS
@ 1 Mbps
PSDU
SELECTABLE
@ 2, 5.5 OR 11 Mbps
802.11b SHORT PREAMBLE
96 usecs
Barker Codes
KEY QUESTION
Is there a shorter Barker sequence that guarantees
useful CCA for deployed 802.11b equipment
when the SFD/header is not detected?
Cf. OFDM in the 2.4 GHz Band
Jan Boer, Lucent Technologies
Doc.: IEEE 802.11-00/188

## Slide 8: 802.11b’s Minimal Intent (Handle 802.11b Signals Properly)
HEADER
48 BITS
@ 2 Mbps
SYNC
56 BITS
@ 1 Mbps
PSDU
SELECTABLE
@ 2, 5.5 OR 11 Mbps
802.11b SHORT PREAMBLE
96 usecs
Barker Codes
SFD
16 BITS
@ 1 Mbps
Equipment with Long Preamble Only:
Detect the presence a short preamble and defer.
Time constraint is the length of short preamble.
Recovery of SFD, header and data is not required.
Equipment with Short Preamble Option:
Detect the long or short preamble, demod header and data.
Behavior is not spec’d for missing SFD or header.
MAC Deferral
Mechanisms
Length
Field

## Slide 9: Shorter than 802.11b’s Short Preamble
HEADER
48 BITS
@ 2 Mbps
SYNC
56 BITS
@ 1 Mbps
PSDU
SELECTABLE
@ 2, 5.5 OR 11 Mbps
802.11b SHORT PREAMBLE
< 96 usecs
Barker Codes
SFD
16 BITS
@ 1 Mbps
Equipment with Long Preamble Only:
No guarantee that deployed equipment defers properly.
Equipment with Short Preamble Option:
Behavior is not spec’d for missing SFD or header.
Missing SFD is indicative of a non-802.11b signal.
No guarantee that deployed equipment defers properly.
MAC Deferral
Mechanisms
Length
Field

## Slide 10: Proof Why Preamble Cannot be Shortened (by counter-example)
HEADER
48 BITS
@ 2 Mbps
SYNC
56 BITS
@ 1 Mbps
PSDU
SELECTABLE
@ 2, 5.5 OR 11 Mbps
802.11b SHORT PREAMBLE
72 usecs Barker Codes
SFD
16 BITS
@ 1 Mbps
AGC on 1st Diversity Antenna
DC offset null ZIF architecture
Energy Assess
AGC on 2nd Diversity Antenna
DC offset null ZIF architecture
Channel matched filter design and load
Allow for start-up transient decay
PLL and Coherent AGC jam
Commence SFD correlation
Successful long/short SFD flags high-rate PHY signal
KEY CONCEPT: A particular implementation may consume all of
short preamble/SFD to perform signal detection, especially if it
is not short-preamble capable.
Receiver has acquired (locked)
the Barker code and
data is being demodulated
24 usecs
Barker Codes

## Slide 11: Bluetooth Example
802.11b WLAN
Bluetooth
Thing-a-Ma-Jig
Access Point can hear laptop fine.
Laptop can hear Access Point fine.
Laptop sees low-level Bluetooth interference.
Absence of SFD flags non-802.11b signal.
Why should 802.11b defer to Bluetooth?
802.11b WLAN

## Slide 12: Examine 802.11b CCA Constituents
CCA time spec at < 15 usecs
CCA has 3 options 1. Energy Detect 2. Carrier Sense 3. Energy Detect plus Carrier Sense
Deployed equipment configuration & re-configuraton?
What is Carrier Sense?
What is Energy Detect?
Does 802.11b specify behavior if neither short or long preamble SFD’s are observed?

## Slide 13: 802.11b Carrier Sense
18.4.5.13 PMD_CS.indicate
This primitive, which is generated by the PMD, shall indicate
to the PLCP layer that the receiver has acquired (locked) the
Barker code and data is being demodulated.
18.4.5.13.1 Function
This primitive, which is generated by the PMD, shall indicate
to the PLCP layer that the receiver has acquired (locked)
the Barker code and data is being demodulated.
Reaction time not specified.
Barker sequence shorter than the 802.11b short preamble may be missed!

## Slide 14: 802.11b Energy Detect
18.4.5.14 PMD_ED.indicate
18.4.5.14.1 Function
This optional primitive may be generated by the PMD to provide
an indication that the receiver has detected RF energy indicated
by the PMD_RSSI primitive that is above a predefined threshold.
18.4.5.14.3 When generated
This primitive is generated by the PHY sublayer when the PHY
is receiving RF energy from any source that exceeds the
ED_THRESHOLD parameter.
Spoofed by Bluetooth
Spoofed by uWave Ovens

## Slide 15: 802.11b Clear Channel Assessment (CCA)
18.4.8.4 CCA
The High Rate PHY shall provide the capability to perform CCA according to at
least one of the following three methods:
a) CCA Mode 1: Energy above threshold. CCA shall report a busy medium upon
detecting any energy above the ED threshold.
b) CCA Mode 4: Carrier Sense with timer. CCA shall start a timer whose duration
is 3.65 ms and report a busy medium only upon the detection of a High Rate PHY
signal. CCA shall report an idle medium after the timer expires and no High Rate
PHY signal is detected. The 3.65 ms timeout is the duration of the longest possible
5.5 Mbit/s PSDU.
Reaction time not specified.
AGC’d pull-in time must be allotted.
Choose 1 of 3

## Slide 16: 802.11b CCA cont’d
18.4.8.4 CCA (cont’d)
c) CCA Mode 5: A combination of Carrier Sense and energy above threshold. CCA
shall report busy at least while a High Rate PPDU with energy above the ED
threshold is being received at the antenna. The energy detection status shall be
given by the PMD primitive, PMD_ED. The carrier sense status shall be given by
PMD_CS. The status of PMD_ED and PMD_CS is used in the PLCP convergence
procedure to indicate activity to the MAC through the PHY interface primitive
PHY-CCA.indicate.
The energy detection status shall be given by the PMD primitive, PMD_ED.
The carrier sense status shall be given by PMD_CS. The status of PMD_ED
and PMD_CS is used in the PLCP convergence procedure to indicate activity
to the MAC through the PHY interface primitive PHY-CCA.indicate.
A busy channel shall be indicated by PHY-CCA.indicate of class BUSY.
Clear channel shall be indicated by PHY-CCA.indicate of class IDLE.
Reaction time not specified.
AGC’d pull-in time must be allotted.

## Slide 17: CCA Mode 1: Energy Detect
10
usecs
SIFS
Data
ACK
Noise Floor
Rcvd
Power
dBm
First Aspect
Detect Packet Onset
Slot contention
Second Aspect
Detect Packet Body
Prevent Interference
Energy Detect is successful for both aspects
But, spoofed by Bluetooth, uWave Oven, etc.
ENERGY DETECT
THRESHOLD

## Slide 18: CCA Mode 2: Carrier Sense
10
usecs
SIFS
Data
ACK
Noise Floor
Rcvd
Power
dBm
First Aspect
Detect Packet Onset
Slot contention
Second Aspect
Detect Packet Body
Prevent Interference
Carrier Sense not always successful for both CCA aspects
Not, spoofed by Bluetooth, uWave Oven, etc.
BARKER Correlation may not
be valid until after
1. AGC lock
2. Diversity Decision
BARKER Correlation does
not detect
1. CCK
2. PBCC
CCA Mode 2 Timer
CS Exceedence
CS Timer
Clear

## Slide 19: CCA Mode 2: Carrier Sense Cont’d
10
usecs
SIFS
Data
ACK
Noise Floor
Rcvd
Power
dBm
Missing Long and Short SFD Indicates Invalid 802.11b Signal
Behavior not specified in standard
Missing Long/Short SFD
Clear timer
CS
Exceedence
CCA Mode 2 Timer

## Slide 20: Conclusion: Can Save Maybe Only 24 usecs of Barker Codes
HEADER
48 BITS
@ 2 Mbps
PREAMBLE
56 BITS
@ 1 Mbps
PSDU
SELECTABLE
@ 2, 5.5 OR 11 Mbps
802.11b SHORT PREAMBLE
72 usecs Barker Codes
SFD
16 BITS
@ 1 Mbps
24 usecs
Barker Codes
AGC on 1st Diversity Antenna
DC offset null ZIF architecture
Energy Assess
AGC on 2nd Diversity Antenna
DC offset null ZIF architecture
Channel matched filter design and load
Allow for start-up transient decay
PLL and Coherent AGC jam
Commence SFD correlation
Successful long/short SFD flags high-rate PHY signal
Not Needed for CCA Mode 1, 4 or 5
But, must convey header information somehow!
CONCLUSION
Insignificant Throughput
Benefit

## Slide 21
Now What?
Cannot guaranteed coexistence under general 802.11b.
So, design new mechanisms into HRb for better performance in the future.
Since throughput is king, propose an ultra-short preamble.
Coexistence is possible if 802.11b equipment uses CCA mode 1.
Provide as an option.

## Slide 22: Proposed Ultra-Short Preamble (~25 usecs of Overhead)
Data
Payload
PSDU
SELECTABLE
@ 6.6, 9.9, 13.2, 19.8, 26.4, 39.6, 52.8 or 59.4 Mbps
SIGNAL
SYMBOL
Data Rate
# bytes of data
Long
SYNC
16 usecs
3.6 usecs
Not coexistent with 802.11b unless CCA Mode 1
is used for all equipment.
12 Short
Syncs Rep’s
Signal
Extension
~6 usecs

## Slide 23: Ultra-Short Preamble Throughput
802.11b
Long
Preamble
HRb
Ultra-Short
Preamble
802.11b
Long
Preamble

## Slide 24: Ultra-Short Preamble Throughput
802.11b
Long
Preamble
HRb
Ultra-Short
Preamble
802.11b
Long
Preamble

## Slide 25
CCA Mode 1: Energy Detect by 802.11b Required for Ultra-Short Preamble Option
10
usecs
SIFS
Data
ACK
Noise Floor
Rcvd
Power
dBm
Identical to 802.11a
Coexistent with 802.11b if 802.11b equipment uses CCA Mode 1
ENERGY DETECT
THRESHOLD

## Slide 26: Carrier Recovery and Diversity
Carrier recovery performance same as 802.11a.
Locked oscillators mandatory.
Diversity same as 802.11a.

## Slide 27: Joint 802.11b-and-OFDM-only Detection Technique
ADC
Barker
Correlator
OFDM
Short-Sync
Correlator
Signal-Type
Decision