## Slide 1: A Contribution Towards Harmonization of IEEE 802.11a, HiperLAN2 and MMAC
D. Connors
H. Saam
Magis Networks
hsaam@magisnetworks.com

## Slide 2: Objectives
Providing uncompromising Quality of Service support
  voice, video and computer data applications
Cost effectiveness
  Avoiding un-necessary complexity
Focus on application support in the local area (home and office environments)
  Wide area mobility not an application requirement

## Slide 3: HiperLAN2, A High Level View
Main Features
  Synchronous MAC
  QoS support for isochronous traffic
  Centralized control
  Connection oriented
  DFS and TPC
Disadvantages
  RLC Complexity due to wide-area mobility
  Complex AP

## Slide 4: 802.11a MAC, A High Level View
Features
  Asynchronous MAC
  Distributed control
  Connectionless
  Out-of-band ARQ signaling (fast ARQ)
Disadvantages
  No QoS support for isochronous traffic
  No security
  Lack of robustness

## Slide 5: A Harmonized Approach
Adopt the H2 MAC framework
  Synchronous MAC
  Centralized control
Incorporate beneficial features of 802.11
  Fast ARQ
  Larger packet size (less overhead)
  Reduced L2-L3 interface complexity
  Distribute some bandwidth management functions
  Connection-oriented at Layer 2

## Slide 6: Other Features
Hardware Abstraction Layer
  supports a variety of hardware interfaces
Transmission security
  protecting sensitive media over the air

## Slide 7: Conclusion
No extensive legacy infrastructure exists today for either 802.11a or H2
Hybrid approaches are expensive and not justified based on existing market realities
A balanced and selective approach to 11a/H2 harmonization is more efficient and supports true universality
MMAC requirements need to be understood and facrtored in.
See white paper for more info.