## Slide 1: TGe Security Baseline
David Halasz, Stuart Norman, Glen Zorn
Cisco Systems, Inc.
Bernard Aboba, Tim Moore
Microsoft
Jesse Walker, Intel
Bob Beach, Symbol
Bob O’Hara, Informed Technology

## Slide 2: Outline
Introduction, Goals
MAC Management
Overview of 802.1X and EAP
Packet exchanges
Roaming
Sample topologies
Privacy Algorithms
Proposed 802.11 and 802.1X
Summary

## Slide 3: Introduction
Represents merger of proposals 163, 362, and 382
Define MAC security negotiation mechanism
Uses Kerberos V for authentication and fast handoff
Uses 802.1X and EAP as authentication transport
Addresses shortcomings of WEP/RC4 encryption
Works with Kerberos KDC and (optionally) RADIUS authentication server

## Slide 4: Goals
Extensible system
Authentication done at higher layer protocol
Per-session key distribution
Promote multi-vendor interoperability
Minimize changes to IEEE 802.11, 802.1X
Define mandatory authentication method
Fast handoff
Fix RC4 problems
Ability to add new authentication methods easily (without changing 802.11)

## Slide 5: Approach
Based on existing protocols
  Kerberos V (RFC 1510)
  GSS-API (RFC 2743)
  IAKERB (draft-ietf-cat-iakerb-05.txt)
  EAP-GSS (draft-aboba-pppext-eapgss-02.txt)
  802.1X/EAPOL
  EAP (RFC 2284)
802.11enhancements
  MAC security management
  New model for authentication/association sequences
  New privacy algorithm

## Slide 6: MAC Security Management
Provide means to register security algorithms
  Open, Shared, Upper Layer
Provide means to distribute security configuration information
  e.g. principal name, realm, etc.
Provide means to discover and select MAC level security options
  e.g. privacy algorithm, message authentication

## Slide 7: Registering Security Algorithms
Provide means to register a new security algorithm with IEEE 802 and obtain unique identifier for it
Three initial algorithms:
  Current ones: Open and Shared
  New one: Upper Layer
Others can be added later

## Slide 8: Advertising Security Options
Modeled on “supported rates”
AP advertises security options in probe response
  Placed in probe response only if STA requests it in probe request
STAs collect this information prior to associations and can make association and roaming decisions based upon it

## Slide 9: Selecting security options
STA requests security options in association request from available options contained in probe response
AP accepts/rejects association based on request contents
No additional protocol handshakes necessary
  No impact on roaming performance

## Slide 10: 802.11 to 802.1X adaptation layer
Supplicant
Authenticator
Supplicant
1 . . . N
One IEEE 802.11 physical port becomes 1 to N virtual IEEE 802.1X ports.
Map 802.11 association IDs to the virtual ports
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: IEEE 802.1X Terminology
Controlled port
Uncontrolled port
Supplicant
Authentication Server
Authenticator
Pieces of the system.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12
Normal Data
Authentication traffic
Wireless laptop
Authentication Server
Access Point
802.1X traffic
Authentication traffic
Wireless client associaton at 802.11 layer: Data blocked by the AP
Access Point blocks everything except 802.1X to authentication traffic.
Authentication traffic is allowed to flow. Access point encapsulates 802.1X traffic into authentication server traffic and vice versa.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13
Normal Data
Authentication traffic
Wireless laptop
Authentication Server
Access Point
802.1X traffic
Authentication traffic
Wireless client mutually authenticates with Authentication Server
Access Point blocks everything except 802.1X to authentication traffic.
In the authentication process the supplicant securely obtains a WEP key.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14
Normal Data
Authentication traffic
Wireless laptop
Authentication Server
Access Point
802.1X traffic
Authentication traffic
Wireless client and AP use WEP key, AP allows traffic to flow
After successful EAP authentication, the Access Point allows all traffic to the Wireless laptop.
The Wireless laptop sets the WEP keys through the MLME interface. (e.g. NIC driver)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: EAP Framework
EAP provides a flexible link layer security framework
  Simple encapsulation protocol
    No dependency on IP
    ACK/NAK, no windowing
    No fragmentation support
  Few link layer assumptions
    Can run over any link layer (PPP, 802, etc.)
    Does not assume physically secure link
      Methods provide security services
    Assumes no re-ordering
    Can run over lossy or lossless media
      Retransmission responsibility of authenticator (not needed for 802.1X or 802.11)
EAP methods based on IETF standards
  Transport Level Security (TLS) (supported in Windows 2000)
  GSS_API (including Kerberos)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: EAP Architecture
EAP
Layer
Method
Layer
EAP
TLS
Media
Layer
NDIS
APIs
EAP
APIs
PPP
802.3
802.5
802.11
IKE
GSS_API

## Slide 17: EAP-GSS and IAKERB
EAP-GSS (draft-aboba-pppext-eapgss-02.txt)
  Use of GSS_API authentication methods within EAP
  Typically will NOT use SPNEGO
IAKerb (draft-ietf-cat-iakberb-05.txt)
  GSS-API method enabling proxy Kerberos
  STA not able to talk to KDC directly prior to authentication
  Initial authentication
    IAKERB enables STA to obtain TGT, Ticket to AP
  Handoff
    Ticket to AP

## Slide 18: Initial Contact
Associate
EAP Identity Request
EAP Identity Response
EAP-GSS Request (Empty)
EAP-GSS Response (IAKERB: AS_REQ)
AS_REQ
EAP-GSS Request (IAKERB: AS_REP)
AS_REP
EAP-GSS Response (IAKERB: TGS_REQ)
TGS_REQ
EAP-GSS Request (IAKERB: TGS_REP)
TGS_REP
EAP IAKERB Response (Empty)
EAP-Success
EAP-Key (AP_REQ)
EAP-Key (AP_REP)
STA
AP
KDC
802.1X is Unblocked
802.11 is Unblocked
Probe Request/Response

## Slide 19: Operational Details
Authentication method defaults to IAKERB
  STA can attempt SPNEGO
  AP can choose IAKERB if it doesn’t support anything else
EAP-Key packets passed up and down via driver interface and 802.11 SAP
  On STA, GSS_API implementation needs to be able to generate AP_REQ, send it down to driver
  On AP, need ability to validate received AP_REQ, force 802.1X controlled port into authorized state
802.11 encryption turned on after AP_REQ/AP_REP exchange
  AP turns on encryption after sending AP_REP
  STA turns on encryption after receiving AP_REP
  If EAP-Key exchange occurs prior to completion of 802.1X, then part of the 802.1X exchange may be encrypted!

## Slide 20: Security Services
Authentication of client to KDC (TGS_REQ)
  PADATA typically NOT used with AS_REQ!
Authentication of KDC to client (AS_REP, TGS_REP)
Session key for client-AP communication (TGS_REP, AP_REQ)
TGT, Session key for client-KDC communication (AS_REP)
Authentication of client to AP (AP_REQ)
Authentication of AP to client (AP_REP)

## Slide 21: Roaming Within Realm
Associate
EAP Identity Request?
EAP Identity Response?
EAP-Success
EAP-Key (AP_REQ)
EAP-Key (AP_REP)
STA
AP
KDC
802.1X is Unblocked
802.11 is Unblocked
Probe Request/Response

## Slide 22: Roaming Issues
How does the STA discover the AP realm, principal name?
  Realm, Principal name placed in Probe Response if asked for by the STA
How does the AP obtain the authorizations for the supplicant?
  Can contact RADIUS server
    Adds an extra roundtrip
    No authorization-only message in RADIUS
  Contact with backend server undesirable
    Kerberos tickets are reusable, don’t require KDC validation
    RADIUS server typically unable to validate the AP_REQ, since it won’t have access to the AP key
    Eliminating backend server contact reduces latency
  Authorizations included in Authorization data of AP ticket
    Authorizations obtained by KDC from RADIUS server on initial contact and plumbed by the AP on ticket/authenticator validation

## Slide 23: RADIUS Topology
Authenticator
(e.g. Access Point)
Supplicant
Enterprise Network
Semi-Public Network /
Enterprise Edge
AuthenticationServer
RADIUS
EAP Over Wireless (EAPOW)
EAP Over RADIUS
PAE
PAE

## Slide 24: Kerberos Topology
Authenticator
(e.g. Access Point)
Supplicant
Enterprise Network
Semi-Public Network /
Enterprise Edge
AuthenticationServer
KDC
EAP Over Wireless (EAPOW)
EAP-GSS with IAKERB
Kerberos
PAE
PAE

## Slide 25: RADIUS with EAP-GSS Topology
Authenticator
(e.g. Access Point)
Supplicant
Enterprise Network
Semi-Public Network /
Enterprise Edge
AuthenticationServer
RADIUS
EAP Over Wireless (EAPOW)
EAP-GSS with IAKERB
EAP-GSS Over RADIUS
PAE
PAE
KDC

## Slide 26: Broadcast Key Distribution
Broadcast key(s) gets securely delivered to the station via IEEE 802.1X EAPOL-Key.
  EAPOL-Key message encrypted using session key obtained in AP_REQ/AP_REP exchange
Authentication server timer gets configured to re-authenticate/re-key the client.

## Slide 27: Addressing WEP Limitations
The problems with 802.11 use of WEP
Short Term fixes to WEP
Using AES as new privacy algorithm

## Slide 28: WEP Analysis
The WEP encapsulation suffers from 3 major design flaws
  IV too small (generic flaw)
  Per-packet key construction by concatenating IV to key (generic flaw)
  No weak-key avoidance (RC4 specific flaw)
Together these problems render WEP privacy meaningless at any key size

## Slide 29: Short term fix proposal
Replace the too-small IV with a 128-bit IV
  Goal is 2128 per-packet keys to avoid definition of an IV avoidance algorithm
Compute per packet key in a new way
  XOR IV with base key
Compatible with existing RC4 hardware
New packet format required

## Slide 30: Short Term WEP Format
802.11 Hdr
128-bit IV
Data
WEP ICV
802.11 Hdr
128-bit IV
Encrypt
Decrypt
Data
WEP ICV

## Slide 31: Long term solution
Use AES-128 as the new cryptographic primitive
Use AES in Offset Codebook Mode OCB mode
  128-bit session key
  per packet 128-bit IV
  algorithm provides both privacy and data integrity
  avoid 2 passes over packet
Add session sequence number to avoid replay
Map base key to session key
  use OCB mode tag to compute session key, to minimize number of cryptographic primitives implemented

## Slide 32: Long Term WEP Format
802.11 Hdr
128-bit IV
Seq Num
Data
128-bit MIC
Seq Num
Data
802.11 Hdr
128-bit IV
128-bit MIC
Encrypt
Decrypt

## Slide 33: Changes to 802.1X
EAPOL-Key message used to carry AP_REQ/AP_REP exchange
EAPOL-Key message needs to go from Supplicant (STA) to Authenticator (AP)
  802.1XD8 spec only supports sending EAPOL-Key from Authenticator to Supplicant

## Slide 34: Mapping to Requirements (1)
Mutual authentication (4.1.1): satisfied by Kerberos V
Accommodation with QoS (4.2.1): satisfied by Kerberos V
Access control (4.2.2): GSS-API can be integrated into 802.11 access control model
Key derivation (4.4.1): satisfied by all GSS-API mechanisms
Security service negotiations (4.5.1): satisfied by EAP or SPNEGO pseudo-mechanism
Extensibility (4.5.2): extensibility via EAP or GSS-API

## Slide 35: Mapping to Requirements (2)
One mandatory-to-implement algorithm (4.5.3): Kerberos V only mandatory-to-implement security mechanism
Scalability to all 802.11 environments (4.6)
  Mandatory to implement mechanisms support Enterprise, SoHo
  PKINIT for ad hoc support
Security framework must protect network traffic from eavesdropping: satisfied by RC4 Fixes/AES (4.3.1)
Security framework must allow for authentication of the source of each packet: satisfied by AES with sequence number (4.3.3)

## Slide 36: For Further Investigation
Simulation of AES computational load
Roaming authorizations
EAP negotiation and support for additional authentication types
Integration of 802.1X and 802.11 state machines

## Slide 37: Summary
This proposal will promote multi-vendor interoperability by making authentication an upper layer function based on 802.1X
Largely based on existing protocols with minor changes to 802.11
Changes to 802.1X specification should be made to enable transmission of keys from STA to AP
Changes to the IEEE 802.11 specification should be made to allow for mixed WEP cells and for more secure WEP data packets.

## Slide 38: For More Information
AES
  http://www.nist.gov/aes
IEEE 802.1X
  http://grouper.ieee.org/groups/802/1/pages/802.1x.html
Kerberos/GSS-API
  http://www.ietf.org/rfc/rfc1510.txt (Kerberos V)
  http://www.ietf.org/rfc/rfc2743.txt (GSS-API)
  http://www.ietf.org/internet-drafts/draft-ietf-cat-iakerb-05.txt
RADIUS
  http://www.ietf.org/rfc/rfc2138.txt
  http://www.ietf.org/rfc/rfc2139.txt
  http://www.ietf.org/rfc/rfc2548.txt
  http://www.ietf.org/rfc/rfc2865.txt
  http://www.ietf.org/rfc/rfc2866.txt
  http://www.ietf.org/rfc/rfc2867.txt
  http://www.ietf.org/rfc/rfc2868.txt
  http://www.ietf.org/rfc/rfc2869.txt
EAP
  http://www.ietf.org/rfc/rfc2284.txt
  http://www.ietf.org/rfc/rfc2716.txt
  http://www.ietf.org/internet-drafts/draft-aboba-pppext-eapgss-02.txt