## Slide 1: Traffic Police Enhancement for E-DCF
Liwen Wu, liwwu@cisco.com (408-853-4065)
Bob Meier, rmeier@cisco.com (330-664-7850)
Doug Smith, dsmit@cisco.com (905-305-0045)
Cisco Systems

## Slide 2: What is Traffic Police
Traffic Police allows AP to limit the traffic from a single station

## Slide 3: Why Traffic Police
Prevent unwanted excessive amount of traffic from going through AP into wired network
Prevent a abusive station from taking radio resources away from other stations of the same traffic category
Prevent premium class traffic from starving the best effort traffic
An ISP operator may want to have a option not letting best effort user to use more than what they paid for.

## Slide 4: When all Stations send data within its limit
Shared Radio medium

## Slide 5: When One Station is abusing the radio resource, other stations get less than they suppose to get
Shared Radio medium

## Slide 6: Where do we use Traffic Police
In Public Access environment, where stations are untrusted entities, such as:
  Airports(e.g. DCF)
  Hotel(e.g. DCF)
  Conference(e.g. DCF)
  Internet Café(e.g. DCF)
  last mile(e.g. PCF)

## Slide 7: How to Traffic Police
Traffic Police inside AP, drop the unwanted excess packets.
  Draw back: This does NOT protect radio resource
Traffic Police on radio medium access

## Slide 8: Traffic Police Proposal for DCF
Define a new Action Code in Action Frame
  category code=1; QoS management
  action code = 10; traffic police
EAP can send an “Traffic Police” Action frame to:
  a ESTA, to police that station
If a ESTA station is the RA of this “Traffic Police” Action frame, it must set its NAV to the value specified in the ‘Duration’ field.

## Slide 9: Traffic Police of a ESTA
data1
data2
exceed the limit!!!
“Traffic Police”
data4
wait
Ack
Ack

## Slide 10: 802.11 Compatibility
All 802.11 stations will set their NAV to the value in the ‘Duration’ field . Then, they all have to wait for that time period
. All other 802.11e stations will ignore this ‘Duration’ field