## Slide 1: DSRC Coexistence
November 2013
Rich Kennedy, Self
Slide <number>
Date: 2013-11-11
Authors:
Notes: doc.: IEEE 802.11-13/1327r0
April 2009
        Rich Kennedy, Self
Page <number>

## Slide 2: Abstract
Rich Kennedy, Self
This presentation describes the DSRC technology, the regulatory requirements for sharing the 5.9 GHz spectrum, and how we propose to move forward with a plan to enable regulators to open this spectrum to allow IEEE 802.11 technologies to operate in this band.
November 2013
Slide <number>
Notes: doc.: IEEE 802.11-13/1327r0
April 2009
        Rich Kennedy, Self
Page <number>

## Slide 3: Agenda
DSRC basics
FCC Part 15 basics
Existing 802.11 sharing mechanisms
Sharing with DSRC
Project to incorporate sharing in 802.11ac
Rich Kennedy, Self
November 2013
Slide <number>

## Slide 4: DSRC Basics
Dedicated Short Range Communications
5.9 GHz DSRC is essential for V2V crash-imminent safety applications, and must be protected from U-NII-3 and U-NII-4 devices.
V2V safety has stringent communications requirements, but future pre-crash and automation requirements may be even more stringent.
All current DSRC channels are needed for future applications and re-channelization and channel use rule changes are not feasible.
Currently in final stages of U.S. DOT NHTSA mandate decision.
Thorough testing is needed to determine whether sharing with U-NII devices is possible.
November 2013
Rich Kennedy, Self
Slide <number>

## Slide 5: Dedicated Short Range Communications (DSRC)
November 2013
Slide <number>
Standards
  IEEE: 802.11p, 1609.2 – 1609.4, 1609.12
  SAE: J2735, J2945
V2V Basic Safety Message (BSM)
  Average message size: ~320 to 350 bytes
  Default transmit rate: 10 Hz
    More sophisticated protocols in development
  Default transmit power: 20 dBm
  Enables multiple V2V Safety Applications
75 MHz of spectrum @ 5.9 GHz for ITS
Key Benefits
  802.11p technology similar to 802.11a
  Low latency communication (<< 50 ms)
  High data transfer rates (3 – 27 Mbps)
  Line-of-sight, up to 1000 m and 360º
  Low power message reception (< -90 dBm)

## Slide 6: V2V Safety Communications – Summary
November 2013
Slide <number>
  Different manufacturers
  Communicating on the same channel
  Exchanging the same BSM information
  Enables multiple V2V safety applications
Forward Collision Warning (FCW)
Blind Spot / Lane Change Warning (BSW / LCW)
Do Not Pass Warning (DNPW)
Intersection Movement Assist (IMA)
Left Turn Assist (LTA)
Emergency Electronic Brake Lights (EEBL)

## Slide 7: DSRC Coexistence Tiger Team
What should be the outcome from the group?
  Set of coexistence requirements for 802.11 in the 5 GHz band with ITS safety of life and property communications in the 5.9 GHz band
  Form a group to provide a formal interface to other organizations in the automotive industry, NHTSA, DOT and other ITS players
What is the required milestone timeline
  Dependent upon the FCC et al, progress on the rollout of the standards, technologies and laws
  Outcome of experiments prior to rulemaking; proof of concepts
  CAMP/DOT testing and validating
November 2013
Rich Kennedy, Self
Slide <number>

## Slide 8: Some Part 15 Basics
15.1 “…an intentional, unintentional, or incidental radiator may be operated without an individual license.”
15.5(b) Operation of an intentional, unintentional, or incidental radiator is subject to the conditions that no harmful interference is caused and that interference must be accepted that may be caused by the operation of an authorized radio station, by another intentional or unintentional radiator, by industrial, scientific and medical (ISM) equipment, or by an incidental radi- ator.
November 2013
Rich Kennedy, Self
Slide <number>

## Slide 9: Existing 802.11 Sharing Mechanisms
The success of 802.11 devices relies on its ability to share with other 802.11 WLAN devices
Other mechanisms have been devised for sharing with non-802.11 devices for special cases
  DFS to protect radars in the 5 GHz bands
    Required in 5250 to 5350 MHz and 5470 to 5725 MHz bands
    Detection and avoidance of interference with radars
  Geo-location Database to protect broadcast equipment in the TV bands
    Approved for unlicensed operation in TV bands
    To transmit, devices access a database to determine available, unused channels, based on geographic location and time, and the device transmit power
November 2013
Rich Kennedy, Self
Slide <number>

## Slide 10: Sharing with DSRC
Study group will determine the best sharing approach
  Based on maximizing spectrum utilization
  Must meet requirements determined by regulation and approval of the DSRC community
  Primary allocation protection is paramount
DSRC community will participate
November 2013
Rich Kennedy, Self
Slide <number>

## Slide 11: Project to Develop Sharing in 5.9 GHz
If IEEE 802.11 is to utilize the 5.9 GHz band, the sharing mechanism must be added to the standard
A Study Group should be formed to develop a PAR and 5 Criteria to start this project
November 2013
Rich Kennedy, Self
Slide <number>

## Slide 12: References
Harmful Interference to DSRC Systems: 11-13/1309r0
DSRC PER versus RSS Profiles: 11-13/1360r0
November 2013
Rich Kennedy, Self
Slide <number>