## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: WATM and BRAN Liaison Presentation
Date Submitted: November 8, 1999
Source: Lou Dellaverson Company: Motorola
Address [Add address Street, City, PC, Province/State, Country]
Voice:[Add telephone number], FAX: [Add FAX number], E-Mail: lpd@interaccess.com
Re: Response to Liaison Request to WATM and ETSI BRAN
Abstract: Review of Collaboration between MMAC, WATM and BRAN
Purpose: Informational to Working Group
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
ETSI BRAN Project

## Slide 3: Scope of the ETSI BRAN Project
BRAN got underway in April 1997
To subsume work of RES10 and TM4 on broadband access
To develop standards for
  Short range broadband radio access systems (HIPERLAN type 2) with portable or slowly moving terminals
  Broadband fixed radio access systems (HIPERACCESS)
To stimulate spectrum allocation for such applications in Europe
  2 / 5 / 10 / 17 / 28 / 40 / 60 GHz
To co-ordinate standard development work
  with core network fora as IETF, ATM Forum, etc.
  with peer fora as ETSI-UMTS, 3GPP, IEEE, MMAC, etc.
Notes: Page <number>
        <footer>
<header>
<date/time>
ETSI’s Broadband Radio Access Networks project has been set up to address the standardization of broadband systems for indoor, cordless systems as well as outdoor, fixed access systems. The common elements are more important than the differences in the environments in which they are used: The typical bit rates is in the range of 25 Mb/s but higher bitrates, up to 155 Mb/s will be possible. Multiplexed over a number of users this gives data rates from 16 kb/s to as much as 16 Mb/s per users.
The scope of the project is to develop the necessary specifications and to work with other fora when it comes to interworking with core networks. This approach avoids the duplication of effort and content that could occur when the project would develop all specifications independently.
Finally, the project works with what might be called peer fora: fora which have work in hand to develop specifications for the same type of system in the same frequency range. Examples are the IEEE 802.11 committee that started a workitem on a 20 Mb/s, 5 GHz version of its current standard; the Japanese Mobile Multimedia Access Communications (MMAC) Promotion Council which currently has work in hand for a 18 GHz system for cordless indoor and outdoor use. And there are is ETSI SMG3, the architecture group responsible for UMTS. Here the intent is to align the access network standards to allow the same applications and services to be offered over both UMTS and broadband access networks.

## Slide 4: Standards for High-Speed Wireless LANs
Europe (ETSI Project BRAN = Broadband Radio Access Networks):
  HIPERLAN1 in 5 GHz developed by RES10 & being maintained by BRAN
  New standard HIPERLAN2 in 5 GHz
    The first phase (support of business applications) ready in 1999
    The second phase (support of home applications) ready in early 2000
U.S. (IEEE):
  IEEE802.11 originally developed for 2.4 GHz with bit rates up to 2 Mbps
  A physical layer with bit rates up to 11 Mbps is currently developed for 2.4 GHz
  New physical layer in 5 GHz band with increased data rates (802.11a)
Japan (MMAC = Multimedia Mobile Access Communication):
  Three standards under development for high speed applications in 5 GHz
    a 802.11a like system
    a HIPERLAN2 like system
    a system for wireless home applications
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 5: Spectrum Allocation at 5 GHz
5.200
5.300
5.400
5.500
5.600
5.700
5.800
5.900
5.100
Europe
USA
Japan
Freq./GHz
5.350
5.150
5.150
5.250
5.350
5.725
5.825
5.150
5.470
5.725
Outdoor 1W EIRP
Indoor 200 mW EIRP
Indoor 200 mW / Outdoor 1 W EIRP
Max mean Tx power
Outdoor 4 W EIRP
Max peak Tx power
DFS & PC
DFS & PC
DFS: Dynamic Frequency Selection
PC: Power Control
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 6: Broadband Radio Networks
HIPERACCESS
HIPERLINK
SERVER
HIPERLAN
HIPERLANs
Notes: Page <number>
        <footer>
<header>
<date/time>
9
The figure shows an example of how the three network categories might be deployed in a business and domestic environment. In both cases, HIPERACCESS provides the means to reach the premises of the customer.
In the business case, HIPERLINK is used internally in the building HIPERLAN is used to as basic local area network giving the employees access to the server. HIPERLINKs are used to complete the wireless infrastructure and link the HIPERLAN access point to the server and to HIPERACCESS.
In the residential example, HIPERLAN is coupled directly to HIPERACCESS.
In both cases, variants with different mixtures of wired and wireless networks are possible.

## Slide 7: Positioning - Mobility vs. Bitrate
Mbps
1
10
100
0,1
Outdoor
Stationary
Walk
Vehicle
Indoor
Stationary/ Desktop
Walk
Mobility
HIPERLAN/2
User Bitrates
LAN
W-CDMA/ EDGE
Bluetooth
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 8: Positioning - Cost vs. Bitrate
W-CDMA/
EDGE
Mbps
1
10
100
0,1
User Cost / bit
HIPERLAN/2
User Bitrates
LAN
Bluetooth
Low
Medium
High
Very Low
$
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 9: Wireless LAN Topologies
Peer-to-peer Topology
  Communication between stations directly in an ad hoc network
    No need for any infrastructure or access point
    Useful in the case of temporary networking for emergency communication
Star Topology
  Communication between stations via access points connected to the backbone network
    Useful for providing wireless coverage of buildings or premises Areas
Access Point
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 10: HIPERLAN2 Features - 1
For short range wireless access to “very” high rate applications
  Business and Home applications
Core network independent with QoS support
  Support of IP transporting networks, ATM networks, Firewire, etc.
Radio sub-system specifications (physical layer, data link control layer and convergence layer)
  Interoperability standard with conformance test specifications
A cellular multi-cell radio network capable of offering access, switching and management functions within a large coverage area
  Centralized mode (mandatory) and direct mode (optional)
Capable of handling different interference and propagation situations
  “Link Adaptation” with multiple modulation and channel coding schemes
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 11: HIPERLAN/2 Features - 2
Indoor and outdoor usage
Supporting asymmetrical traffic load in up- and downlink and for different users
Scalable security
  56 to 168 bit key encryption (DES), optional pre-shared or public-key authentication
LAN mobility and IP roaming management
Low power consumption by using uplink power control, downlink power setting, sleep mode
Globally available
Physical layer is aligned with IEEE 802.11a & MMAC
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 12: HIPERLAN2 in Wireless LAN Scenarios
SGSN
GGSN
IWU
Office
ISP
Home
GPRS/UMTS
Ethernet
Internet
HIPERLAN2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 13: HIPERLAN2 Protocol Stack
IP
Ethernet
H/2
H/2
Ethernet
Control plane
User plane
PHY
EC
Convergence Layer
Access
Point
Terminal
Adapter
RLC
DLC
MAC
Logical channels
Transport channels
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 14: Convergence Layer
Cell based
Packet based
ATM
Segmentation and re-assembly to / from 48 bytes packets
Priority mapping from IEEE 802.1p
Address mapping from IEEE 802
Multicast & broadcast handling
Flexible amount of QoS classes
PPP
Firewire
Ethernet
Multiple convergence layers
One single convergence layer active at a time
Mapping between higher layer connections/priorities and DLC connections/priorities
UMTS
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 15: HIPERLAN / 1
“Wireless Ethernet”
  Topology: peer-to-peer structure
  Traffic: Connectionless data transfer, time-critical services (voice, video)
  Multiple access scheme: CSMA with collusion avoidance
  Quality of Service (QoS): best effort service, no QoS guaranty
Radio sub-system specifications (physical layer, medium access control sub-layer)
  Interoperability standard with conformance testing Operating
Data rat up to 23 Mbps (carrier spacing in the order of 23.5 MHz)
No link adaptation, no DFS, no Tx power control
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 16: Basic Approach
Network Convergence sublayer
ATM Network
BRAN DLC -1
BRAN PHY -1
IP Network
UMTS Network
Notes: Page <number>
        <footer>
<header>
<date/time>
11
7
The basic approach to core network independence is the introduction of a Core Network Convergence sublayer where the differences between the different core networks are removed and a common BRAN interface can be used. The difference between the core networks occur in three main areas: call set-up and clearing, changing connections within the network and management of the quality of service provided to the network user. Mapping the different mechanisms or filling in for the absence of certain mechanisms will be performed with the convergence sublayer. The specification of these sublayers will be done in cooperation with the forum that owns the core network standard, e.g. the ATMForum in case of ATM Core networks.
This interface is at the top of the BRAN specific Data Link Control layer. The implication of this approach is that the DLC layer specification must be carefully matched to the superset of the requirements for supporting ATM and IP traffic.
There may be different specifications of the DLC layer - that will be resolved during the actual specification work. However, in view of the various frequency bands in which these networks will operate, a number of different radio physical layers will have to be specified by the project

## Slide 17: Reference Model
Wireless
Terminal
Adapter
Wireless
Access Point
Core
Network
User
AN.0
AN.1
Core
Network
e.g.
ATM, N-
ISDN or
TCP/IP
AN.2
AP
Trans-
ceiver
AP
Controller
Wireless
Subsystem
AN node
Core
Network
specific
IWF
Wireless Access Network
Roaming
Support,
Authen,
security
Roaming
Support,
Authen,
security
BRAN Specifications
Core
Network
specific
IWF
Notes: Page <number>
        <footer>
<header>
<date/time>
12
6
The high level reference model used by the project as basis for its cooperation with the ATMForum and ETSI SMG is shown in this picture which also shows the scope of the work of the project.
The figure has in its centre the wireless access subsystem flanked by Core Network specific InterWorking Functions. Together, these make up the wireless access network functionality.
The IWFs support all core network specifics. Examples are not only call set-up and hand-over between access points but also security functions such as user authentication and data confidentiality.
The BRAN project is responsible for the wireless subsystem specifications and, together with the appropriate owner forum, it will develop the IWF specifications or provide the BRAN side of sucha specification and leave it to the other fora to fill in the core network specific part.
In approaching its scope in this way, the project is probably unique: it implements a modular approach to standardization and it shares its work with other fora.

## Slide 18
Multimedia Mobile Access Communications

## Slide 19
Study Committee
MPT formed MMAC (Multimedia Mobile Access
Communications ) study committee to study about the next
generation broadband mobile communication systems in 1995.
The MMAC report (issued in May 1996) suggests;
  - Early deployment of MMAC around 2000
  - Seamless access to backbone networks, e.g. ATM-NW
  - Trade-off of access speed and mobility (portability)
  - Two system concepts were identified.
    ・ High-speed wireless access
    - Broadband mobile/ubiquitous wireless access to
    both private and public services
    - Up to 25 Mbit/s using 3-60 GHz
    ・ Ultra-high-speed wireless LAN
    - Wireless LAN for private use only
    - Up to 156 Mbit/s, using 30-300 GHz

## Slide 20
Organization of MMAC-PC
Following the recommendation in the MMAC report,
MMAC Promotion Council was established in Dec. 1996 to
promote MMAC in cooperation with ARIB (Association of
Radio Industries and Businesses of Japan).
134 member companies participating the MMAC-PC(Jan.1999)
MMAC-PC organization
  - Technical Committee
  ・ High Speed Wireless Access Subcommittee
  ・ Ultra High Speed Wireless LAN Subcommittee
  ・ Two ad-hoc committees
  - 5GHz Band Mobile Access Ad-hoc Committee (New)
  - Wireless Home-Link Ad-hoc Committee (New)
  - Promotion Committee
  ・ Application Development Subcommittee
  ・ Popularization Promotion Subcommittee

## Slide 21
Outline of MMAC families

## Slide 22
Positioning of MMAC

## Slide 23
Application image of MMAC
Wireless access in
various environments
・ Home (indoor)
・ Office (indoor)
・ Premises
・ Public spaces
(outdoors and indoors)

## Slide 24
Liaison relationship with other organizations

## Slide 25
Service
Backbone network / interface
Environments
TM services
Mobility enabled A
TM networks
public / private
IP services
Mobility enabled IP networks
public / private
MAC services
Ethernet
mostly private
Ad-hoc services
Audio/Visual (e.g. TV set), PC etc
private
Hybrid/Dual mode services
Up: PHS/Cellular
Down: Mobility enabled IP networks
mostly public
"High speed wireless access subcommittee" and "5GHz band mobile
access ad-hoc subcommittee, ATM-WG"
Basic requirements
  - >20Mbit/s and 10Mbit/s max per user
  - Mobility support (pedestrian) and cell radius is 150-200m.
  - ATM cell transport over wireless and QoS support
  - Seamless access by standard air interface
  - Variety of services in various types of backbone networks
    Public: ATM, IP Private: Ethernet, IP, ATM etc.
ATM-based high speed wireless access using 5GHz

## Slide 26
Seamless roaming concept

## Slide 27
Harmonization: Importance of system commonality by global
standardization
  - Common frequency spacing, resulting in efficient frequency
  utilization
  - Common PHY, resulting in economical wireless terminal
  - Common frequency sharing rule, resulting in co-existence
  - Common air interface, resulting in inter-operability
  - Common air interface for various network interfaces,
  resulting in ubiquitous access
Concluding remarks (2)

## Slide 28
The ATM Forum
Wireless ATM: Mobile Networking

## Slide 29: The ATM Forum
The ATM Forum is an international non-profit organization formed with the objective of accelerating the use of ATM (Asynchronous Transfer Mode) products and services through a rapid convergence of interoperability specifications. In addition, the Forum promotes industry cooperation and awareness.
The ATM Forum consists of a worldwide technical Committee, three Marketing Committees for North America, Europe and Asia-Pacific as well as the Enterprise Network Roundtable, through which ATM end-users participate.
The ATM Forum

## Slide 30: ATM Forum Organization
Board of Directors
Secretariat Offices
Worldwide Headquarters
Mountain View, CA
Asia-Pacific Office
Tokyo, Japan
European Office
Brussels, Belgium
Enterprise Network Roundtable Committee
Working Groups:
European Activities
Marketing Communications
Technical Communications
Worldwide Communications
Asia-Pacific Market Awareness Committee
Working Groups:
Education
Interoperability & Demo
Marketing Communications
North America Market Awareness Committee
Working Groups:
Education
Interoperability Test & Demo
Marketing Communications
Market Requirements
Residential & Small Business
European Market Awareness Committee
Working Groups:
Information & Promotion
Education
Implementation, Market & Services
Worldwide Technical Committee
Working Groups:
Broadband ICI
LAN Emulation
Multiprotocol
Network Management
Physical Layer
Private NNI
Residential Broadband
Security
Service Aspects and Applications
Signalling
Testing
Traffic Management
Voice and Telephony Over ATM
Wireless ATM
The ATM Forum

## Slide 31: Charter
The Wireless ATM (WATM) working group will develop a set of specifications intended to facilitate the use of ATM technology for a broad range of wireless network access scenarios, both private and public. This specification will include both “mobile ATM” extensions for mobility support within an ATM network, as well as “radio access layer” for ATM-based wireless access. The WATM specifications are intended for use in networks involving terminal mobility and/or radio access, and will be designed for compatibility with ATM equipment adhering to the (then) current ATM Forum specification. Explicit liaison arrangements will be established with relevant standards bodies.
The ATM Forum
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 32: Work Items and Technical Scope Outlines
The following major work items have been identified for consideration by WATM working group.
  “Radio Access Layer” protocols including (but not limited to):
    A.1 Radio physical layer
    A.2 Medium access control for wireless channel (with QoS, etc.)
    A.3 Data link control for wireless channel errors
    A.4 Wireless control protocol for radio resource management
  “Mobile ATM” protocol extensions including (but not limited to):
    B.1 Handoff control (signalling/NNI extensions, etc.)
    B.2 Location management for mobile terminals
    B.3 Routing considerations for mobile connections
    B.4 Traffic / QoS control for mobile connections
    B.5 Wireless Network Management
The ATM Forum
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 33: Group Members
3Com Corp
Alcatel Telecom
Ameritech
AMP/Connectware
ANRITSU
Apple
ASCOM
AT&T
Bell Atlantic
Bell South
Bell South Wireless, Inc.
Bellcore
Boeing
British Telecom
CEL
Columbia University
COMSAT
CSELT
CSIRO
Desknet Sys
Deutsche Telecom
Dialogic Corp
DoD
DSC
DSC Comm
DSRC
Ericsson
ETRI
ETSI
FORE
Fujitsu
GDC
GOTD Fokers
GTE
GTE Ltd
HEA
Hitachi
Hughes
IBM
IDT
Intel
IST
ITI
Korea Telecom
Level One
Litton FiberCom
Lockheed-Martin
Lucent Tech
M/A-COM
Madge
MITRE
Motorola
NASA
NASA Lewis
National Comm System
NEC
Network General Corp
Newbridge
NIST
Nokia
Nortel
NTT
Oki
Olivetti Research Ltd
Pacific Bell
Philips Research
Qualcomm
Racal-Datacom
Samsung
Sandia National Labs
Sarnoff
SEC
SGS-Thomson
Siemens
Sierra Tech and Research
Sprint
SRTI
Sun
Symbionics
TASC
Telia Research
Tellabs
Toshiba
Trillium
US West
Yurie
ZAE
The ATM Forum

## Slide 34: Universal Access
Ad Hoc Communication
Satellite Link
Static Topology
Wired ATM Node
Fixed Wireless
Mobile End-Users
Mobile Infrastructure
The ATM Forum
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 35: WATM Relationship with Other Groups
Europe
ERC
ETSI
ACTS (EC R&D)
UMTS Forum
GSM MOU
ATM Forum WATM Working Group
International
ITU - T/R WRC
FPLMTS - IMT2000
Japan / Asia
TTC MPT
MMAC-PC
United States
FCC
WINForum
WINSpectrum
IEEE
802.11
TIA
The ATM Forum
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 36: Protocol Development Responsibilities
WATM Working Group
Radio Design Groups
User Groups
Application Interface
Q.2931m
SAAL
AAL-X
ATM
RADIO PHY
Mobile Terminal
RADIO DLC
Vendors
WATM Mobility Spec
WATM Radio Reqmts
Radio Spec
A single Mobility Specification will produce the maximum interoperability among all wireless and wireline ATM networks.
Each Radio Frequency and Spectrum Administration Region will have different usage rules requiring several Radio Physical Layer designs.
Other Standards Bodies
The ATM Forum
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 37: Fixed wireless network, Configuration 0
The ATM Forum
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 38: Network Support for Mobile End Users, Configuration 1
The ATM Forum
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 39: Network Support for PCS Access, Configuration 2
The ATM Forum
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 40: Network Support for Mobile Switches, Configuration 3
The ATM Forum

## Slide 41: Wireless Ad Hoc Networks, Configuration 4
The ATM Forum
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 42: What is Mobile ATM?
Mobile ATM has two major components:
1) Location Management - The ability to determine, topologically, the current location of the mobile terminal.
2) Mobility Management - The ability, of the network, to maintain an active connection as the mobile terminal moves through the infrastructure.
Both of these components place additional security requirements on the network.
The ATM Forum
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 43: Location Management Reference Configuration
EMAS-E
EMAS-E
RAS
RAS
RAS
LS/AUS
Inf. 3/4
RAS
LS
Inf. 3
EMAS-E
Domain 2
AUS
RAS
Location Response/Failure 2
EMAS-E
EMAS
RAS
RAS
Inf. 3/4
Domain 1
LS/AUS
RAS
The ATM Forum

## Slide 44: Handover Scenarios
EMAS-E1
EMAS-E2
MT
Intra-EMAS-E
Inter-EMAS-E
Intra-RAS
RAS1
RAS2
RAS3
The ATM Forum

## Slide 45: Registration with a New MSC
VLR
MSC
MSC
VLR
HLR
Old Network
New Network
REGNOT
REGNOT
regnot
regnot
REGCANC
regcanc
QUALREQ
qualreq
PROFREQ
profreq
REGCANC
regcanc
BS
CSS
Home
Network
Registration
Loc Update
Accepted
Registration Accept
The ATM Forum
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 46: Calling an Idle Mobile
VLR
MSC
PSTN
MSC
VLR
HLR
Serving Network
ROUTREQ
PROFREQ
profreq
ROUTREQ
routreq
(TLDN)
LOCREQ
routreq (TLDN)
locreq (TLDN)
IAM
SS7 Call Setup
Home Network
The ATM Forum
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 47: Immediate Call Forwarding
VLR
MSC
PSTN
MSC
VLR
HLR
Serving Network
LOCREQ
locreq (NULL)
IAM
SS7 Call Setup
Home Network
The ATM Forum

## Slide 48: Call Forwarding on Time-Out
MSC
PSTN
VLR
HLR
Serving Network
ROUTREQ
ROUTREQ
routreq (TLDN)
locreq (TLDN)
pagersp
TRANUMREQ
tarnumreq
REDREQ
redreq
BS
CSS
Home Network
IAM
LOCREQ
Paging Request
Page
MSC
routreq (TLDN)
SS7 Call Setup
SS7 Call Release
New Call
The ATM Forum

## Slide 49: VLR Loading
MSC Coverage Area
VLR
Assume:
L = 70 miles
 = 150 Users/Square Mile
n = 50 Miles/Hour
l = 3 Calls/User/Hour
Mobility
Assume: Random direction and constant velocity.
Rate of crossings = nL/p
46 Crossings per second generates
46 REGNOT upon Entry
46 REGCANC upon exit
92 Operations per Second
Call Termination
Assume: Equal number of in and out.
MSC Coverage Area =
46,000 Users/MSC
19 Call Terminations/Second
Each Call Termination generates a ROUTREQ
19 Operations per Second
The ATM Forum