## Slide 1: IEEE P802.15 Working Group for Wireless Personal Area Networks
MAC Performance Evaluation Process in a Coexistence Environment
Nada Golmie
NIST

## Slide 2: MAC Coexistence Model
Different performance levels will lead to different levels of coexistence:
  Coexistence could mean an “acceptable” performance level to be quantified.
At the MAC layer coexistence translates into a performance measure:
  What is the impact of interfering devices all sharing the 2.45 GHz ISM band on the MAC performance?
How to evaluate and quantify WPAN MAC performance?

## Slide 3: Objectives
The main goal of this contribution is to propose a methodology for conducting a performance evaluation of the WPAN MAC in presence of other wireless devices sharing the same air space.
The motivation is to agree on an evaluation process so that simulation/ experimental/ analysis results can be conducted independently by different parties and presented to the IEEE 802.15 SG.

## Slide 4: MAC Performance Evaluation Set Up
Traffic Models
PHY Layer
Assumptions
BT MAC
Traffic Models
802.11 MAC
PHY Layer
Assumptions
Traffic Models
BT MAC
Traffic Models
802.11 MAC
PHY Layer Assumptions
PHY Layer Assumptions
Network Topology
in a Coexistence Environment
Measure performance at the MAC layer
Identify MAC Specifications
Make assumptions on the PHY layer (interference/ propagation models) and traffic models

## Slide 5: MAC Coexistence Evaluation Process
The evaluation process of a given MAC layer protocol in a shared environment consists of:
  Usage scenarios
    User situations
    Applications
  Parameters
    Traffic generation models
    Network topology
    PHY layer assumptions
    MAC layer parameters
  Performance metrics

## Slide 6: Bluetooth User Situations *
Internet Bridge
Interactive Conference
Cordless Desktop
Headset/Portable speaker phone
Briefcase Trick
Forbidden Message
Automatic Synchronizer
Instant Postcard
    * www.bluetooth.com

## Slide 7: IEEE 802.11 User Situations
The Basic Service Set (BSS) consists of:
  Access Points (AP)
  Wireless Stations (STA)
Need to consider *:
  STAs density per area
  AP density per area
  Number of STAs per AP
  * refer to IEEE 802.15-99/073r0

## Slide 8: Coexistence User Situations
Office space situations
  desktop, interactive conference,
  automatic synchronizer, headset
Dynamic situations (anywhere else)
  internet bridge
  instant postcard
  forbidden message

## Slide 9: Applications
Telephony
Email
Web Browsing
File Transfer
Paging
Video Conferencing

## Slide 10: Traffic Generation Models
Traffic models that describe the distribution of the message size and interarrival time are derived from the application set considered.
Many traffic models exist in the literature for voice, data (FTP, HTTP), video traffic.
Illustrations from IEEE 802.14/96-083r2

## Slide 11: Network Topology
Number of devices in a piconet
Distance among devices in a piconet
Number of piconets

## Slide 12: Physical Layer Parameters and Assumptions
Frequency hopping
Interference model
  Power level
  BER
  Overlapping probability
Propagation model
  Path loss

## Slide 13: MAC Layer Parameters
Contention slot allocation
Slot scheduling algorithm
Timers: Flush, ACK
Packet size/compression
Backoff algorithm:
  contention window size (max, min)

## Slide 14: Performance metrics
Access delay (mean, variance, PDF):
  time to transmit a message
Collisions per slot
  average number of collisions per slot
Offered Load
  actual traffic presented to the network for transmission in bits/s
Throughput
  Measure in bits/s of the successful traffic transmitted excluding MAC and PHY overhead.

## Slide 15: Summary
Propose a methodology for MAC coexistence model evaluation.
List major components and provide examples for parameters, user situations, and performance metrics.
Details within each components are work in progress

## Slide 16: Next Step
Let’s start the debate
Agreement on this evaluation process
Solicit input to complete
  Usage situations
  Network Topology
  Parameters
RF
DATA
MAC
PHY