## Slide 1: Bluetooth Qualification Program
Thomas Müller, Waldemar Hontscha
Nokia Mobile Phones
Notes: Page <number>
        <footer>
<header>
<date/time>
Magnus Sommansson, working inside the BT Regulatory WG in the task force which is responsible for the establishment of the Qualification program. This task force is focusing on process, authority and information flow and not so much test case development, type approval issues or test and messurement equipment due to the fact that these issues are handeld in other task forces within the BT Regulatory WG. To some extent though the task force is coordinating the other issues.
The Bluetooth Qualification Program is the process by which an Adopter demonstrates that a particular product meets the requirements specified in the Specification as well as the Brand book.

## Slide 2: Qualification vs. Type Approval
Global Market
Bluetooth Devices
'Bluetooth License'
'License to sell'
Qualification Process
Regulatory Type Approval
&
Complies with
the specification ?
Notes: Page <number>
        <footer>
<header>
<date/time>
The Bluetooth Qualification Program is the process by which an Adopter demonstrates that a particular product meets the requirements specified in the Spcification as well as the Brand book.
Regulatory certification as such is not a part of the Bluetooth qualification requirements, yet a must in all markets. It is the sole responsibility of each manufacturer to ensure that their products have all necessary regulatory approvals for the markets where they are intended to be sold or used.
The Bluetooth SIG works for a global harmonisation of regulatory approval processes

## Slide 3: Qualification Program: Mission
Protect the Bluetooth Brand by ensuring
  good performance of products
  interoperability of products
  clearly stated product capabilities
Notes: Page <number>
        <footer>
<header>
<date/time>
This is the key enabler to high probabilty of achieving interoperability.
This is also very tight coupled to the market promises which was previously presented by Simon Ellis and the value of the brand which was previously presented by Anders Edlund.

## Slide 4: Compliance requirements
Radio link
Protocols (lower layers)
Profiles
Capability information to end-users
Notes: Page <number>
        <footer>
<header>
<date/time>
Details about this may be found in the Compliance chapter of the specification 1.0. Additions, modifications or clarifications will be issued on the qualification webpages.
The test specification for BT protocol requirements will be based on the BT specification Part B,C,D and H (Baseband, Link Manager, L2Cap and if applicable HCI)
The test specification fo BT profile requirements will be based on the BT specification part K (Profile specs)
The following must always be met:
The „generic access“ must always be complied to
All implemented service must be described in the „ICS“ according to each profile spec
All mandantory features of a profile role shall be implemented according to the profile specification
Rules and guidelines on how to use the Bluetooth Brand are stated in the document “The Bluetooth Brand Book” which is available on the Bluetooth Web site.

## Slide 5: Authorization of the Program
Bluetooth SIG -PM
Bluetooth Qualification
Review Board (BQRB)
Bluetooth
Qualification
Administrator
(BQA)
Bluetooth
Technical
Advisory Board
(BTAB)
Manage/review/improve qualification process
Administration of qualification program
Checking declarations, review test reports
Recognized test facility for Bluetooth products
Know-how exchange & forum for problems related to testing and qualification
Bluetooth
Qualification
Test Facility
(BQTF)
Bluetooth
Qualification
Body
(BQB)
Notes: Page <number>
        <footer>
<header>
<date/time>
The Program defines the following entities:
Bluetooth Qualification Review Board (BQRB) – responsible for managing, reviewing and improving the Bluetooth qualification program. The original Bluetooth SIG companies will appoint BQRB initial members
Bluetooth Qualification Administrator (BQA) - responsible for administering the Bluetooth Qualification Program on behalf of BQRB
Bluetooth Qualification Test Facility (BQTF) - a test facility that is officially authorised by BQRB to test Bluetooth products
Bluetooth Qualification Body (BQB) - a person authorized by the BQRB to be responsible for checking declarations and documents against requirements, reviewing product test reports, and listing products on the official database of Bluetooth qualified products
The BQB-function is the wrap up of the whole process of showing compliance. Eventhough it is the wrap up in the process some tasks not related to testing can be performed in parallel or semi-parallel to the tests.

## Slide 6: Bluetooth Qualification Process
BQA
BQTF
BQB
Manufacturer
Qualified
Products
Database
Qualification
Program Documents
Test Sample
& TCF
Test Report
& TCF
Application
& Declaration
of Compliance
Pull Documents
from Web site
Insert into Database:
Product Qualified!

## Slide 7: Early Bluetooth Products
Reduced Test requirements for qualification of “early products”
Initial Qualification Program to be launched End 1999
Additional info: www.bluetooth.com
Notes: Page <number>
        <footer>
<header>
<date/time>
Bluetooth products are in development even before the final specification is released. These early products may lack full compliance with the Bluetooth specification, but still incorporate sufficient functionality to merit release.
For this reason, the qualification program will consider listing products that have deviations from the Bluetooth specification as “Bluetooth Qualified”, until June 30, 2001.
A comprehensive Test Specification with validated test cases will not be available on the same schedule as the Bluetooth Specification. Consequently, BQTF product testing against validated test cases will not be sufficient to ensure product compliance with the Specification. For this reason, Bluetooth Qualification initially requires the applicant to, in addition to those items specified in chapter , submit an Interoperability Test Report including as a minimum:
A list of products that the manufacturer has found to interoperate with its own product.
Proposed resolution of known incompatibilities or inconsistencies.
The manufacturer must make his product available to at least 1 official ad-hoc interoperability test no later than 6 months after shipping the product.
Manufacturers of early products are not allowed to state any profile compliance if compliance has not been proven by a BQTF.
The BQRB reserves the right at any time to withdraw approval for a waiver, de-list the product and rescind the license, if in the opinion of the BQRB continued listing of the product with waiver may have adverse consequences for the Bluetooth Brand.