## Slide 1: HomeRF: Bringing Wireless Connectivity Home
Jim Lansford
Wireless Systems Architect
Intel Corporation
Technical Committee Chair
Home RF Working Group
March 9, 1999

## Slide 2: Where does wireless fit?
Part of the home intranet mix
Why wireless? Portability and “No new wires”
Core home networking capabilities, including internet, anywhere in and around the home
Share wireless voice and data
Review incoming messages
Activate other home electronic systems by voice
Needed in countries where phone lines cannot be used

## Slide 3
  “No new wires”
  Simple to Install
  Easy to Use
  Low Cost: ~$200 for 2 PCs
  Bandwidth To Support Common Home Applications
  Industry Standards
Home Networking Solutions Designed for the Home User

## Slide 4: Home Networking Needs 1 Mbps
1
100,000
10
100
1,000
10,000
Printing
Internet
Drives
Gaming
Voice
Real Audio G2
MP3 Audio
MPEG Video
HDTV
Bandwidth (Kbps)
(100 Mbps)
(10 Mbps)
(1 Mbps)
First Home NW Applications

## Slide 5: HomeRF™ Working Group Mission Statement
To enable the existence of a broad range of interoperable consumer devices, by establishing an open industry specification for unlicensed RF digital communications for PCs and consumer devices anywhere, in and around the home.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 6: Establishing SWAP-CA
It happened one day e.g. ISA, Soundblaster
Standards body
e.g., ITU, IEEE, ANSI
Industry leadership
and dedicated forum e.g., IrDA, TAPI, USB
SWAP-CA
Shared Wireless Access Protocol - Cordless Access

## Slide 7: 70+ Member Companies
Broad, cross industry support
Communications
Consumer Electronics
Home Control/Home Automation
Networking
Peripherals
Personal Computer
Semiconductors/Components
Software

## Slide 8: Partial Membership Roster
(70+ companies are now Participants)
3COM
Alps
Advanced Micro Devices
Aironet
Apple
Broadcom Corporation
Butterfly Communications
Casio
Cirrus Logic
Cisco Systems
Compaq
Ericsson Enterprise Networks
Fujitsu
Harris Semiconductor
Hewlett-Packard
Hosiden
IBM
Primax
Philips Consumer Communications (PCC)
Proxim
Raytheon Wireless Solutions
RF Monolithics
RF Micro Devices
Rockwell Semiconductor Systems
Samsung Electronics
Sharp
ShareWave
Siemens
Siemens Microelectronics
Silicon Wave
Symbionics
Symbol
Texas Instruments
WebGear
Intel
Intellon
Interval Research
Industrial Tech. Research
iReady Systems
Kansai Denki
LG Electronics
Matsushita Electronics
Matsushita Works
Microsoft
Mitsubishi
Motorola
National Semiconductor
NEC Corporation
Nortel
Oki
Ositis Software

## Slide 9: SWAP Product Development
Butterfly Communications
Compaq
Hewlett-Packard
IBM
Intel
iReady
Microsoft
Motorola
Proxim
OTC Telecom
RF Monolithics
Samsung
Symbionics
The following member companies are developing SWAP products:

## Slide 10: Enabling the Vision
Printer
Camera
Game Pad
USB
Stereo
Camcorder
VCR
TV
Multimedia (e.g. 1394)
Grandma’s Brownies
3 cups flour
1 cup grated chocolate
1 cup sugar
1 stick butter
HomeRF SWAP
Control Point
HomePNA
Phone
Cable
1394

## Slide 11: The SWAP Network
Slide <number>
<footer>
<date/time>
Other Home Networks (HPNA,phone,AC)
TCP/IP Based Network of Asynchronous Peer-Peer Devices
Main Home PC
Isochronous Clients
Grandma’s Brownies
3 cups flour
1 cup grated chocolate
1 cup sugar
1 stick butter
PSTN
HomeRF
Control Point
USB
Internet

## Slide 12: HomeRF Origins
802.11
Uses CSMA/CA
Good for Data
DECT
Uses TDMA
Good for Voice
SWAP
TDMA + CSMA/CA
Good for Voice & Data
Optimized for small networks (in home)
Simplified radio & protocol to reduce cost
Both voice and data are important for home RF

## Slide 13: Why a new protocol?
It handles voice like DECT or PHS, but...
  Frequency hopping
  20 ms frames (better for data)
  interleaved up and down links
  Retransmission (single)
It handles data like 802.11, but...
  Relaxed PHY layer specs to reduce cost
  Beacons to manage isochronous traffic
  Simplified protocol (no PCF)
IP data at up to 2Mb/s and supports cordless telephony

## Slide 14: SWAP Features
Range: >50 meters indoors
Speed: dual speed - supports TCP/IP traffic at over 1Mb/s
Voice: High quality voice channels with retransmission
  High quality cordless telephones
  Voice recognition

## Slide 15: Device Types
Cordless Telephone
Isochronous (I node)
> minimum latency -telephones, etc.
Asynchronous (A node)
> TCP/IP traffic
Fridge pad
Grandma’s
3 cups flour
1 cup grated chocolate
1 cup sugar
1 stick butter
1/2 cup chopped walnuts
minutes.
HOME
INDEX
CP - Connection point…can manage a network or act as an A node
  Can be USB, PCI, PC-Card, Device Bay, etc.
  CP can place calls even when PC is down
CP
PSTN

## Slide 16: Topology
CP
Connection Point*
PSTN
SWAP Frame
It’s a circuit switched, isochronous network
TDMA
I Node
TDMA
I Node
TDMA
I Node
CP
CSMA
A Node
Fridge pad
Grandma’s
3 cups flour
1 cup grated chocolate
1 cup sugar
1 stick butter
1/2 cup chopped walnuts
minutes.
HOME
INDEX
CSMA
A Node
CP
CSMA
A Node
CSMA
A Node
It’s a packet switched, asynchronous network
HOME
INDEX
CSMA & TDMA
A/I Node
It’s both - I nodes get priority on bandwidth

## Slide 17: PHY Features
Nominal 100 mW transmit power
Minimum receiver sensitivity of -76 dBm (2FSK)
  range >50 m in typical homes/yards
  -85 dBm sensitivity typical
Cost effective filter requirements
  Use MAC to reduce PHY cost
  Makes single-chip integration simpler

## Slide 18: MAC Features
MAC provides good support for voice and data
Leverages existing DECT technology for voice
Excellent integration with TCP/IP networking protocols
  easy integration with Ethernet
  Supports broadcast, multicast and fragmenting
Data security - Basic/Enhanced levels of encryption
  Basic: 24-bit Network ID and Frequency Hopping
  Enhanced: Basic + LFSR algorithm
Extensive power management for ultra-portable devices
Optimizes existing technology for home use

## Slide 19: The PC interface
SWAP’s PC connection is designed for use under Windows 98* , Windows2000*, and beyond
  Wake on ring
  Connection Oriented NDIS (NDIS 5…for Windows2000*)
  A nodes appear as Ethernet devices
  I nodes become Connection Oriented clients
* Third party brands and marks are property of their respective owners.

## Slide 20: PC Software Architecture Diagram
RCA filter
NDIS TAPI
proxy
TAPI 3.0
connection-
oriented client
connection-
less client
DirectShow*
“Ethernet”
MP/CM
connectionless I/F
connection-oriented I/F
Windows2000*
Windows2000*
Windows2000*
* Third party brands and marks are property of their respective owners.

## Slide 21: Voice: Robust clarity
Service Slot used by nodes to Page Control Point
Control Point Beacon
B
Contention period
CSMA/CA access mechanism
Hop
Service Slot
Superframe structure controlled by Beacon
Superframe - 20ms
Hop
Uplink Slots
Downlink Slots
TDMA slot pairs allocated by the Control Point
D2
U3
D3
U2
D1
U1
Voice data transmitted in the slots in CFP #2
D4
U4
D2
U3
D3
U2
D1
U1
CFP #2
Contention free periods
Any voice data to be retransmitted is sent:
  In CFP1, after a hop
  frequency/time diversity & low latency
D3
D4
U3
U4
CFP #1

## Slide 22: Data transmission
CSMA/CA during the contention period
Efficient for small networks
Tolerant of interference
Data for entire frame if no voice
Service Slot
Contention period
CSMA/CA access mechanism
Hop
Superframe - 20ms
B
D3
D4
U3
U4
D4
U4
D2
U3
D3
U2
D1
U1
Hop
D2
U3
D3
U2
D1
U1
CFP #2
CFP #1
Contention free periods

## Slide 23: Encryption Algorithm
Open, royalty free - published in open literature over 30 years ago
Low gate count
Fast “warm up”
Required for CP in the US market, optional for other devices and geographies
Robust
Similar concept to GSM A5 algorithm, but “stronger”

## Slide 24: Usage - Voice Control
CP IWU
Co-NDIS
Application
PC
CP
PSTN
TDMA
I Node
Fridge pad
Grandma’s
3 cups flour
1 cup grated chocolate
1 cup sugar
1 stick butter
1/2 cup chopped walnuts
minutes.
HOME
INDEX
CSMA
A Node
Handset initiates voice transfer to PC
Application accepts streaming audio from CP
Application performs speech recognition and sends commands back down stack
For automatic call placement, CP dials number and connects handset
Handset - PSTN connection remains until call teardown
Data traffic can also be active

## Slide 25: Usage - ISP Sharing
TDMA
I Node
Fridge pad
Grandma’s
3 cups flour
1 cup grated chocolate
1 cup sugar
1 stick butter
1/2 cup chopped walnuts
minutes.
HOME
INDEX
CSMA
A Node
CSMA
A Node
CP IWU
Co-NDIS
Application
PC
CP
PSTN
PC initiates ISP connection (modem, ISDN, UDSL, Cable, etc.)
Applications on host PC can access ISP immediately
Remote A nodes access ISP through NAT and TCP/IP
Remote A nodes can also share files and printers
Ad hoc peer-peer transfers between nodes do not require resources of “server” PC
USB
Voice traffic can also be active

## Slide 26: Timeline
Home RF Working Group Announced
Published R0.5 (Functionally complete)
Reached 50 members
‘98
Q1
‘98
Q2
‘98
Q3
‘98
Q4
‘99
Q3
‘99
Q2
Sample Physical Layer radios
Define Logo Usage Requirements
‘99
Q1
SWAP 1.0 Provisional Specification
‘99
2H
First Products
SWAP 1.1 Specification
www.homerf.org

## Slide 27: What about “Firefly”?“Home-RF lite”
Market Requirements Document phase
MRD is at 0.5 rev level
When MRD is approved (May?), goes out for technical proposals
  Off the shelf technology proposals
  Spec team will convert proposal to final specification
What is it?
  Ultra low cost
  Oriented toward toys, peripherals, control devices

## Slide 28: HomeRF Summary
Home RF Working group developing open, royalty free spec
Over 80 member companies
NOW is the time to begin implementation plans
More info (including membership) at www.homerf.org
$4,800 membership fee